## Slide 1: WF on Triggered Modification of UL LBT Parameters
Ericsson, …
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.3.1.5

## Slide 2: Background
Agreements:
For eLAA, flexible timing between UL grant and UL transmission is supported
For the details of UL grant(s) for a UE in a subframe enabling PUSCH transmission for the UE in multiple subframes in LAA SCell, at least the following options are considered
  Option 1) Single UL grant in a subframe for a UE can schedule N (N1) PUSCH transmissions for the UE in N subframes with single PUSCH per subframe
    FFS: N is consecutive or non-consecutive
  Option 2) Single UL grant in a subframe for a UE can schedule single PUSCH transmission in a single subframe while UE can receive multiple UL grants in a subframe for PUSCH transmissions in different subframes
  Option 3) Single UL grant in a subframe for a UE can enable the UE to transmit single PUSCH transmission among one of the multiple subframes depending on UL LBT result
  FFS: Two stage grants. A common semi-persistent grant provides high level information (e.g. RB allocation, MCS etc.) and a second grant in a subframe for a UE can schedule PUSCH transmissions following options 1 and 2 for certain UL subframes.

## Slide 3: Background
As per the ETSI BRAN draft regulations being developed, a TXOP with gaps larger than 100 microseconds are allowed
  This is essential to combat scheduling delays
However, additional flexibility is also necessary to mitigate scheduling delay and an updated grant or 2-stage grant is useful

## Slide 4: Proposal
The eNB signals whether a Cat. 4 LBT scheme or a CCA over 25 µs is used for UL LBT in the UL grant
The LBT procedure for an UL subframe for which the eNB indicates a Cat. 4 LBT scheme can be switched to a CCA over 25 µs if the UE detects a full DL subframe prior to the UL subframe

## Slide 5: Annex
Example of a switc
DL | DL | UL |  |  | UL | UL | UL | UL | UL | UL
Cat. 4 LBT
A : Tx starting time
after Cat 4 LBT
MCOT= 3 ms
UL grant indicates Cat. 4
Cat. 4 LBT
DL | DL | DL |  | DL | UL | UL | DL | UL | UL | UL
Trigger 25µs LBT
A : Tx starting time
after Cat 4 LBT
MCOT= 3 ms
UL grant indicates Cat. 4
Trigger 25µs LBT