## Slide 1: WF on PRACH Waveform
Ericsson, …
R1-163853
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, April 11–15, 2016
Agenda item 7.3.1.4

## Slide 2: Background
There is a working assumption on RB-interlaces as the unit for resource allocation in UL subframes
It is beneficial to multiplex PRACH with PUSCH from other UEs in the same subframe for efficiency
With RB-interlaced design, it is beneficial to locate PRACH within one or more interlaces
PRACH transmissions will have uncertain timing
An LBT region for PRACH within the subframe would be useful

## Slide 3: Proposal
Preamble durations of up to 1 ms are supported in eLAA.
PRACH is transmitted in one or more of RB interlaces
  The interlaces to use is configured by RRC
PRACH preamble is based upon repetition of one DFTS-OFDM symbol of the same length as a PUSCH DFTS-OFDM symbol.
A region for LBT is provided by not transmitting one or more OFDM symbols

## Slide 4: Annex
PRACH preamble format with preamble constructed by repeating DFTS-OFDM symbols and LBT gap in the first DFTS-OFDM symbol

## Slide 5: Annex
Interlacing of PRACH preambles