## Slide 1: Way forward on sPDCCH
Huawei, HiSilicon, Ericsson
3GPP TSG RAN WG1 #84bis R1-163855
Busan, Korea, April 11 - 15, 2016
Agenda item: 7.3.10.2

## Slide 2: Proposals
Both CRS-based sPDCCH and DMRS-based sPDCCH are recommended to be supported
  In the first sTTI of a subframe, PDCCH region can be shared by CRS-based sPDCCH and PDCCH;
  For DMRS-based sPDCCH, FFS on whether sharing the same DMRS for sPDCCH and its scheduled sPDSCH or not.
sPDSCH assigned by a sPDCCH can be allocated to unused resources within the sPDCCH region if sPDCCH region is not shared with PDCCH region
  Details are for further study, e.g., FFS whether unused resources is RB or RE level
The total number of maximum BD for USS in PDCCH and USS in sPDCCH within a subframe in one carrier is no more than X
  FFS x, e.g., x =32 for UEs not supporting UL transmission mode 2; x =48 for UEs supporting UL transmission mode 2.
Two-level DCI can be considered for sTTI scheduling
  Slow DCI is carried in legacy PDCCH region or sPDCCH and transmitted at most once per subframe
  Fast DCI is carried by sPDCCH and transmitted within a sTTI.
  Note that other enhancement to legacy DCI is not precluded.