## Slide 1
Alternative options to a achieve
2^n symbols per 1 ms numerology
ZTE, Qualcomm Incorporated
R1-163864
3GPP TSG RAN WG1 #84bis
Busan, Korea, 11th – 15th April 2016
Agenda item 8.1.5

## Slide 2
    Modular design for 2^n symbols per 1 ms is desired
    Concerns have been raised regarding
      CP length only scales with symbol duration
      Sampling rate does not line up with LTE sampling rate
Alternative options to achieve 2^n symbols / 1ms

## Slide 3
    Keep fs = 30,72 MHz, change FFT size
    Example:
How to line up with LTE sampling rate
 | LTE | Qualcomm (17,5 kHz) | ZTE 1
 | Normal CP | fixed FFT | fixed sampling rate
SC spacing [kHz] | 15 | 17,5 | 17,07
OFDM symbol length [us] | 66,67 | 57,14 | 58,6
CP-length [us] | 5,2/4,7 | 5,36 | 3,9
Nr of symbols per subframe | 14 | 16 | 16
subframe length | 1ms | 1ms | 1ms
sampling rate [Mhz] | 30,72 | 35,84 | 30,72 MHz
CP overhead | 7% | 8,60% | 6,00%
Note | FFT = 2048 | FFT=2048 | FFT=1800
Note |  | scaling 7/6 | 2^3*3^2*5^2

## Slide 4
    Increase the CP part, reduce the useful symbol part in the symbol
    Examples below:
How to enable longer CP without changing symbol (CP+useful symbol) duration
 | LTE | Qualcomm (17,5 kHz) | ZTE 1 | ZTE 2
 | ECP | fixed FFT | fixed sampling rate | fixed sampling rate
SC spacing [kHz] | 15 | 17,5 | 17,07 | 21,33
OFDM symbol length [us] | 66,67 | 57,14 | 58,6 | 46,87
CP-length [us] | 16,67 | 5,36 | 3,9 | 15,63
Nr of symbols per subframe | 12 | 16 | 16 | 16
subframe length | 1ms | 1ms | 1ms | 1ms
sampling rate [Mhz] | 30,72 | 35,84 | 30,72 MHz | 30,72
CP overhead | 20% | 8,60% | 6,00% | 25%
Note | FFT = 2048 | FFT=2048 | FFT=1800 | FFT = 1440
Note |  | scaling 7/6 | 2^3*3^2*5^2 | 2^5*3^2*5

## Slide 5: Proposals
Define common test cases for evaluation of different numerologies
Interested companies are encouraged to select and evaluate numerologies