## Slide 1: WF on scheduling delay of NPDSCH and NPUSCH
MediaTek
R1-163868
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.1.2

## Slide 2: Observations
0, Rmax/8, 2Rmax/8 4Rmax/8, 6Rmax/8, ~1Rmax,2Rmax, 3Rmax are important

## Slide 3: Scheduling delay for NPDSCH
  Proposal
    3 bit indicate number of valid DL subframes. The gap between end of NPDCCH and the start of the associated NPDSCH equals kdelay valid DL subframes + 4ms
    Number of valid DL subframe set:
      Alt 1: Based on Rmax of NPDCCH search space
        {0,1,2,4,6,8,16,24}*ceiling(Rmax/8)
          This is when Rmax >=8, {0,1/8,2/8,6/8, 1, 2, 3} *Rmax
      Alt 2: Fixed
        {0,4,8,12,16,32,64,128} DL subframes
      Alt 3: Two fixed sets for different Rmax
        If Rmax <128
          {0,4,8,12,16,32,64,128}
        If Rmax>=128,
          {0,16,32,64,128, 256,512,1024}

## Slide 4: Proposal
The gap indicated by DCI used for NPUSCH scheduling delay indicates absolute number of subframes.