## Slide 1
3GPP TSG RAN WG1 Meeting #84bis R1-163885 Busan, Korea, 11th - 15th April 2016
Agenda item: 8.1.3
WF on antenna modelling and related parameters for NR evaluations
Intel, Samsung, CATT, …

## Slide 2: Proposal
The antenna model for NR evaluations is a generalized version from TR 36.897 with the purpose to allow for more freedom in the placement of antennas as follows:
  Define the 1D/2D antenna array as in TR 36.897 as an antenna panel
    Containing (M,N,P) antenna elements following FD-MIMO TR 36.897
  Panel Model 1: Uniform 1D/2D rectangular panel array is illustrated below:
    The antenna panel array has (Mg,Ng) antenna panels per column and row respectively and uniform (dg,H, dg,V) panel spacing

## Slide 3: Proposal
Other panel models, including placements and orientation of the antenna panels in the model, are FFS
  For example when the UE antennas are modelled with panels
  For example non uniform panel array for the UE covering different directions
  For example when panels of UE are pointing in different directions

## Slide 4: Proposal

## Slide 5: Proposal
    6-sector TRP antenna model is not precluded
    TRP antenna model for high speed train is not precluded
    The above antenna parameters are for the above 6GHz

## Slide 6: Proposal
    Other UE antenna radiation patterns e.g. omnidirectional are not precluded and can be also considered for NR evaluations
    The above antenna parameters are for the above 6GHz