## Slide 1: Way forward on evaluation assumptions for 5G waveform
Huawei, HiSilicon, InterDigital, [NTT DOCOMO], [Nokia], [Intel], [MediaTek], [Samsung], [LGE], [Ericsson], [QualComm], [Sony], [Cohere]
3GPP TSG RAN WG1 Meeting #84bis R1-163897
Busan, Korea, 11th – 15th April 2016
Agenda Item: 8.1.3

## Slide 2: Background
NR should have,
forward compatibility
multiple numerologies for many reasons, e.g. wide spectrum ranges, large bandwidth, diverse deployments and services, etc..
Waveform design is a fundamental component that needs to address the above issues, and appropriate evaluation should be defined
Evaluation method (Agreed)
Evaluation cases (Agreed)
Evaluation metrics
Evaluation parameters

## Slide 3: Proposal (Possible Evaluation metrics)
User spectrum efficiency as performance metric
  Take into account guard band and time domain overhead. The values and their calculation method of guard band and time domain overhead should be reported.
  BLER vs SNR should be reported for calibration
  OOBE level is reported (Similar to ACLR but applied to adjacent sub-band/UE instead of carrier)
EVM (FFS: clear definition)
PAPR/Cubic metric
UE Complexity (FFS: how to quantify)
The following is also reported
  Receiver waveform design
  Rx processing delay (FFS: definition)
Power spectral density

## Slide 4: Proposal (Evaluation metrics)
User spectrum efficiency is given by
 =BWcarrier is the whole bandwidth including system guard band
Case 1b, 2, 3, 4:
 is the data bandwidth plus guard tone of the target UE.
Case 1a:
where  denotes the number of correctly received information bits by target user, T is the transmission time of the target user.  is defined as follows