## Slide 1: Way forward on evaluation assumptions for NR waveform
Huawei, HiSilicon, InterDigital, [NTT DOCOMO], [Nokia], [Intel], [MediaTek], [Samsung], [LGE], [Ericsson], [QualComm], [Sony], [Cohere]
3GPP TSG RAN WG1 Meeting #84bis R1-163933
Busan, Korea, 11th – 15th April 2016
Agenda Item: 8.1.3

## Slide 2: Background
NR should have,
forward compatibility
multiple numerologies for many reasons, e.g. wide spectrum ranges, large bandwidth, diverse deployments and services, etc..
Waveform design is a fundamental component that needs to address the above issues, and appropriate evaluation should be defined
Evaluation method (Agreed)
Evaluation cases (Agreed)
Evaluation metrics (Agreed)
Evaluation parameters

## Slide 3: Proposal
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD/TDD
System Bandwidth | 10 MHz
TTI length | 1 ms as baseline, other TTI length is FFS (e.g. short TTI )
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: one is 15KHz, and the other subcarrier spacing should be selected by companies from the agreed numerologies.
Guard time interval | 4.7us (interval of LTE normal CP) as baseline, other interval is FFS
FFT size | e.g. 1024 for 15KHz subcarrier spacing
Data transmission bandwidth | Single numerology case: 4 and/or 1 PRBs for the bandwidth of target UE in case 1b Mixed numerology case: At least two candidate BWs for target UE. At least two candidate BWs for interfering subband At least two numerologies. The values are FFS
Guard tone number | [0~12] subcarriers for the mixed numerology case
Antenna configuration | 1T1R or 2T2R or 4T4R, other is not precluded
MIMO mode | TM3, other non-LTE TM model is not precluded
Rank per UE | Fixed rank
MCS | Fixed. 16QAM: 1/2 or 2/3; 64QAM: 1/2 or 3/4; 256 QAM: 1/2 or 3/4
Control Overhead | Zero
Channel estimation * | Ideal
Channel Model ** | TDL (1T1R), CDL (MIMO) in TR38.900 is mandatory, ETU/EPA/EVA are optional. Mobility: 3km/h or 30 km/h or 120 km/h, higher speed is not precluded.
Table 1 Parameters for case 1a/1b and case 2
NOTE: *Non-ideal effects to be considered in a second stage (e.g., channel estimation, frequency offset, details are FFS)
**For RAN1#85: CDL in TR38.900 or ETU/EPA/EVA can be used