## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167948 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on RS for CSI Acquisition and Demodulation in NR
Huawei, HiSilicon

## Slide 2: Background
Following WF has been agreed in RAN1#85:
  In NR multi-antenna schemes, studies on RS design and CSI acquisition considering following use cases
    Non-UE-specific RS use case for CSI measurement
    UE-specific RS use case for CSI measurement
      Note: functionally may be analogous e.g.: to R13/14 UE-specific beamformed CSI-RS (with dynamic beamforming)
      Note: maybe relevant to UE receiving beam sweeping
    Use of a joint operation among multiple RS from the same or different use cases
    RS for interference measurement use cases
    RS for channel reciprocity use cases
    Other use cases is not precluded
  Note: including measurement over aperiodic/periodic/semi-persistent RS
  Note: Subband RS is not precluded

## Slide 3: Proposal
Studies on RS for CSI measurement in NR at least include
  RS is mapped on few consecutive symbols
  RS is located at the earlier part of a “time interval X”
    FFS: RS located at other part of a “time interval X”
  Configurable density of RS in frequency domain
  Multi-level RS should be considered
    E.g. functionally analogous to R13/14 hybrid non-precoded and beamformed CSI-RS
Studies on RS for channel reciprocity in NR at least include
  Beamformed RS
  Dynamic indication of number of RS symbols in a time interval
  Dynamic indication of the bandwidth for SRS hopping
    total SRS hopping bandwidth within a “time interval X”
    bandwidth for each SRS hopping instance
At least following RS configurations for CSI acquisition are supported in NR
  Aperiodic RS
  Semi-persistent RS

## Slide 4: Proposal
Studies on design of RS for demodulation in NR at least include
  DMRS is concentrated within one or more consecutive symbols at earlier part of a “time interval X”
    FFS: DMRS located at middle part of a time interval
  Configuration/indication of density of DMRS in frequency domain
  Note: here the definition of 'time interval X' follows the agreements in RAN1#85 meeting