## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-168179
Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on CSI measurement and reporting in NR
Huawei, HiSilicon, Ericsson, China Telecom

## Slide 2: Background
Following WF has been agreed in RAN1#85:
  In NR multi-antenna schemes, studies on CSI acquisition framework include
    CSI reporting schemes
      Implicit CSI feedback
        Parameters indicating channel quality based on a set of transmission and receiving hypotheses associated with one particular UE, e.g. CQI, PMI, RI, CRI
      Explicit CSI feedback: for both quantized and unquantized/analog CSI feedback
        Parameters representing channel coefficients or some reduced-space representation thereof
      Reciprocity-based feedback
        For example, take into account interference and/or receiver hypothesis can be included
      Note: including aperiodic, periodic and semi-persistent, and single/wide band and sub-band feedback
      Mixed feedback is not precluded
    Interference measurement
    FFS: CSI measurement and/or reporting and/or triggering can be ‘self-contained’ in at least time domain

## Slide 3: Proposal
A unified CSI acquisition framework should be studied in NR, which could support
  CSI measurement based on CSI-RS
  Implicit and explicit CSI feedback
  Reciprocity based CSI acquisition
  Other features to be supported
The implicit CSI feedback methods should be studied in NR
  Codebook design
  Interference measurement based on IMR which could be one or more of the following options
    ZP CSI-RS
    NZP CSI-RS
    DMRS
  Beam measurement results
The explicit CSI feedback methods should be studied in NR
  Feedback of channel covariance matrix
    E.g. based on Kronecker-product
  Feedback of channel matrix
    E.g. based on multi-beam combination
  Feedback of channel eigenvector
    E.g. based on multi-beam combination
  Both quantized and unquantized/analog feedback
CSI measurement and reporting with the following components should be studied in NR
  Wideband/long-term CSI
  Subband/short-term CSI
  Explicit CSI
  Implicit CSI
  Configuration of the above components individually or jointly is FFS