## Slide 1: WF on PTRS
NTT DOCOMO, Huawei, HiSilicon, Panasonic, […]
3GPP TSG RAN WG1 Meeting #88
Athens, GREECE 13th - 17th Feb. 2017
Agenda item: 8.1.2.4.3
R1-1703787

## Slide 2: Proposal
Presence/patterns of PT-RS are configured by a combination of RRC signaling and association with parameter(s) used for other purposes (e.g., MCS) which are (dynamically) indicated by DCI.
  Whether PT-RS can be present or not depends on RRC configuration.
  When configured, the dynamic presence is associated with DCI parameter(s) including at least MCS.
  FFS: Time domain density is associated with dynamic configuration of MCS.
  When present, frequency domain density is associated with at least dynamic configuration of the scheduled BW.
    FFS: Frequency-domain pattern design supports both frequency-localized and frequency-distributed allocation of PT-RS subcarriers.
  Other association factors/rules are not precluded.
  Above associations can be pre-defined in specification or can be re-configured by higher layer signaling.