## Slide 1
WF on the maximum number of orthogonal DL DMRS ports
Mitsubishi Electric, Nokia, Huawei, HiSilicon, NTT DOCOMO, AT&T, CATT, Ericsson, Deutsche Telekom, China Unicom, Xinwei, Fujitsu, MediaTek, Orange, CATR, CMCC, Telecom Italia
3GPP TSG RAN WG1 Meeting #88 R1-1704030 Athens, Greece, 13th - 17th February 2017
Agenda item: 8.1.2.4.2

## Slide 2: Background
Agreements on DMRS made in RAN1 NR Ad-Hoc meeting:
For the design of front-loaded DMRS, Alt. 1 is agreed as a working assumption.
  Alt. 1: Front-loaded DMRS is mapped over 1 or 2 adjacent OFDM symbols.
    FFS: Further down-selection between 1 and 2, if necessary
    Companies are encouraged to propose further details
Additional DMRS can be configured for the later part of the slot.
  FFS: Density reduction compared to front-loaded DMRS
DMRS configuration can be up to the max. number of DMRS ports.
Study the following options:
  Option1: with 16 orthogonal DMRS ports or
  Option2: with non-orthogonal DMRS ports in addition to 8 orthogonal ports
  Other options are not precluded.

## Slide 3: Proposals
Support at least the following design of DL DM-RS for data channels
  Support the maximal 16 orthogonal DL DMRS ports for MU-MIMO