## Slide 1: WF on Polar code construction
Qualcomm, ERICSSON, [xxx, xxx]
3GPP TSG RAN WG1 #88b R1-1706485
3th – 7th April 2017
Spokane, USA
Agenda item: 8.1.4.2.1.1

## Slide 2: Background
Until RAN1#88bis, work together on a coding scheme that achieves the benefits of both Alts 1&2
  With J’ bits for the purpose of assisting the polar decoding, where 0<=J’<=Jmax , aiming for Jmax , e.g. in the region of 8 (other values are not precluded)
    This does not preclude the use of the J bits for assisting decoding
    Note that any PC-frozen bits would be considered to be among the J’ bits
    The following are examples:
J bits CRC + J’ bits CRC + basic polar;
J bits CRC + J’ bits distributed CRC + basic polar;
J bits CRC + J’ PC bits + basic polar; (i.e. PC-Polar)
J bits CRC + J’ Hash sequence + basic polar;
(J + J’) bits CRC + basic polar

## Slide 3: Observation
It is been observed by majority companies, extra CRC bits (in addition to CRC for error detection) are needed to assist polar decoding to achieve good performance and decoding complexity

## Slide 4: Proposal
CRC bits used to assist polar decoding is adopted as NR control channel coding design baseline:
  FFS hybrid schemes
  J’ bits are available to assist decoding (in addition to J CRC bits for error detection):
    J’ <= Jmax’ <= 5 bits
      This does not preclude the use of the J bits for assisting decoding when the same FAR as LTE can be maintained