## Slide 1: WF on cell-specific and fixed CSI-RS for L3 mobility
ZTE
3GPP TSG RAN WG1 Meeting #89
Hangzhou, USA, 15th – 19th May 2017
Agenda: 7.1.1.5.2
R1-1709203

## Slide 2: Background
RAN2 asks the following in LS R1-1709061
Furthermore RAN2 understands that RAN1 has agreed that:
“For Connected mode, CSI-RS are supported to be configured using at least dedicated RRC signaling for DL based RRM measurement for L3 mobility.
Note that signalling other than dedicated RRC signalling is not precluded”
RAN2 independently reached a similar agreement and would then like to ask RAN1 about potential additional options:
Question2: Besides being UE-specifically configurable, are the CSI-RS for RRM measurements for L3 mobility also intended to be:
- Cell-specifically configurable and/or
- Cell-specific and fixed (all UEs can derive the CSI-RS for RRM measurements for L3 mobility from the cell IDs of the serving and neighbor cells) or
- are multiple options foreseen?
Note: these are not necessarily preferences from a RAN2 point of view.

## Slide 3: Background
One mode of operation is that a UE performs CSI-RS based RRM measurements only on detected cells for which it has obtained an explicit configuration ("listed cells").
In some scenarios, inter-gNB coordination is limited and neighbor relations are not available/accurate, for example unlicenced and early deployments.
It is useful to support a mode of CSI-RS based RRM measurements on a particular frequency layer configured by dedicated RRC signaling where:
  Some CSI-RS configuration parameters, e.g. RS sequence, are derived from the cell ID of a detected cell.
  Other CSI-RS configuration parameters are based on a frequency layer specific configuration (fixed in spec or configurable)
Note that this does not impose that the CSI-RS are always on. A UE can blindly detect or measure the CSI-RS of a detected neighbor cell.
A configuration derived from cell ID and frequency layer could be overridden by a UE-specific configuration for the detected cell.

## Slide 4: Example
Mode 1 (only listed cells): If the UE has an explicit CSI-RS configuration for the detected cell (i.e. listed cell), the UE measures/reports it.
Mode 2 (listed and detected cells): The CSI-RS configuration of a (non-listed) detected cell is derived from cell ID and frequency specific configuration.
frequency layer f1
frequency layer f2
frequency layer f3
UEs in serving cell on f1
Mode 1 on f1: UEs measure
CSI-RS only on cells with
explicit CSI-RS configuration
(only listed cells)
Mode 2 on f3: UEs can obtain
CSI-RS configuration from cell ID
and frequency specific config
(listed and detected cells)
Mode 1 on f2: UEs measure
CSI-RS only on cells with
explicit CSI-RS configuration
(only listed cells)

## Slide 5: Proposal
Mappings between cell IDs and values of some configuration parameters of CSI-RS for L3 mobility can be defined, including at least
  CSI-RS sequence
A UE can be configured (using dedicated RRC signaling) for a particular frequency layer to use such mappings for CSI-RS based RRM measurements and reporting of detected cells for which the UE has received no explicit configuration.
It is up to RAN2 whether and how such mappings should be used.