## Slide 1: WF on CSI-RS framework
CATT, Ericsson, Nokia, ASB, Intel, OPPO
3GPP TSG RAN WG1 #89 R1-1709447
Hangzhou, China, May 15th – 19th 2017
Agenda Item: 7.1.2.3.1

## Slide 2: Background: Example settings
2 Resource settings
  Resource setting 1: 4 resource sets
    Resource set 1: K= 1, N ports (e.g. 16)
      Linked to reporting setting relevant to CSI acquisition (similar to LTE Class A)
    Resource set 2: K= 1, N ports (e.g. 16)
      Linked to reporting setting relevant to CSI acquisition (similar to LTE Class A)
    Resource set 3: K>1, each with N ports (e.g. 8)
      Linked to reporting setting relevant to CSI acquisition (similar to LTE Class B)
    Resource set 4: K 1,
      Linked to reporting setting relevant to CSI acquisition
  Resource setting 2: 4 resource set
    Resource set 1: K>1, N ports (e.g. 1 or 2)
    Resource set 2: K>1, N ports (e.g. 1 or 2)
    Resource set 3: K>1, N ports (e.g. 1 or 2)
    Resource set 4: K>1, N ports (e.g. 1 or 2)
    Linked to one reporting setting relevant to beam management
Or it can be 1 resource set with K=2

## Slide 3: Background: Examples
Periodic CSI-RS
  Ks1 periodic CSI-RS can be transmitted with same or different periodicity, same or different slot offset
Semi-persistent CSI-RS
  Semi-persistent CSI-RS is transmitted according to periodicity configured by RRC after activation/triggering
  Semi-persistent CSI-RS can be transmitted on each OFDM (or on sub time unit smaller than OFDM symbol if supported) symbol after activation/triggering
Aperiodic CSI-RS
  An UE can be triggered to receive Ks1 aperiodic CSI-RS resources by one signal

## Slide 4: Proposals
Need to agree on maximum number of CSI reporting settings (N value), maximum number of resources settings (M value), maximum number of resource sets (S value), maximum number resources per resource set (Ks value) before determining dynamic signaling mechanism.
If RAN1 determines DCI based dynamic signaling is inefficient, decision on activation/deactivation via higher layer protocols (e.g., MAC-CE) should involve RAN2
Note that it is has been agreed in 88bis: maximum number of simultaneously triggered report settings and the maximum number of links corresponding to those triggered settings can be different for reporting types (e.g. beam reporting, CSI reporting)