## Slide 1: WF on Construction of Polar Codes
NTT DOCOMO, Qualcomm, IAESI, Ericsson
R1-1709520
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China 15th – 19th May 2017
Agenda item 7.1.4.2.1.1

## Slide 2: Background
Conclusion:
Study until RAN1#89 polar code construction techniques to facilitate early termination (i.e. before decoding all the information bits) without degrading BLER performance or latency (especially considering the time for deinterleaving the information and assistance bits) compared to purely implementation based methods such as path-metric based pruning
  e.g. assistance bits distributed in the codeword in such a way that error detection can be performed after partial decoding
  Investigate performance, complexity and FAR impacts
  Study of use of data-independent scrambling to facilitate early termination is also not precluded

## Slide 3: Background
Agreement:
J CRC bits are provided (which may be used for error detection and may also be used to assist decoding and potentially for early termination)
  J may be different in DL and UL
  J may depend on the payload size in the UL (0 not precluded)
In addition, J’ assistance bits are provided in reliable locations (which may be used to assist decoding and potentially for early termination)
J + J’ <= the number of bits required to satisfy the FAR target (nFAR) + 6
  Working assumption:
    For DL, nFAR = 16 (at least for eMBB-related DCI)
    For UL, nFAR = 8 or 16 (at least for eMBB-related UCI; note that this applies for UL cases with CRC)
J’>0
Working assumption: J”<=2 additional assistance bits are provided in unreliable locations (which may be used to assist decoding and potentially for early termination)
  Can be revisited in RAN1#89 if significant benefit is shown from a larger value of J” without undue complexity – companies are encouraged to additionally evaluate J”=8
The J’ (and J” if any) bits may be CRC and/or PC and/or hash bits (downscope if possible)
Placement of the J, J’ (and J” if any) assistance bits is FFS after the study of early termination techniques
  Appended?
  Distributed?
    evenly?
    unevenly?

## Slide 4: Proposal
J CRC bits and J’ assistance bits are applied for Polar codes construction
  All the J+J’ bits are provided in reliable locations, i.e., J’’ = 0.
  J’ = 3
FFS: The locations and encoding method of the J’ assistance bits
FFS: How to facilitate early termination by J’ assistance bits
Note: The evaluation for early termination is not needed for UL