## Slide 1: WF On RRM measurement
MediaTek, Intel …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda: 7.1.1.5.1
R1-1709624

## Slide 2: Background
In RAN1#88 following agreement was made
For detecting non-standalone NR cell, NR should support adaptation and network indication of SS burst set periodicity and information to derive measurement timing/duration (e.g., time window for NR-SS detection)
  For detecting non-standalone NR cell, network provides one SS burst set periodicity information per frequency carrier to UE and information to derive measurement timing/duration if possible
    In case that one SS burst set periodicity and one information regarding timing/duration are indicated, UE assumes the periodicity and timing/duration for all cells on the same carrier
    RAN1 recommends short measurement duration than configured periodicity e.g., 1, 5 or 10 ms
      Note that L1/L3 filtering across multiple periods is still allowed
    FFS more than one periodicity/timing/duration indication
  NR should support set of SS burst set periodicity values for adaptation and network indication
    Candidate periodicity values to be evaluated are [20, 40, 80 and 160 ms]
    FFS other values with consideration for functionalities provided by NR-SS in connected mode
  FFS whether to support NR-PBCH in non-standalone NR cell

## Slide 3: Proposals
Only one SS burst set periodicity and one information regarding measurement timing/duration are indicated per frequency layer.