## Slide 1: WF on UL Command and Control Traffic for Aerial Vehicles
Nokia, Alcatel-Lucent Shanghai Bell
R1-1709742
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China, May 15th – 19th 2017
Agenda item: 6.2.8.2

## Slide 2: Background
In RAN1#89 meeting, it has been agreed that
For aerial UE, command and control traffic is assumed in downlink
    Command and control traffic in DL
      Periodic traffic with fixed packet size is assumed:
        inter-packet arrival time interval of D = [100ms]
        FFS: packet size X
Note: X is determined based on the requirement on DL data rate and latency for command and control traffic. and D can be revised according to RAN2 agreement.
Note: Command and control traffic in UL is not precluded.

## Slide 3: Background
In RAN2#98 meeting, it has been agreed that
Command and Control (C&C) includes telemetry, waypoint update for autonomous UAV operation, real time piloting, identity, flight authorization, navigation database update, etc.
C&C data rate: [60-100] kbps for UL/DL
C&C reliability: Up to 10-3 packet error loss rate

## Slide 4: Proposal
Proposal 1: Same traffic model including packet size and inter-packet arrival time interval for downlink and uplink command and control traffic of aerial UE.
  inter-packet arrival time interval of D = [100] ms
  FFS: packet size [750] Bytes
Proposal 2: For aerial UE, uplink command and control traffic is assumed.