3GPP TSG RAN WG1 Meeting #92			R1-1801317

Athens, Greece, February 26th – March 2nd, 2018

3GPP TSG-RAN WG2 NR Ad hoc 1801			R2-1801568

Vancouver, Canada, 22nd January – 26th January 2018

Title:	LS on PHR

Response to:	-

Release:	Release 15

Work Item:	NR_newRAT-Core

Source:	RAN WG2

To:	RAN WG1

Cc:	-

Contact Person:

#### Name:	Toru Uchino

Tel. Number:	+81-46-840-3190

E-mail Address:	tooru[dot]uchino[dot]fv[at]nttdocomo[dot]com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

1. Overall Description:

RAN2 addressed followings on PHR in NR:

- PH for PUCCH

RAN2 discussed the necessity of the PH for PUCCH in PHR MAC CE in NR. RAN2 understands that the parallel transmission of PUCCH and PUSCH across primary PUCCH group and secondary PUCCH group is supported for NR. RAN2 would like to understand whether RAN1 supports the scenario and PH for PUCCH.

RAN2 also discussed following features which might affect to the PHR MAC CE format design, i.e. how many PHs need to be reported in a PHR MAC CE. RAN2 would like to understand whether RAN1 supports them.

- Simultaneous configuration of EN-DC and NR PUCCH SCell

- Simultaneous transmission of PUCCH and PUSCH in LTE for EN-DC

- PH for SRS

RAN2 agreed to use the term “Type3 PH” to refer the PH for SRS in NR (as in LTE) to avoid impact to LTE MAC spec. This is because, in EN-DC, UE reports PHs of NR cells to eNB using PHR MAC CE format of LTE.

NOTE: This is applicable regardless of the support of PH for PUCCH transmission in NR.

- phr-ModeOtherCG

RAN2 confirmed that phr-ModeOtherCG is used for EN-DC (as for LTE-LTE DC).

2. Actions:

To RAN1 group.

ACTION: 	RAN2 respectfully asks RAN1:

- to answer the question whether RAN1 supports following in NR:

  - the scenario RAN2 considers and PH for PUCCH (as in LTE)

  - Simultaneous configuration of EN-DC and NR PUCCH SCell

  - Simultaneous transmission of PUCCH and PUSCH in LTE for EN-DC

- to update RAN1 spec to use term “Type3 PH” to refer the PH for SRS as in LTE.

- to confirm that phr-ModeOtherCG is used for EN-DC (as for LTE-LTE DC)

3. Date of Next TSG-RAN2 Meetings:

RAN2#101	26th February – 2nd March 2018					Athens, Greece

RAN2#101-Bis	16th – 20th April 2018					China