3GPP TSG-RAN WG2 Meeting #109-e-bis	R2-2004190

e-meeting, 20 - 24 April 2020						revision of R2-2002922

Title:	[DRAFT] Response LS on the “LS OUT on Location of UEs and associated key issues”

Response to:	S2-1912560

Release:	Rel-17

Work Item:	FS_5GSAT_ARCH

Source:	Thales [To be RAN2]

To:	SA2, RAN3, SA3-LI

Cc:

Contact Person:

Name:	Nicolas Chuberre

Tel. Number:	+33680948432

E-mail Address:	nicolas.chuberre@thalesaleniaspace.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

# 1. Overall Description:

RAN2 would like to thank SA2 for their LS in S2-1912560 on Location of UEs and associated key issues.

RAN2 would like to clarify that it has already completed its work in the scope of the rel-16 NTN Study Item (“Study on solutions for NR to support non-terrestrial networks (NTN)”, FS_NR_NTN_solutions). The solutions considered by RAN2 are captured in TR 38.821. No further study on NTN is expected in Rel-16 by RAN2.

RAN2 starts the normative work in Release 17 earliest in August and there is no allocated RAN2 time to progress on NTN solutions before that.

RAN2 also recommends tracking areas as being fixed on Earth (see TR 38.821, clause 7.3.1.3.3 “Tracking Area recommendation”). RAN2 has studied several solutions for mobility management including some based on similar assumptions (i.e. UE would have the capability to determine their position) as SA2, for example as provided in TR 38.821 in clause 7.3.1.3.2. In addition, RAN2 has also studied solutions in clause 7.3.1.3.1 for the case when UE is not able to determine their position. Detailed solutions will be evaluated and defined in the normative phase.

Note that existing definition in 3GPP TS 36.300 and 3GPP TS 38.300 mandates that a cell is combination of downlink and optionally uplink resources.

# Actions:

To SA2 working group

RAN WG2 respectfully requests SA2 to take the above information into account. More detailed information will not be available until after RAN2 starts normative work

# Date of Next TSG-RAN2 Meetings:

3GPPRAN2#110e	01 - 12 June 2020   	e-meeting

3GPPRAN2#111	24 - 28 August 2020   	Toulouse, France

3GPPRAN2#111-bis	12 - 16 October 2020   	India

# Comments

SA2 colleagues indicated it is useful to inform them about RAN2 timeplan.

As indicated by chair condition to send LS is to re-use the Rel-16 information/conclusion. The TR 38.821 does not tell us one solution is better than the other. Therefore, this should be sufficient at this time.

We suggest to also mention the case when UE is not able to determine their position and the corresponding solutions we have studied to give SA2 a full picture of our study and also show them that the fixed TAC can be applicable to all kinds of UE no matter it has location information or not.

Added as unlike SA2 usually(always?) does, RAN2 did not include conlcusions on which solutions to take in normative phase but discussion starts in WI phase.

We share the similar view with Ericsson and Qualcomm, The discussion for NTN in R16 is already closed, what RAN2 can do now before R17 NTN WI is just to inform SA2 of our progress in TR38.821, no further analysis is needed in this reply LS. So we prefer to remove all the info in section1.1 and 1.2 to avoid any misleading for SA2.

We do not know which solutions will be agreed in the normative phase thus it is better not to potentially mislead SA2.

We agree with Ericsson and this is true for solution 12 below as well.

RAN2 did specified geographical zones as a possible solution which is similar to the concept of the solution 12. Please check in TR 38.821 in clause 7.3.1.3.2	Approach 2: For the case when UE location information is available.

We cannot mislead SA2 by indicating solution 6.1 is better than the solution 6.12 without having discussion in RAN2. There is no such recommendation in TR 38.821 in clause 9.2	Recommendations from RAN2.