3GPP TSG-RAN WG2 Meeting #109bis-e	R2-20XXXXX

# Electronic, 20 April – 30 April 2020

Agenda item:	6.7.3.1

Source:	Samsung

Title:	Offline-028: Intra-UE prioritization and MAC, Part 3

Document for:	Discussion & Decision

# Introduction

This document provides the outcome of Part 3 of offline discussion #028. Companies are requested to review the contents of this document and to provide their view.

# Discussion on MAC Corrections

## 2.1 Procedure Captured in TS 38.321

The MAC entity shall follow the procedures specified in the spec, as follows [TS 38.321 v16.0.0]:

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant.

In the current MAC specification, whether an uplink grant is prioritized is decided one by one. Since RAN2 agreed not to specify any timeline restriction, when the MAC entity performs the prioritization is fully up to UE implementation. But it is clear that if an uplink grant was already a de-prioritized uplink grant, it will never be able to become a prioritized uplink grant in the future. Note that for this paragraph, UE shall follow the rule at least if anything is specified. So, there is no room for UE implementation not to follow.

## 2.2 Problematic Scenario

Assumption

- t1: deadline of prioritization for DG whose PHY priority index is low

- t2: deadline of prioritization for CG whose PHY priority index is high

- At t1, the DG has some data available whereas the CG does not have.

- Between t1 and t2, high priority data arrives for the CG

- The MAC entity decides whether a grant is prioritized at the very last moment before delivery to PHY

Figure 1. (Potential) Problematic scenario

UE behaviour based on the current spec will be as follows:

At t1:

- The MAC entity should decide whether the DG is prioritized.

- Since the DG is not de-prioritized yet, MAC entity checks whether it can be a prioritized uplink grant or not. (by cyan highlighted text)

- Since no data is available for the CG, the DG should be a prioritized uplink grant. (by yellow)

- The overlapping CG will be a de-prioritized uplink grant (by green)

At t2:

- The CG remains de-prioritized. By the cyan highlighted text, re-prioritization is not allowed, i.e. cannot proceed to 1> 2> …

But the problem is that CG should become a prioritized uplink grant and be delivered to PHY.

## 2.3 Companies’ View

Q1) Do companies agree the problem of the current texts, as described above?

- Yes, we agree.

- No, this scenario does not happen.

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |

# Conclusion

TBD