3GPP TSG-RAN WG2 Meeting #109bis-e	R2-2xxxxx

Electronic, 20 April – 30 April 2020

Agenda Item:	6.19

Source: 	OPPO

Title:  	Email report of [AT109bis-e][042][NR16 Other] P bit for Single Entry PHR (OPPO)

Document for:	Discussion and decision

# Introduction

This paper aims to trigger the email discussion for introduction of P bit for Single Entry PHR in R16.

[AT109bis-e][042][NR16 Other] P bit for Single Entry PHR (OPPO)

Scope: Treat papers above on P bit for Single Entry PHR

Wanted Outcome: Agreed-in-principle CRs

Deadline: April 28 0700 UTC

# Discussion

In RAN4 LS [1], RAN4 found the inconsistency for the P bit between single entry PHR MA CE and multiple entry PHR MAC CE. RAN4 also said that it is up to RAN2 to decide whether the introduction of “P” bit in single entry PHR MAC CE is necessary or not.

In [4], the necessary to introduce the “P” bit in single entry PHR MACE is discussed and some observations are provided:

Obervation 1: LTE PHR MAC CE only includes one single PH field even though the P-MPR is supported since R10 in LTE.

Observation 2: The PCMAX,f,c is included in NR single entry PHR MAC CE compared with PHR MAC CE in LTE and NR single entry PHR MAC CE is used for one serving cell case.

Observation 3: the UE will report the UE power class in UE capability container in NR.

Observation 4: The maximal value of A-MPR and MPR are under control of the network.

Observation 5: The “P” bit is not essential from RAN4 perspective and gNB perspective.

Observation 6: The gNB will identify the “P” bit or R bit according to the UE release version or UE capability indication if the “P” bit is captured in single entry PHR MAC CE since R16.

Based on the observation, the network will know if the P-MPR is applied or not if the power reduction is enough high. If P-MPR is applied and power reduction is not high, it is not desirable for the network to know it. The “P” bit is not essential from RAN4 perspective. So, it is proposed that “P” bit is not introduced [2,4]

In [3], it proposed to introduce the “P” bit in single entry PHR MAC CE.

Question 1: Do you agree that the “P” bit is not introduced in current single entry PHR MAC CE?

| Company | Yes or NO | Comment, if any |
| --- | --- | --- |
| OPPO | Yes | The network will know if the P-MPR is applied or not if the power reduction is enough high. If P-MPR is applied and power reduction is not high, it is not desirable for the network to know it. The “P” bit is not essential from RAN4 perspective. |
| Nokia | No | Disagree with the observations. If the above statement is true, why did we have it for multiple entry PHR then, the logic should be the same. RAN4 only specified the maximal allowed A-MPR, but the actual value the UE applies is unknown to the NW. |
| Intel | FFS | We understand that RAN4 bought up this issue with respect to MPE discussion. Therefore, we can wait until RAN4 finish MPE related discussion. If there is no new MAC CE reporting for MPE, it would be useful to add P-bit in single PHR MAC CE. Otherwise, there is no much big need to introduce it. |
| Ericsson | No | Disagree with the observations. The P-bit is required to have the actual value known to the network. We think the summary is biased towards not having the P-bit as the analysis in [2, 4] are not sufficiently recognized. |
| HW |  | P-MPR can be applied to CA and non-CA case since R10, and it is beneficial for UE to report P bit in non-CA case for NW to distinguish if power management is applied for better estimation of the link budget. It should be common sense from R10 and the reason why P bit was excluded is mainly due to missing of Pcmax. But it is worthy to mention that RAN4 is still discussing enhancements to P-MPR beyond P bit that may further impact the PHR format and we understand they would be on the basis of P bit indication. So we think we should at least include the P bit in single entry PHR in R16 and keep the format open to additional inputs. |
| Apple | No | Disagree with the observations. Currently the absence of the P-bit in the single entry PHR MAC CE prevents a UE from reporting that it has applied power back-off (e.g. due to the boxy proximity sensor input) in certain configuration cases; and thus, the network is not aware about the reason for it. |
| vivo | No | We see some benefit of using the “P” bit also in the single PHR MAC CE. Regarding the MPE discussion in RAN4, we consider that if the reserved bits in the current PHR MAC is reused for the report of the P-MPR, we would anyway needs to introduce the P bit. |
| LG | Yes, but | We have similar understanding with Intel. Currently, P bit is not essential. However, RAN4 discusses about MPE in FR2 considering P bit and Power backoff level, and RAN2 may be asked to change PHR MAC CE format depending on RAN4 decision. Therefore, we think it would good to wait RAN4 progress. |
| MediaTek |  | We share same view with Intel. |

Question 2: If the answer of Question 1 is NO, do you agree the “P” bit is introduced for single entry PHR MAC CE from R16?

| Company | Yes or NO | Comment, if any |
| --- | --- | --- |
| OPPO | Yes |  |
| Nokia | Yes |  |
| Ericsson | Yes |  |
| HW | Yes | Can be revisited once RAN4 has additional inputs. |
| Apple | Yes |  |
| vivo | Yes |  |

Furthermore, another issue is how does a R16 gNB to decode the single entry PHR from R15 UE and R16 UE if we support to capture the “P” bit in single entry PHR MAC CE since R16.

Option 1: the gNB use the release version of the UE in UE capability container to identify that is “P” indication or “R” bit. It means the UE from R16 should implement the “P” bit in single entry PHR.

Option 2: the gNB use one UE capability indication in UE capability container to identify the “P” indication or “R” bit.

Option 3: introduce a new LCID to identity the new single PHR MAC CE with P indication.

- Current single entry PHR with LCID= 57               (b)	Current single entry PHR with LCID= xx

Question 3: If the answer of Question 1 is NO, Which option do you prefer to address gNB decoding single entry PHR issue?

| Company | Yes or NO | Comment, if any |
| --- | --- | --- |
| OPPO | Option 2 or 3 |  |
| Nokia | Option 1 | No capability needed. |
| Ericsson | Option 1 or 2 | There is no need for a new LCID. |
| HW |  | We understand R bit has no backward compatible issue from the NW side but it is more flexibility to introduce a UE capability signalling. Either works. But we think it is not critical to decide anything this meeting for capability signalling and suggest to postpone to next meeting to check if any further inputs from RAN4 on the P-MPR. |
| Apple | Option 1 |  |
| vivo | Option 2 | Option 2 would be clean from the specification. One the other hand, maybe some UEs which do not support Rel-16 new feature at all still want to support the P bit. |
| MediaTek | Option 2 | Share same view with HW and vivo that using capability signalling would be more flexible. |

# Conclusions

# Reference

[1] R2-2002532	LS on the misalignment in P-bit between single entry and multi-entry PHR (R4-2002820; contact: OPPO)	RAN4	LS in	Rel-16	NR_RF_FR2_req_enh	To:RAN2

[2] R2-2002616	P bit in Single Entry PHR MAC CE	Samsung	discussion	Rel-16	NR_RF_FR2_req_enh

[3] R2-2003010	P bit for Single Entry PHR	Nokia, Nokia Shanghai Bell, Apple, Ericsson, Lenovo, NTT DOCOMO, INC.	CR	Rel-16	38.321	16.0.0	0716	-	F	TEI16	Late

[4] R2-2002676	Discussion on P indcatior in single entry PHR    OPPO    discussion    Rel-16