3GPP TSG-RAN WG2 Meeting #109bis-e					R2-20xxxxx

Electronic, 20 April – 30 April 2020

Agenda Item:		6.20.3.1		Open / ongoing proposals

Source:			Huawei

Title:				Summary on eCall over NR

WI code(s):			TEI16

Document for:		Discussion and Decision

## 1	Introduction

In section 6.20.3.1 Open/ongoing proposals, there is an email discussion as below:

[AT109bis-e][055][TEI16] eCall over NR (Huawei)

Scope: Treat papers above on eCall over NR.

Wanted Outcome: Agreed solution, if possible Agreed-in-principle CR(s)

Deadline: April 28 0700 UTC

Since the target of the email discussion is agreed solution and if possible AIP CRs, it is suggested to have the following deadlines:

- Phase 1: discuss the solution. Deadline:April 25 0700 UTC

- Phase 2: discuss CRs. Deadline:April 28 0700 UTC

The relevant papers are listed in [1] ~ [6]. This paper is to progress on the topic eCall over NR.

## 2	Discussion

Among all papers, [1] is the incoming LS on eCall over NR, and [2] is a discussion paper for potential RAN2 impacts. It is proposed to use [2] as a basline for collecting companies’ opinions.

In [2], the following observations and proposals are provided:

Observation 1: In NR specifications, the eCall over IMS has been defined in stage-2 and stage-3 (signaling aspect), but the parameter eCallOverIMS-Support is not used.

Observation 2: TS 38.304 does not capture anything on eCall only mode like TS 36.304.

Proposal 1: It is proposed to add a clarification for eCall over IMS in TS 38.300:

UEs that are not in limited service state need to only consider eCallOverIMS to determine if eCall over IMS is possible.

Proposal 2: It is proposed to keep the parameter eCallOverIMS-Support in SIB1 and change the condition from “Cond Absent” to “Need R”. The UE should forward the parameter to its upper layer if received in SIB1.

Proposal 3: It is proposed to add a clarification on eCall only mode to TS 38.304, i.e. control and restrict registration for a UE in eCall only mode.

Regarding the above observations and proposals, please companies provide comments into the following table.

| Company | Comments |
| --- | --- |
| Qualcomm Incorporated | We support all the proposals. One specific comment on the 38.331 CR in R2-2003567 It is not clear to us why "5GC" needs to be mentioned in the field description of eCallOverIMS-Support. We can simply add a reference to SA2 specification, i.e. 23.501. Essentially the same approach that has been taken in 36.331. |
| OPPO | Agree the above proposals and CRs. |
| ZTE | We support above proposals. Regarding the 331 CR, we have the similar comment as Qualcomm, suggest to revise the field description as below: eCallOverIMS-Support Indicates whether the cell supprots eCall over IMS services via 5GC as defined in TS 23.501 [32]. If absent, eCall over IMS via 5GC is not supported by the network in the cell. |
| Huawei, HiSilicon | We support all the proposals and CRs. For the wording “5GC”, the incoming LS R2-2002549 has the following action for RAN2, and 5G Core/5GC is explicitly mentioned. That is why we used “5GC” in the CRs. ACTION: SA asks SA2, SA5, RAN2, CT1 and RAN5 to identify specification changes needed to support eCall in IMS over NR (with 5G Core) and to prepare the required CRs. However, we are also ok with the changes from Qualcomm and ZTE. |
| Samsung | We support all the proposals. In the 38.331 CR, one typo needs to be fixed as well i.e. supprots ( supports |
| Nokia, Nokia Shanghai Bell | We agree with the intentions to clarify eCall support in RAN2 |
| Ericsson | Agree with the above comments. |
| Lenovo | We agree with the observations and proposals. On the 38.300 CR we have a minor comment: The references to the field names (eCallOverIMS, ims-Emergency) should be corrected to eCallOverIMS-Support and ims-EmergencySupport. |

Summary:

- Almost all companies are fine with P1, P2 and P3 in [2]

- Some companies also provided suggestions to CRs

Based on the above summary, the email rapporteur suggests to conclude on the solution, and start Phase 2 discussion to progress on CRs (the suggestions on CRs in the table above will be taken into account).

## 3	Conclusions

Based on Phase 1 discussion, there is consensus on the solution of eCall over NR. So Phase 2 is to be started to progress on CRs.

## 4	References

eCall over NR

Moved from AI 3:

[1] R2-2002549	Reply LS on support for eCall over NR (SP-200287; contact: Qualcomm)	SA	LS in	Rel-16	EIEI, 5GS_Ph1	To:SA2, SA5, RAN2, CT1, RAN5	Cc:SA1, SA4, RAN, CT

[2] R2-2003564	Discussion on eCall over IMS for NR	Huawei, HiSilicon	discussion	Rel-16	TEI16

[3] R2-2003565	Introduction of eCall over IMS for NR	Huawei, HiSilicon	draftCR	Rel-16	38.300	16.1.0	C	TEI16

[4] R2-2003566	Introduction of eCall over IMS for NR	Huawei, HiSilicon	draftCR	Rel-16	38.304	16.0.0	C	TEI16

[5] R2-2003567	Introduction of eCall over IMS for NR	Huawei, HiSilicon	draftCR	Rel-16	38.331	16.0.0	C	TEI16

[6] R2-2003568	Draft reply LS on support for eCall over NR	Huawei	discussion	Rel-16	TEI16