3GPP TSG-RAN WG2 Meeting #109bis electronic	                                                                           R2-200xxxx

20th April – 30th April 2020

Agenda Item:	4.1

Source: 	ZTE (email discussion rapporteur)

Title:  	Draft report of [AT109bis-e][302][NBIOT]Trigger for dedicated SR with HARQ-ACK (ZTE)

Document for:	Discussion and Decision

# Scope of the offline email discussion

This document contains the summary of the offline email discussion “[AT109bis-e][302][NBIOT] Optimisation on trigger for dedicated SR with HARQ-ACK”, as indicated below:

[AT109bis-e][302][NBIOT] Optimisation on trigger for dedicated SR with HARQ-ACK (ZTE)

Status: Starts Monday April 20th at 7:00 UTC

Scope: Check if there is support and update based on the comments if the CR is agreeable.

Intended outcome: Report from the discussion and, if agreeable, in-principle agreed CR. The report can be provided in R2-2004037

Deadline: 27-04-2020, 10:00 UTC

In this document, we will list the issues raised in the related discussion paper/CRs and collect the comments from companies with the aim to confirm whether the issues exist and if yes, to achieve aggregable CRs to resolve them.

# Offline email discussion

## 2.1 Discussion on the issues

As mentioned in the discussion paper [1], for the case that only physical SR with HARQ-ACK is configured (e.g., both physical SR with dedicated NPRACH and UL SPS for BSR are not configured), the pending SR would be triggered even when there has no acknowledgement of the data.

As the timing for checking HARQ-ACK for the DL transmission is in TTI level and in the real application services, downlink and uplink transmission doesn’t always happen at the same time, especially at the same TTI, when the UE has pending SR to be sent in the uplink, it may be highly possible that there has no HARQ-ACK for the downlink transmission at the same time. Therefore, it’s hardly to send the SR together with the acknowledgement of the data and legacy RA procedure would be used.

As a result, the benefit of piggybacked SR cannot be achieved (even the function has been configured). The NPRACH resources and UE power are unnecessarily consumed. In order try to avoid legacy random access procedure for the pending SR, intensive ping transmission during has been applied in the IoT testing.

Q1: Companies are invited to provide comments to the table below based on the observation 1 and observation 2 in the discussion in [1].

| Company | Do you agree that it’s hard to trigger physical SR with HARQ-ACK if only this function is configured? | Comments |
| --- | --- | --- |
| MediaTek | Yes | SR with HARQ-ACK is hard to trigger when the DL data is not sufficient, and UE would not know when the resource of HARQ-ACK would be available, it makes UE hard to fully utilize the piggybacked SR. |
| ZTE | Yes | Agree with MediaTek and some above analysis. And the difficulty has been observed in the product testing. |
| Qualcomm | Yes | Very much dependent on when resources for HARQ-ACK are configured and SR needs to be sent. |
| Huawei, HiSilicon | yes | Very much dependent on the probability of UL data arrival during a DL transmission. |
| Nokia | Yes |  |
| Ericsson | Yes | It is true that the use is quite limited since it depends on whether the data to be transmitted in the UL arrives sometime between when UE is scheduled to receive data in the DL and the transmission in the DL ends, however this was known when the feature was introduced. |

Conclusion: TBD

Proposal: TBD

Moreover, according to the MAC spec, if there has no HARQ-ACK in a certain TTI, UE will immediately initiate legacy RA procedure and cancel all pending SR. However, it may be also highly possible there are no available NPRACH resource on this TTI, e.g., UE may still need to wait for some time period for the next available radio frame / subframe containing NPRACH resource. How long of this time period is related to the NPRACH resource period configuration (which has minimum value of 40ms and maximum value of 2540ms). Purely based on the spec text, it’s not crystal clear whether the UE would or would not “immediately” cancel the pending SRs when it initiates the RA. If UE would not cancel the SR immediately, the UE may continuously check the following TTIs and it's still possible for the UE to use piggybacked SR before the TTI on which there has an available PRACH resource. On the other hand, if UE would cancel the SR immediately, even there may have a HARQ-ACK in the following TTIs after the UE initiates RA but before an available NPRACH resource occurs, this HARQ-ACK cannot be used. With such process, the possibility of using piggybacked SR is further reduced.

Q2: Companies are invited to provide comments to the table below based on the observation 3 in the discussion in [1].

| Company | Do you agree that it’s not clear whether the UE would “immediately” cancel the pending SRs when it initiates the RA? | Comments |
| --- | --- | --- |
| MediaTek | Yes | The specification does not specify when exactly to cancel the pending SRs. |
| ZTE | Yes | Agree with MediaTek. And one understanding based on such ambiguity is that the UE would also cancel the pending SR at the same time when it initiates legacy RA. This may be not the good way. |
| Qualcomm | Yes | Specification should allow SR to be piggy-backed on HARQ-ACK if it occurs before the start of NPRACH. |
| Huawei, HiSilicon | yes | We agree that the UE shall only cancel the SR when RACH is actually transmitted. |
| Nokia | Yes | Agree with Huawei that SR should be cancelled only on triggering the RACH Access. |
| Ericsson | Yes | We agree that the SR shall only be cancelled when NRACH is actually transmitted. |

Conclusion: TBD

Proposal: TBD

## 2.2 Discussion on the proposals

Based on the discussion on the issues, especially the observation 3, the following proposal 1 regarding clarification on UE behavior when UE has pending SR and initiates legacy RA is made in [1] and related specification changes can be found in [2].

Proposal 1: It’s suggested to clarify that after initiation of legacy RA, UE would not cancel the pending SR immediately till the next available subframe containing NPRACH resource.

Q3: Companies are invited to provide comments to the table below.

| Company | Do you agree the clarification in proposal 1? | Comments |
| --- | --- | --- |
| MediaTek | Yes | The proposal increases the possibility of usage of piggybacked SR without any harm. |
| ZTE | Yes | Agree with MediaTek. |
| Qualcomm | Maybe | Yes, clarification is needed to maximize piggy-backed HARQ-ACK. But not sure if the proposed solution is right because this solution requires MAC to know when the NPRACH transmission will start. Currently MAC knows when the NPRACH transmission ends (this is needed for random access response window management). The other issue we see is that MAC initiates the random access procedure for SR but due to NPRACH configuration the random access procedure may be delayed. If SR is then sent pigg-backed on HARQ-ACK before the NPRACH transmisison starts then NPRACH must be cancelled. |
| Huawei, Hisilicon | yes | we are fine with a clarification |
| Nokia | Yes |  |
| Ericsson | Yes, considering the intention | SR shall be cancelled when NPRACH is actually transmitted and if SR is sent using the HARQ-ACK before NPRACH transmission, NPRACH must be cancelled unless there is any other reason. |

Conclusion: TBD

Proposal: TBD

Q4: If the answer for Q3 is yes, companies are invited to provide comments to the table below.

| Company | Any detailed suggestion on the related changes in the CR [2]? |
| --- | --- |
| MediaTek | The changes are fine. |
| ZTE | Fine with this part change and no other comments. |
| Qualcomm | Two issues with the CR and propose the following changes: The wording ‘just before the available subframe containing NPRACH resource’ is vague. Cancel the random access procedure if piggy-backed HARQ-ACK is to be transmitted. - For NB-IoT: - if the MAC entity has no valid resource for SR together with acknowledgement of the data in this TTI, sr-DelayTimer is not running and no valid PRACH resource for SR configured in any TTI: - initiate a Random Access Procedure (see clause 5.1) and cancel all pending SRs in the first subframe containing NPRACH transmission for SR. - else: - if the MAC entity has valid resource for SR together with acknowledgement of the data in this TTI: - instruct the physical layer to signal the SR together with acknowledgement of the data. - If Random Access Procedure was initiated for SR then cancel the Random Access Procedure. - else: - if the MAC entity has valid PRACH resource for SR configured in this TTI and sr-ProhibitTimer is not running: - instruct the physical layer to signal the SR on one valid PRACH resource for SR. - start the sr-ProhibitTimer in the subframe containing the last repetition of the corresponding SR transmission. - if running, stop the sr-DelayTimer. Note: Whether there is a need for sr-DelayTimer is discussed in the next question. |
| Huawei, Hisilicon | We are not sure about the proposed wording. we would prefer: - initiate a Random Access Procedure (see clause 5.1) and cancel all pending SRs when the random access preamble is transmitted. |
| Nokia | Second change seems not required. |
| Ericsson | QC’s suggestion above can be used as the baseline. The WI code for the 36.321 CR is not correct, it should be for NB-IoT. |

Conclusion: TBD

Proposal: TBD

Moreover, in order to make the dedicated SR with HARQ-ACK to be used as much as possible when the function is configured, a configurable SR delay timer for avoiding that the UE immediately initiates legacy RA when it cannot find HARQ-ACK for DL in the current TTI is proposed as following in [1]. The related specification changes can be found in [2] and [3].

Proposal 2: It’s suggested to introduce a SR delay timer with value range no more than 8s or a value with unit of NPRACH periodicity.

Proposal 2a: If dedicated SR with HARQ-ACK is configured, a SR delay timer can be activated when there has a SR to be transmitted. Random access procedure would be triggered only when the SR delay timer expires.

Q5: Companies are invited to provide comments to the table below.

| Company | Do you agree to introduce a configurable SR delay timer for avoiding that the UE immediately initiates legacy RA when it cannot find HARQ-ACK for DL? | Comments |
| --- | --- | --- |
| MediaTek | Yes | A SR delay time can increase the possibility of usage of piggybacked SR, but the power consumption and latency could be optimized only if the DL data would be sufficient. The network must configure this timer with caution, it must be sure the incoming DL data is sufficient, otherwise the piggybacked SR would not be triggered and the RA is prevented, so power consumption and latency are harmed. |
| ZTE | Yes | The main intention of this SR delay timer is to pend initiation of legacy RA a little time and increase the possibility of usage of piggybacked SR. The network can reasonably configure the timer based on some knowledge about DL service. |
| Qualcomm | No | With the delay timer, SR can be delayed for quite some time e.g. up to 8s due to sr-DelayTimer and then further delay (up to 2.54s) due to NPRACH configuration and this can have negative impact on applications, potentially leading to retry by upper layers. With changes to allow for piggy-backed HARQ-ACK to be sent if it occurs before the NPRACH, it is not necessary to add a delay timer. |
| Huawei, HiSilicon | No | This has been proposed several times in Rel-15 and not agreed. We do not see any new aspect that would justify to change. As DL data and UL data are not correlated, we actually think this will increase latency and power consumption at the UE. |
| Nokia | No | Not using the available RACH opportunity and delay SR waiting for HARQ-ACK is not needed. As the availability of such opportunity is not known. Overall it will delay the uplink transmission. |
| Ericsson | No | We do not think that the timer is needed. Agree with the comments from Huawei. |

Conclusion: TBD

Proposal: TBD

Q6: If the answer for Q5is yes, companies are invited to provide comments to the table below.

| Company | What’s the value range of this SR delay timer? Several seconds, several NPRACH periodicities or other? | Comments |
| --- | --- | --- |
| MediaTek | Several seconds | NPRACH periodicity could vary from different CE levels, so the timer length could also vary if the NPRACH periodicities is used as a base of value range. Uncertainty is not preferred. |
| ZTE | Several seconds | Agree with MediaTek’s analysis. |
| Qualcomm | - | As per response to Q5, delay timer is not useful. |
| Huawei, HiSilicon | NA | see answer to Q5 |
| Ericsson | N/A | See our reply to Q5 |

Conclusion: TBD

Proposal: TBD

Q7: If the answer for Q4 is yes, companies are invited to provide comments to the table below.

| Company | Do you agree a UE capability would be needed? | Comments |
| --- | --- | --- |
| MediaTek | No | The capability information is not useful for network configuration is this case. |
| ZTE | Yes | As this is an additional change to R15 UE, we assume the network could configure this timer to the UE only if it knows that the UE supports this function. |
| Qualcomm | No | If sr-DealyTimer is not introduced then signalling changes are not needed. The MAC spec clarification for UE behavior would not cause any inter-operability issue hence no capability signalling is needed. |
| Huawei, HiSilicon | NA | see answer to Q5 |
| Ericsson | N/A | See our reply to Q5 |

Conclusion: TBD

Proposal: TBD

Q8: If the answer for Q7is yes, companies are invited to provide comments to the table below.

| Company | Any detailed suggestion on the related changes in the CR [2] and [3]? |
| --- | --- |
| MediaTek | Network can configure SR delay timer based on the information that the pending DL data is sufficient, so that the piggybacked SR could be used in a high possibility and the SR delay timer is an optimization in this case. But what if the DL data has been sent out? The remaining SR delay timer would be harmful since then, it should be disabled from that moment. Can network disable the SR delay timer? For CP solution, there is no way that network can disable the SR delay timer in the duration of the connection. For UP solution, RRC reconfiguration is available, but signaling cost is on the table. I suggest that let UE disable the SR delay timer. The condition of disabling the timer could be once HARQ-ACK is missed in the duration of SR delay timer. |
| ZTE | Even we think the network can decide whether to set and try to set a suitable value for this timer based on some knowledge, e.g., traffic pattern, we still think it may be not easy for network to do prediction for short-term. Then it may be very rare a reconfiguration is needed. We think the case is similar for UE, e.g., some statistics/prediction about DL on UE side may be not so reliable. Therefore, I think we'd better not to indicate this self-disable process in UE, at least not in the specification. It may still be possible to leave to UE implementation. |
| Qualcomm | As per our response to Q7, if dedicated signaling changes are not needed i.e. not add sr-DelayTimer then there is no interoperability issue with different UE implementations. |
| Huawei, HiSilicon | NA. See answer to Q5. |
| Ericsson | N/A. See our reply to Q5. |

Conclusion: TBD

Proposal: TBD

# Summary

[TBD]

# References

- R2-2003245	Optimisation on trigger for dedicated SR with HARQ-ACK	, ZTE Corporation, Sanechips, MediaTek Inc.	, discussion	Rel-15

- R2-2003254	Optimisation on trigger for dedicated SR with HARQ-ACK, ZTE Corporation, Sanechips, MediaTek Inc.	CR	Rel-15,  36.321    15.8.0     	1469   	-	F

- R2-2003256	Optimisation on trigger for dedicated SR with HARQ-ACK, ZTE Corporation, Sanechips, MediaTek Inc.	CR	Rel-15, 	36.331	   15.9.0	     4254  	-	F

# Comments

I think this should be Q5.

This can’t be Q4. Which Question is this referring to?

In any case, Q7 is clear.

assume Q5 again

Question 4 does not have Yes/No answer, it is for comments if answer to Question 3 is Yes.

Should this be Question7?

assume Q5 again