3GPP TSG-RAN WG2 Meeting #109bis electronic	                                                                           R2-200xxxx

20th April – 30th April 2020

Agenda Item:	4.2

Source: 	ZTE (email discussion rapporteur)

Title:  	Draft report of [AT109bis-e][401][eMTC] Correction on reception type combination (ZTE)

Document for:	Discussion and Decision

# Scope of the offline email discussion

This document contains the summary of the offline email discussion “[AT109bis-e][401][eMTC] Correction on reception type combination for eMTC”, as indicated below:

[AT109bis-e][401][eMTC] Correction on reception type combination for eMTC (ZTE)

Scope: Check if there is support and update based on the comments if the CRs are agreeable

Intended outcome: Report from the discussion and, if agreeable, in-principle agreed CR(s). The report can be provided in R2-2003916.

Deadline: Monday, Apr. 27th 10:00 UTC

# Offline email discussion

[1] R2-2003189	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-13  	36.302    	13.7.0	   1204   -F

The intention of the CRs is to correct the misalignment between the Downlink "Reception Type" combinations for eMTC UE in TS 36.302 and RAN1 description about reception on Type0-MPDCCH common search space and MPDCCH UE-specific search space.

Q1: Companies are invited to provide comments to the table below.

| Company | Do you agree with the intent and changes in the R13 CR? | Detailed comments |
| --- | --- | --- |

Conclusion: TBD

Proposal: TBD

[2] R2-2003190	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	 Rel-14	    36.302    14.5.0	    1205	    -	A

[3] R2-2003222	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR  	Rel-15	     36.302	  15.2.0     	1206    	-	A

For the issue itself, these R14 and R15 CRs may be shadow ones. Even some other new reception types have been introduced for UE in RRC_IDLE in R14 and R15 respectively, as the changes in CR are for UE in RRC_CINNECTED, the changes are still same as that in R13 CR.

Q2: Companies are invited to provide comments to the table below.

| Company | Do you agree with the changes in R14 and R15 CRs? | Detailed comments |
| --- | --- | --- |

Conclusion: TBD

Proposal: TBD

[4] R2-2003228	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR   	Rel-16   	36.302   	16.0.0   	1207   	-	A

As other new reception type has been introduced for UE in RRC_CINNECTED in R16, the changes in this R16 CR is different from those in R13~R15 CRs. But the reason for change is same.

Q3: Companies are invited to provide comments to the table below.

| Company | Do you agree with the changes in R16 CR? | Detailed comments |
| --- | --- | --- |

Conclusion: TBD

Proposal: TBD

# Summary

[TBD]

# References

- R2-2003189	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-13	36.302	13.7.0	1204	-	F	LTE_MTCe2_L1-Core

- R2-2003190	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-14	36.302	14.5.0	1205	-	A	LTE_MTCe2_L1-Core

- R2-2003222	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-15	36.302	15.2.0	1206	-	A	LTE_MTCe2_L1-Core

- R2-2003228	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-16	36.302	16.0.0	1207	-	A	LTE_MTCe2_L1-Core