3GPP TSG-RAN WG2 Meeting #109bis electronic	                                                                           R2-200xxxx

20th April – 30th April 2020

Agenda Item:	4.2

Source: 	ZTE (email discussion rapporteur)

Title:  	Draft report of [AT109bis-e][401][eMTC] Correction on reception type combination (ZTE)

Document for:	Discussion and Decision

# Scope of the offline email discussion

This document contains the summary of the offline email discussion “[AT109bis-e][401][eMTC] Correction on reception type combination for eMTC”, as indicated below:

[AT109bis-e][401][eMTC] Correction on reception type combination for eMTC (ZTE)

Scope: Check if there is support and update based on the comments if the CRs are agreeable

Intended outcome: Report from the discussion and, if agreeable, in-principle agreed CR(s). The report can be provided in R2-2003916.

Deadline: Monday, Apr. 27th 10:00 UTC

# Offline email discussion

[1] R2-2003189	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-13  	36.302    	13.7.0	   1204   -F

The intention of the CRs is to correct the misalignment between the Downlink "Reception Type" combinations for eMTC UE in TS 36.302 and RAN1 description about reception on Type0-MPDCCH common search space and MPDCCH UE-specific search space.

Q1: Companies are invited to provide comments to the table below.

| Company | Do you agree with the intent and changes in the R13 CR? | Detailed comments |
| --- | --- | --- |
| Huawei, HiSilicon | Yes | Agree that USS and type 0 CSS share the same resources, but only one DCI in USS or DCI in CSS is transmitted, so they will not transmitted at the same time |
| Sequans | Yes | The coversheet states that current spec allows C and (I or F) or receive D and (J or E or B), but that according to 36.213 this is not possible and therefore needs to be fixed. Actually C or D cannot be received simultaneously or with any USS, which is what this CR states. In addition, since this spec is in contradiction with 36.213 (which is more procedural and we assume has been implemented correctly in UEs) we see no harm in fixing 36.302 which is more descriptive in nature, even for Rel-13. Of course, as this CR is applied to more advanced releases it will be more helpful in avoiding confusion. Furthermore, keeping this mistake in only some of the releases may also be confusing, given the wrong idea that something has actually changed in this regard. |
| Qualcomm | May be | No issue has been reported since Rel-13. We agree, in practice, C and D will not be scheduled simultaneously. However, if change is needed, Rel-16 CR is enough. |
| ZTE | Yes | We agree with Sequans and also assume no harm in fixing 36.302. The main intention is just to align the 36.302 with physical layer description which should have been implemented correctly in UEs. We also agree with Sequans to correct this from the start release in which the issue is introduced would be helpful to avoid confusion. |
| Ericsson | Agree with intent, not with R13 CR | While the UE monitors for the combination, it is true that C and D cannot be transmitted simultaneously (and hence will never be received simultaneously) or with USS. However, the functionality regarding monitoring and what would be transmitted in practice is clearly specified in TS 36.213, which would take precedence as L1 specification. While we think that the specifications should be aligned between releases when there are no functional changes in principle, we do not think CRs until R15 are essential CRs which need to be agreed to frozen releases. |
| Lenovo | Yes | As mentioned by Sequans, actually C or D cannot be received simultaneously or with any USS, |

Conclusion:

All companies agree with the intention of the CRs. 4 companies out of all 6 companies agree to correct this from the start release in which this misalignment issue is introduced. 2 companies do not think CRs until R15 need to be agreed to frozen releases and Rel-16 CR is enough.

Considering more companies’ preference, Rapporteur still think it’s better to have CRs for earlier releases in order to completely resolve this issue and avoid any future confusion. With reference to the company’s comment mentioned in Q3, Rapporteur suggest the following modification on the coversheet:

Impacted functionality:

There are no functional changes due to this CR is just a clarification to align with TS 36.213.

Consequences if not approved:

If CR is not approved, there are no functional impacts. But such misalignment between TS 36.302 and TS 36.213 may cause future confusion.

Proposal:

Proposal 1: In principle agree on the Rel-13 CR with a revised coversheet as suggested in the conclusion.

[2] R2-2003190	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	 Rel-14	    36.302    14.5.0	    1205	    -	A

[3] R2-2003222	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR  	Rel-15	     36.302	  15.2.0     	1206    	-	A

For the issue itself, these R14 and R15 CRs may be shadow ones. Even some other new reception types have been introduced for UE in RRC_IDLE in R14 and R15 respectively, as the changes in CR are for UE in RRC_CINNECTED, the changes are still same as that in R13 CR.

Q2: Companies are invited to provide comments to the table below.

| Company | Do you agree with the changes in R14 and R15 CRs? | Detailed comments |
| --- | --- | --- |
| Huawei, HiSilicon | Yes |  |
| Sequans | Yes | See answer to Q1 |
| Qualcomm | No | See response in Q1 |
| ZTE | Yes | See answer in Q1 |
| Ericsson | No | See answer to Q1. |
| Lenovo | Yes | See answer to Q1. |

Conclusion:

4 companies out of all 6 companies agree with Rel-14 and Rel-15 CRs while 2 companies disagree.

With the similar reason mentioned for Rel-13 CR, Rapporteur still suggest to agree on Rel-14 and Rel-15 CRs with the following modification on the coversheet.

Impacted functionality:

There are no functional changes due to this CR is just a clarification to align with TS 36.213.

Consequences if not approved:

If CR is not approved, there are no functional impacts. But such misalignment between TS 36.302 and TS 36.213 may cause future confusion.

Proposal:

Proposal 2: In principle agree on the Rel-14 and Rel-15 CRs with revised coversheets as suggested in the conclusion.

[4] R2-2003228	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR   	Rel-16   	36.302   	16.0.0   	1207   	-	A

As other new reception type has been introduced for UE in RRC_CINNECTED in R16, the changes in this R16 CR is different from those in R13~R15 CRs. But the reason for change is same.

Q3: Companies are invited to provide comments to the table below.

| Company | Do you agree with the changes in R16 CR? | Detailed comments |
| --- | --- | --- |
| Huawei, HiSilicon | Yes |  |
| Sequans | Yes | See answer to Q1 |
| Qualcomm | Yes | See response in Q1 |
| ZTE | Yes | See answer in Q1 |
| Ericsson | Yes | We agree to have R16 CR on this issue, where we clearly explain on cover page there are no functional changes of any kind due to this CR but it is a clarification to align with TS 36.213 (and that similar behavior applies to all R13-R15). We suggest to additionally update the titles of the rows 2.3 and 2.4 in Table 8.2-2a to: "2.3 UEs supporting ETWS and CMAS in RRC_CONNECTED" And "2.4 UEs supporting ETWS and CMAS in RRC_CONNECTED and FS2" 1) To align with the style of other rows 2) To make it clear support of ETWS/CMAS in connected is different from idle; Current formulation can be understood as if there was no support for ETWS and CMAS in RRC_IDLE. |
| Lenovo | Yes | See answer to Q1. |

Conclusion:

All companies agree with the Rel-16 CR.

Based on company’s suggestion, Rapporteur propose same modification on the coversheet as that for Rel-13~Rel-15 CRs:

Impacted functionality:

There are no functional changes due to this CR is just a clarification to align with TS 36.213.

Consequences if not approved:

If CR is not approved, there are no functional impacts. But such misalignment between TS 36.302 and TS 36.213 may cause future confusion.

One company further suggest to additionally update the titles of the rows 2.3 and 2.4 to "2.3 UEs supporting ETWS and CMAS in RRC_CONNECTED" and "2.4 UEs supporting ETWS and CMAS in RRC_CONNECTED and FS2". Per Rapporteur’s understanding, this is not necessary as these rows are already under the high level row of “2. RRC_CONNECTED”.

Proposal:

Proposal 3: In principle agree on the Rel-16 CR with a revised coversheet as suggested in the conclusion.

# Summary

Conclusions:

Proposal 1: In principle agree on the Rel-13 CR with a revised coversheet as suggested in the conclusion.

Proposal 2: In principle agree on the Rel-14 and Rel-15 CRs with revised coversheets as suggested in the conclusion.

Proposal 3: In principle agree on the Rel-16 CR with a revised coversheet as suggested in the conclusion.

Updated CRs in the draft folder:

draft 36302_(Rel-13)_R2-200xxxx Correction on reception type combination for eMTC-r1

draft 36302_(Rel-14)_R2-200xxxx Correction on reception type combination for eMTC-r1

draft 36302_(Rel-15)_R2-200xxxx Correction on reception type combination for eMTC-r1

draft 36302_(Rel-16)_R2-200xxxx Correction on reception type combination for eMTC-r1

# References

- R2-2003189	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-13	36.302	13.7.0	1204	-	F	LTE_MTCe2_L1-Core

- R2-2003190	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-14	36.302	14.5.0	1205	-	A	LTE_MTCe2_L1-Core

- R2-2003222	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-15	36.302	15.2.0	1206	-	A	LTE_MTCe2_L1-Core

- R2-2003228	Correction on reception type combination for eMTC	ZTE Corporation, Sanechips, Sequans Communications	CR	Rel-16	36.302	16.0.0	1207	-	A	LTE_MTCe2_L1-Core