3GPP TSG-RAN WG2 Meeting #109bis-e	draft0_R2-2004078

Online, 20 – 30 April 2020

Title:	[DRAFT] LS on Cast type indication

Response to:

Release:	Rel-16

Work Item:	5G_V2X_NRSL

Source:	LG Electronics [To be RAN2]

To:	RAN1

Cc:

Contact Person:

#### Name:	Youngdae LEE

Tel. Number:

E-mail Address:	youngdae.lee@lge.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

RAN2 recently agreed the following working assumption:

- The V field is supported in a SL-SCH MAC subheader at least for future extensibility.

In addition, when a MAC PDU is successfully decoded, a receiving NR MAC entity needs to understand the cast type associated to the received MAC PDU e.g. to correctly perform packet filtering. It is because the NR MAC entity may not correctly identify the associated cast type from the Layer-2 IDs included in the SL-SCH MAC subheader.

Thus, RAN2 assumes that the V field in the SL-SCH MAC subheader can also indicate a cast type for NR sidelink, as specified for LTE sidelink.

Regarding the indication to a cast type, RAN2 would like to ask RAN1 to respond to the following questions:

Q1: Will a cast type be included in SCI?

Q2: Does RAN1 expect any L1 impact when the MAC subheader indicates a cast type for NR sidelink?

2. Actions:

To RAN1 group

RAN2 respectfully requests RAN1 to take the above into account in the related work and provide their answers to the above questions.

3. Date of Next TSG-RAN2 Meetings:

3GPPRAN2#110-e	1 - 12 June 2020   	Online

3GPPRAN2#111	24 - 28 August 2020   	Toulouse, FR