3GPP TSG-RAN WG2 Meeting #109bis-e	draft0_R2-2004078

Online, 20 – 30 April 2020

Title:	[DRAFT] LS on Cast type indication

Response to:

Release:	Rel-16

Work Item:	5G_V2X_NRSL

Source:	LG Electronics [To be RAN2]

To:	RAN1

Cc:

Contact Person:

#### Name:	Youngdae LEE

Tel. Number:

E-mail Address:	youngdae.lee@lge.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

RAN2 recently agreed the following working assumption:

- The V field is supported in a SL-SCH MAC subheader at least for future extensibility.

On the one hand, when a MAC PDU is successfully decoded, the NR MAC entity needs to understand the cast type associated to the received MAC PDU e.g. to correctly perform packet filtering. On the other hand, the NR MAC entity may not correctly identify the associated cast type from the Layer-2 IDs included in the SL-SCH MAC subheader.

Thus, RAN2 assumes that the V field in the SL-SCH MAC subheader can be used to explicitly indicate the cast type for NR sidelink, if such indication is not provided by physical layer signalling (e.g. SCI).

Regarding the indication to a cast type, RAN2 would like to ask RAN1 to respond to the following questions:

Q1: Will the corresponding cast type be indicated in SCI?

Q2: Does RAN1 has any concern if the MAC subheader indicates a cast type for NR sidelink?

2. Actions:

To RAN1 group

RAN2 respectfully requests RAN1 to take the above into account in the related work and provide their answers to the above questions.

3. Date of Next TSG-RAN2 Meetings:

3GPPRAN2#110-e	1 - 12 June 2020   	Online

3GPPRAN2#111	24 - 28 August 2020   	Toulouse, FR

# Comments

There is no distinguish between TX and RX MAC entity.

We fail to understand the point of the comment from E///, the two are the same thing so why we need on the one/other hand for differentiation? The original text seems good to us.

V field in LTE spec is not used to indciate cast types.

We also support this sentence since the main reason for this LS is for RAN1/2 coordination.

Not necessary to have a cast type field. Any explicit/implicit indication will work.

I understand this comes from meeting minutes, but wonder why RAN2 care about RAN1 impact? Or is the main intention is to ask if RAN1 has any concern if cast-type is included in MAC HD?