3GPP TSG-RAN WG2 Meeting #109bis-e	draft1_R2-2004078

Online, 20 – 30 April 2020

Title:	[DRAFT] LS on Cast type indication

Response to:

Release:	Rel-16

Work Item:	5G_V2X_NRSL

Source:	LG Electronics [To be RAN2]

To:	RAN1

Cc:

Contact Person:

#### Name:	Youngdae LEE

Tel. Number:

E-mail Address:	youngdae.lee@lge.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

RAN2 recently agreed the following working assumption:

- The V field is supported in a SL-SCH MAC subheader at least for future extensibility.

In addition, a receiving NR MAC entity needs to understand the cast type associated to the received MAC PDU in order to determine the appropriate Rx UE behaviour. When the MAC PDU is successfully decoded, RAN2 assumes that the V field in the SL-SCH MAC subheader can be used to explicitly indicate the cast type of the received MAC PDU for NR sidelink, as specified for LTE sidelink. When the MAC PDU is unsuccessfully decoded, the corresponding cast type could not be obtained. As such, RAN2 would like to ask RAN1 if cast type information will be provided in L1.

Regarding the cast type indication, RAN2 would like to ask RAN1 to respond to the following questions:

Q1: Will the corresponding cast type be indicated by SCI?

Q2: If the cast type is indicated by SCI, will the corresponding cast type enable an Rx UE to determine the appropriate ACK/NACK behaviour when a TB is successfully decoded or when a TB is not successfully decoded?

Q3: Does RAN1 expect that L1 filtering on cast type for determining an Rx UE’s ACK/NACK behaviour is performed by PHY layer (i.e., RAN1 TS 38.213) or MAC layer (i.e., RAN2 TS 38.321)?

2. Actions:

To RAN1 group

RAN2 respectfully requests RAN1 to take the above into account in the related work and provide their answers to the above questions.

3. Date of Next TSG-RAN2 Meetings:

3GPPRAN2#110-e	1 - 12 June 2020   	Online

3GPPRAN2#111	24 - 28 August 2020   	Toulouse, FR