3GPP TSG-RAN WG2 Meeting #109bis-e                                      R2-2004083

Electronic, 20 April – 30 April 2020

Title:	[Draft] LS response to SA3 on the security related issues for NR SL

Response to:

Release:	Rel-16

Work Item:	5G_V2X_NRSL-Core

Source:	CATT [to be RAN2]

To:	SA3, CT1

Cc:

Contact Person:

#### Name:	Da Wang

#### E-mail Address:	wangda@catt.cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

# 1. Overall Description

RAN2 would like to thank SA3 for the reply LS on NR V2X Security issue and PDCP SN size (S3-200478) to inform RAN2 of the security related fields/information for AS ciphering and integrity protection.

- Regarding5-bit input for the security algorithms derived from a specific LCID, RAN2 has made following working assumption.

1: Working assumption: the 5 least significant bits of LCID can be used as 5-bit input to the ciphering/integrity algorithms. Working assumption will be RAN2 agreement if there is no SA3 concern until next RAN2 meeting.

- RAN2 agreed PDCP re-establishment is triggered by re-keying procedure, in order to better understand the impact on AS layer, RAN2 respectively ask SA3 f following questions:

Question 1: What is the granularity of the re-keying procedure, e.g., per PC5 unicast link or per SL QoS flow?

Question 2: Does the re-keying procedure trigger the PDCP COUNT wrap around in SL unicast?

- Regarding Counter Check procedure, RAN2 would like to ask SA3following question:

Question 3: Is Counter Check procedure needed in PC5 interface for SL unicast DRB?

- RAN2 agreed that Key ID is necessary to be carried in the PDCP PDU header

2. Actions to SA3:

RAN2 respectively asks SA3 to take the above information into account for subsequent specification work and provide their feedback for question 1 and question 3:

Actions to CT1:

RAN2 respectively asks CT1 to take the above information into account and wants to confirm that PDCP re-establishment trigger will be captured in CT1’s specification.

3. Date of Next RAN2 Meetings:

TSG-RAN WG2 Meeting #110	1 – 12 June 2020	Electronic

TSG-RAN WG2 Meeting #111	24 – 28 August 2020	Toulouse, France

# Comments

Redundant with action part

I think it is per SLRB instead of per SL QoS flow which was discussed online.

Maybe one example is sufficient to avoid further argument i

We are fine to remove “SL QoS flow”.

Not sure what does this question mean. If the intention is to ask whether re-keying procedure will result in reset of PDCP COUNT, I guess we should not ask since this is purely RAN2 issue and our understanding is PDCP COUNT will carry on since key is changed. If the intention is to ask what will trigger re-keying, I guess we go too far away. Therefore this question should be removed.

Apple: We also feel this is not needed since PDCP COUNT wrap around is defined in RAN2 spec.

We need your clarification with this question what we’d like to hear from SA3. As OPPO and Apple commented, if it is related with PDCP COUNT wrap around handling, then we don’t have to ask. During yesterday’s online discussion, we felt that companies think that PDCP COUNT wrap around handling is not that related with this rekeying issue and can be handled as Uu.