3GPP TSG-RAN WG2 Meeting #109bis-e                                      R2-2004083

Electronic, 20 April – 30 April 2020

Title:	[Draft] LS response to SA3 on the security related issues for NR SL

Response to:

Release:	Rel-16

Work Item:	5G_V2X_NRSL-Core

Source:	CATT [to be RAN2]

To:	SA3

Cc:	CT1

Contact Person:

#### Name:	Da Wang

#### E-mail Address:	wangda@catt.cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

# 1. Overall Description

RAN2 would like to thank SA3 for the reply LS on NR V2X Security issue and PDCP SN size (S3-200478) to inform RAN2 of the security related fields/information for AS ciphering and integrity protection.

- Regarding5-bit input for the security algorithms derived from a specific LCID, RAN2 has made following working assumption.

1: Working assumption: the 5 least significant bits of LCID can be used as 5-bit input to the ciphering/integrity algorithms. Working assumption will be RAN2 agreement if there is no SA3 concern until next RAN2 meeting.

Please note that the 5 least significant bits of LCID can uniquely identify SLRB, as specified in TS 38.321:

- Table 6.2.4-1 Values of LCID for SL-SCH

| Index | LCID values |
| --- | --- |
| 0 | SCCH carrying PC5-S messages that are not protected |
| 1 | SCCH carrying PC5-S messages "Direct Security Mode Command" and "Direct Security Mode Complete" |
| 2 | SCCH carrying other PC5-S messages that are protected |
| 3 | SCCH carrying PC5-RRC messages |
| 4-19 | Identity of the logical channel |
| 20-61 | Reserved |
| 62 | Sidelink CSI Reporting |
| 63 | Padding |

- RAN2 agreed PDCP re-establishment is triggered for re-keying procedure. In order to better understand the impact on AS layer, RAN2 respectfully ask SA3 f following question:

Question 1: What is the granularity of the re-keying procedure, e.g., per PC5 unicast link?

- Regarding Counter Check procedure, RAN2 would like to ask SA3following question:

Question 2: Is Counter Check procedure needed in PC5 interface for SL unicast DRB?

2. Actions:

RAN2 respectfully asks SA3 to take the above information into account for subsequent specification work and provide their feedback for above questions.

3. Date of Next RAN2 Meetings:

TSG-RAN WG2 Meeting #110	1 – 12 June 2020	Electronic

TSG-RAN WG2 Meeting #111	24 – 28 August 2020	Toulouse, France

# Comments

We think according to the minutes, for compromise, we can cc to CT1.

We think according to the majority view, one example is enough. If SA3 has other solutions, they can anyway feedback to us.

I think it is per SLRB instead of per SL QoS flow which was discussed online.

Maybe one example is sufficient to avoid further argument i

We are fine to remove “SL QoS flow”.

We agree with the comments that RAN2 does not need to ask about PDCP COUNT wrap around. For this question, our view is RAN2 should understand from a security perspective if a reset of COUNT is required when PDCP re-key is performed.  Our suggestion (from the prior version) is:

Question 2: Does the re-keying procedure trigger require reset of the PDCP COUNT wrap around in SL unicast

According to majority view, we think it’s unnecessary to ask SA3 the PDCP COUNT issue. Thus, we prefer to remove it.

I don’t think we need to inform SA3 this, since this is purely SA3 issue and we just agree to follow SA3’s decision on this.