3GPP TSG RAN WG2 #110-e	draft R2-20xxxxx

Electronic meeting, 1 – 12 Jun 2020

Source: 	Huawei, HiSilicon

Title: 	[draft] Summary for Offline [010][NR15] Measurements and System Information

Agenda Item:	5.4.1.2

Document for:	Discussion and decision

# Introduction

This document contains a list of TDocs covered in the following offline discussion:

[AT110e][010][NR15] Measurements and System Information (Huawei)

Scope: Treat R2-2004363 R2-2005419, R2-2005420, R2-2005421, R2-2005422, R2-2005392, (proponents are responsible to explain and drive)

Part 1: Decision whether to make corrections or not, identify agreeable corrections. Deadline: June 4, 0700 UTC.

Part 2: For agreeable parts, continuation to agree CRs. Deadline: June 10, 0700 UTC

Companies are invited to share their views on each TDoc submitted.

# Discussion

## R2-2004363 LS on UE reporting criteria (contact: Nokia)

Q1: Do you think any RAN2 action is needed for this LS? If YES, please clarify.

| Company | Any action needed? (YES/NO) | Comments |
| --- | --- | --- |
| Huawei | NO | Before receiving the RAN4 reply LS, RAN2 has defined the MN-SN coordination on measId, with Stage 3 and Stage 2 CRs agreed. |
| ZTE | NO | Agree with Huawei. |
| vivo | No | Agree with Huawei. |

## R2-2005419, R2-2005420 36331 CR on inter-RAT SFTD measurements

Q2: Do you agree with the changes in R2-2005419/R2-2005420?

| Company | YES/NO | Comments |
| --- | --- | --- |
| Huawei | YES | Motivation for the change: 1) The current text is inconsistent with RAN4 spec; 2) Although relying on explicit deletion by the NW is also feasible, autonomous removing the measId is a more robust solution from UE’s perspective. Compared with the version (R2-2003734/R2-2003735) submitted to the previous meeting, the clarification was made in a note and only applies when the network does not configure the UE to remove the measId, therefore NBC problems were avoided. |
| ZTE | No | We understand the intention, however, if not all UEs support autonomous removal of measId, then from network perspective, network anyway has to explicitly release the measId during SN addition. Therefore, autonomous release mechanism is redundant. In addition, we don’t think the 331 spec is inconsistent with RAN4 spec, regarding UE’s implementation, UE can stop SFTD measurement when PSCell is configured. But the RAN4 sentence does not imply the measId must be removed. Of course, a smart network implementation will trigger measId release in this case. |
| vivo | Yes | Autonomous removing of the measId can avoid explicit release signaling |

## R2-2005421, R2-2005422 38331 CR on inter-RAT SFTD measurements

Q2: Do you agree with the changes in R2-2005421/R2-2005422?

| Company | YES/NO | Comments |
| --- | --- | --- |
| Huawei | YES | In the 109bis-e meeting, the 1st and 3rd change were agreed R2-2003701 Correction to inter-RAT SFTD measurements Huawei, HiSilicon CR Rel-15 38.331 15.9.0 1578 - F NR_newRAT-Core R2-2003702 Correction to inter-RAT SFTD measurements Huawei, HiSilicon CR Rel-16 38.331 16.0.0 1579 - A NR_newRAT-Core [010] 1st and 3rd changes are agreed [010] revised However, we failed to provide a revised version due to some mistake. R2-2005421/R2-2005422 keeps the 1st and 3rd changes of R2-2003701/R2-2003702 and the 2nd change was removed. |
| ZTE | Yes |  |
| vivo | Yes |  |

## R2-2005392 Corrections to SIB1 Processing

Q2: Do you agree with the changes in R2-2005392?

| Company | YES/NO | Comments |
| --- | --- | --- |
| Huawei | YES | The changes look reasonable to us. |
| ZTE | Yes | We also think the proposed changes are reasonable. |
| vivo | Yes |  |

# Conclusion

To be added.