3GPP TSG-RAN WG2 Meeting #110-e                         R2-2005441

# Electronic Meeting, 1 June – 12 June, 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 38.306 | CR | 0242 | rev | 4 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network | x | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Introduction of signalling for high-speed train scenarios |
| --- | --- |
| Source to WG: | CMCC, Huawei, HiSilicon, CATT, Ericsson |
| Source to TSG: | R2 |
| Work item code: | NR_HST-Core |  | Date: | 2020-05-22 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | As per the LS R2-2000040/R4-1915855 and R4-1915916, RAN4 requests RAN2 to introduce the UE capability to support NR HST in Rel-16. In RAN2 #109-e, there are following agreements on signaling design for NR HST: Introduce new UE capability for NR HST to indicate whether UE is capable of supporting the enhanced RRM requirements. Introduce new UE capability for NR HST to indicate whether UE is capable of the enhanced demodulation processing for HST-SFN joint transmission scheme with velocity up to 500km/h. As per the LS R4-2005192, more details are provided for the UE capability on NR HST. |
| Summary of change: | Early implementation of HST enhancement by Rel-15 UE does not cause any inter-operability issues. Add the UE capabilities for high speed as follows: measurementEnhancement-r16 demodulationEnhancement-r16 For the FDD-TDD DIFF, replacing “TBD” with “No” according to RAN4 LS R4-2005192. |
| Consequences if not approved: | The UE capabilities are not defined for NR HST in Rel-16 |
| Clauses affected: | 4.2.15 |
|  | Y | N |  |  |
| Other specs | x |  | Other core specifications | TS 38.331 CR 1464 TS 36.331 CR 4326 TS 36.306 CR 1767 |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

## << Start of changes >>

## 4.2	UE Capability Parameters

## << partially omitted >>

### 4.2.14	RRC buffer size

The RRC buffer size is defined as the maximum overall RRC configuration size that the UE is required to store. The RRC buffer size is 45Kbytes.

### 4.2.xx	High speed parameters

| Definitions for parameters | Per | M | FDD-TDD DIFF | FR1-FR2 DIFF |
| --- | --- | --- | --- | --- |
| measurementEnhancement-r16 Indicates whether the UE supports the enhanced intra-NR and inter-RAT E-UTRAN measurement requirements to support high speed up to 500 km/h as specified in TS 38.133 [5]. This field only applies to SN configured measurement enhancement when EN-DC is configured. | UE | TBD | No | FR1 only |
| demodulationEnhancement-r16 Indicates whether the UE supports the enhanced demodulation processing for HST-SFN joint transmission scheme with velocity up to 500km/h as specified in TS 38.101-4 [18]. This field only applies to SN configured demodulation enhancement when EN-DC is configured. | UE | TBD | No | FR1 only |

## << End of change >>