3GPP TSG-RAN WG2 Meeting #110 electronic	R2-20xxxxx

Online, June 1 – June 12 2020

Agenda item:	6.7.3

Source:	Samsung

Title:	Report of [AT110e][055][IIOT] MAC

Document for:	Discussion

# Introduction

This document is for the following offline discussion:

[AT110-e][055][IIOT] MAC (Samsung)

Scope 1: Treat the email discussion summary in R2-2005645, make agreements as far as possible (difficult discussion can be brought on-line instead, for desicions). Address other relevant issues under 6.7.3.1 not overlapping with the email discussion and/or previous agreements, if any. Address also inter-UE-prioritization below.

Scope 2: Implement meeting agreements in the CR.

Part 1: Agreements (rapporteur to announce deadline)

Part 2: Agreed CRs 38321. Deadline: EOM

# Discussion

## 2.1 Confirmation of Easy Proposals from [Post109bis-e][913]

During the email discussion (R2-2005645), we had the following proposals which were supported by overwhelming majority of companies:

Proposal 1. For closest N determination, TP in R2-2003586 is adopted. Proposal 2. UE continues to use the occasion of the suspended configured grant type 1 when the related UL BWP is activated. Proposal 4. A de-prioritized SR shall be excluded in prioritization. TP proposed by Fujitsu/Huawei/vivo/OPPO/Nokia can be a baseline.

- P1: All companies except one company agree to leave up to UE implementation or are fine with TP in R2-2003586.

1> initialise or re-initialise the configured uplink grant to start in the symbol according to timeDomainOffset, timeReferenceSFN, and S (derived from SLIV as specified in TS 38.214 [7]), and to reoccur with periodicity.

- P2: All companies were ok with this option.

- P4: All companies were ok to fix the problem that a de-prioritized SR could make other uplink grant de-prioritized”. Regarding exact TP,

The rapporteur thinks those proposals can be considered as potential easy agreements, so would suggest to agree.

Q1. If you do not accept any of proposals above, please explain the reason. (If you could accept all, you can skip Q1)

| Company | Proposal | Reason why it is not acceptable. |
| --- | --- | --- |

## 2.2 Issue #3: De-prioritization by already de-prioritized SR

In RAN2#109bis-e, RAN2 confirmed a problem that an already de-prioritized uplink grant may need to be prioritized, after high-priority data arrival, as seen the figure below:

Figure 1. (Potential) Problematic scenario

RAN2 confirms the following problematic scenario happens for the case of two PDUs generation: “An already de-prioritized uplink grant needs to be prioritized after high-priority data arrival. But the current normative text does not allow it”

How to fix in the spec will be discussed in the next meeting.

Regarding how to capture in the spec, following two options were supported most during the email discussion (R2-2005645):

- Option 1: Remove the current condition to perform the prioritization (R2-2002778, vivo): When and how many times UE performs the prioritization is totally up to UE implementation.

  - Supported by 13 companies: SONY, Huawei, LG, vivo, CATT, Sharp, ITRI, Nokia, MediaTek, Ericsson, Apple, Sequans, Qualcomm

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. …

- Option 2: Add a condition (R2-2002942, Samsung): Allow prioritization when the priority of an uplink grant changes.

  - Supported by 11 companies: Fujitsu, Lenovo, ZTE, vivo, Intel, OPPO, Nokia, Samsung, Ericsson, Apple, Sequans

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant or whose priority has changed higher: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. …

During the email discussion, OPPO proposed slightly different alternative:

- Option 2-1: Add a condition (R2-2005337, OPPO)

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant or whose priority has changed higher than the priority of other overlapping uplink resource(s): 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. …

During the email discussion, most companies thought both option 1 and option 2 (or 2-1) would work. The rapporteur thinks none of them has any critical blocking point. The rapporteur would suggest the final check on company view and decide based on majority view.

Q2) Companies are invited to provide your preference(s):

- Option 1: Remove the current condition “for each uplink grant which is not already a de-prioritized uplink grant”

- Option 2: Add a condition: “whose priority has changed higher”

- Option 2-1: Add a condition: “whose priority has changed higher than the priority of other overlapping uplink grant(s)”

| Company | Preference | Comments (if there is a critical reason for a specific option) |
| --- | --- | --- |
| LG | Option 1 | But even if the CG (having higher L1 priority) is re-evaluated to be higher LCH priority, the MAC PDU on CG may not be transmitted by the PHY if there is not enough processing time in PHY. Thus, we have to consider the MAC PDU not transmitted by the PHY as a de-prioritized grant, as addressed in Issue #6. |
| Samsung | Option 2 | No strong view.. both options would work. The intended UE implementation will be the same. |
| ZTE | Option 2 |  |
| Lenovo | Option 2 |  |
| OPPO | Option 2-1 (or 2) | From our point of view, any solution can work. But, if we go to Option 2-1 or 2, the UE processing load is decreased. In addition, we think there is one further issue to be discussed. In details, if the resource is deprioritized by another uplink grant which is not already deprioritized, and the uplink grant is changed to deprioritized, the resource should be changed to prioritized again. For example, At t1: Grant 1 and Grant 3 are deprioritized by Grant2. At t2: The priority of Grant 3 is changed higher than the priority of Grant 2. Grant 3 is identified as prioritized, then Grant 2 is changed as deprioritized. Accordingly, Grant 1 should be changed as prioritized. Thus, we propose to allow prioritization for the uplink grant which is originally deprioritized by another grant and the another grant is changed to deprioritized later. |
| ASUSTeK | Option 1 |  |

## 2.3 Issue #5: Autonomous transmission after BWP switching

During the email discussion, most companies agreed that autonomous Tx cannot be continued after BWP switching. But companies had different understandings on the current behaviour.

- Huawei, OPPO point out that it is not clear whether CGs on different BWPs are viewed as the same CG configuration.

- ZTE, vivo, Sharp, Intel, MediaTek, Samsung, and Sequans see that CG configurations are per BWP. Thus, CGs on different BWPs cannot be the same configuration.

- ITRI has a different view that those are viewed as the same  CG configuration.

- Ericsson mentioned that type 2 CG on deactivated BWP is cleared and prefers to align.

As a start point, we need to discuss whether CG configurations with the same HARQ process on different BWPs are considered as the same CG configuration.

- If the answer is yes, current texts allow autonomousTx after BWP switching.

- If the answer is no, current texts do not allow. We may need to specify something.

Depending on the correct answer, we can discuss further whether and how to change the text or current behaviour.

Q3) Companies are invited to provide your view:

- A) CG configurations with the same HARQ process on different BWPs are for the same CG configuration.

- B) CG configurations with the same HARQ process on different BWPs are different and separate CG configurations.

| Company | A/B | Comments (if there is a critical reason for a specific option) |
| --- | --- | --- |
| LG |  | We think it doesn’t matter whether it is same or different CG configuration. We don’t see any problem with the current specification to perform autonomous transmission as long as the TB size matches. |
| Samsung | B | Since CG is configured per BWP basis, they are different configurations. The autonomous transmission cannot be continued. Anyway, we agree with LG that continuation of autonomous TX does not have a problem. But current spec does not allow it, if they are different configurations. |
| ZTE | B | In the current RRC structure, One CG configuration is configured in a granularity of BWP. For two CG configurations are configured for different BWP with the same TB-size and HARQ process ID, if LCH restriction for CG#1 is to map to LCH#1 while LCH restriction for CG#2 is to map to LCH#2, the auto-Retransmission will defer the transmission of data from LCH#2, especially for TSN service, the delay caused by the auto-retransmission seems not reasonable. In addition, NW still can schedule a retransmission after BWP swtich if needed. |
| Lenovo | B | We agree basically that CG configurations are defined per BWP and from that perspective B would be the correct understanding. However, we think that the current spec doesn’t prevent autonomous (re)transmissions upon BWP switching even if we assume that CG configurations are different. Essentially the condition for determining whether to perform an autonomous transmission is more related to the HARQ process and not to the same CG configuration. else if the previous uplink grant delivered to the HARQ entity for the same HARQ process was a configured uplink grant (i.e. retransmission on configured grant): It should be noted that HARQ protocol operation continues across different BWP(s). Therefore we think if we agree on B, some clarification in the spec is required. |
| OPPO | B | According to ASN.1 structure, the CG is configured per BWP per serving cell. One CG will be identified by CG index, BWP index, serving cell index. Clearly, the CG on different BWP is not the same CG configuration. |
| ASUSTeK | B | In RRC, configuredGrantConfig is per UL BWP configuration. Therefore, CGs on different BWP should be treated as different CGs. |

## 2.4 Issue #6: Prioritization with Equal L1 (PHY) Priority

Regarding prioritization with equal PHY priority, RAN1 made the following agreements:

Agreement RAN2 changes MAC specification to accommodate current PHY behaviour. With this option, MAC will avoid providing second MAC PDU with the same L1 priority to PHY, meaning that PHY would transmit the packet with lower LCH priority data. Send an LS to RAN2 to inform them of this agreement LS is endorsed in R1-200XXXX

Then, it seems clear that MAC shall not provide the second PDU to PHY. However, there are different view whether to generate the second PDU:

- Not to generate the second PDU: Nokia (R2-2004922), Samsung (R2-2005647), Fujitsu (R2-2004890, R2-2004891), CATT (R2-2004588), Ericsson (R2-2004959), SHARP (R2-2004885), OPPO (R2-2005337)

- Always generate the second PDU: LG (R2-2005503), SONY (R2-2005149)

Q4) Do companies agree that the MAC entity shall not generate the second PDU for equal L1 priority?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| LG | No | We want to discuss this issue together with the Issue #3 and Issue #8. RAN1 currently discusses how to handle the second MAC PDU (based on the RAN2 LS on the equal L1 priority), and it seems that PHY is not able to transmit the second MAC PDU if the second MAC PDU is received within the processing time. In other words, even if the MAC determines that the second MAC PDU has higher L1 priority and higher LCH-based priority, the second MAC PDU may not be transmitted due to short processing time in PHY. In Issue #3, if the re-evaluated UL grant is determined to have higher priority, the MAC will submit the second MAC PDU to PHY, but it may not be transmitted by the PHY. In Issue #8, the MAC PDU submitted by MAC may not be transmitted by the PHY if CI is received. As there is a case that the MAC PDU submitted by the MAC is not transmitted by the PHY, we propose to have a single solution to cover all cases. The single solution would be that when a MAC PDU is not transmitted by the PHY, the PHY indicates to MAC that the MAC PDU is not transmitted (due to e.g. lack of processing time, reception of CI, etc), and the MAC considers the MAC PDU as a de-prioritized grant. With this single solution, we don’t need to consider a special handling for the case of equal L1 priority. Taking the L1 priority into consideration when performing LCH-based prioritization would make the UE implementation much complex. |
| Samsung | Yes | We can simply add a condition “if PHY can transmit the uplink grant” for generating the second PDU or prioritizing the second uplink grant. |
| ZTE | Yes | Share the same view with Samsung |
| Lenovo | Yes | Agree with Samsung |
| OPPO | Yes | According to RAN1’s LS reply, multiple MAC PDUs are not allowed to send to PHY, thus, the only way MAC can do is only generated one MAC PDU, and send it to PHY. Considering RAN1 wants to follow R15 principle for the case with the same PHY priority, RAN2 needs to specify different behaviours for different cases. In details, RAN2 needs to discuss the exceptional condition, e.g., by only delivering one CG (for CG/CG collision), by prioritizing DG (for CG/DG collision) and by deprioritizing SR (for PUSCH/PUCCH-SR collision). |

## 2.5 Issue #7: Priority of SR Triggered by MAC CE

In RAN2#109bis-e, RAN2 agreed not to consider MAC CE priority in intra-UE prioritization. However, it may be still unclear whether and how to prioritize the SR triggered by MAC CE, not by LCH.

- Prioritize SR triggered by MAC CE or leave up to UE implementation whether to prioritize: vivo, OPPO (R2-2004738), ZTE (R2-2005124)

- Specify how to handle SR triggered by MAC CE: ASUSTek (R2-2005565)

- No need to change the spec. SR will be cancelled: CATT (R2-2004587)

Q5) Companies are invited to provide your preference(s) or acceptable options:

- Option 1: Prioritize SR triggered by MAC CE

- Option 2: De-prioritize SR triggered by MAC CE

- Option 3: Up to UE implementation (UE can prioritized or not prioritize the SR)

- Option 4: No need to specify at all

| Company | Preference | Comments (if any) |
| --- | --- | --- |
| LG | Option 4 | There is no problem to prioritize PUSCH over SR, because those MAC CEs have higher priority than LCHs, and they will be included in the MAC PDU. |
| Samsung | Option 1 or 2 | We prefer to have a deterministic UE behaviour. Regarding CATT’s comments, we cannot say that the SR will be always cancelled. For instance, if the MAC PDU is already generated and stored in the HARQ buffer, the MAC CE cannot be included. This can occur in case of a normal retransmission. |
| ZTE | Option 3 | For this issue ,we would like to give a chance to UE for determining which transmission is more important in the case that the SR triggered by MAC CE is collided with UL-SCH transmission. And regarding the collision case is complicated, for example, SR triggered by BFR is collided with the URLLC PUSCH transmission, or SR triggered by LBT is collided the PUSCH transmission with BFR MAC CE. This is time consuming to discuss how to find a appropriate way in such late stage, thus we propose to defer this discussion about a detail solution in the next release. For the current release, we just leave it to UE implementation |
| Lenovo | Option 1/2 | We think that there should be a deterministic UE behaviour for such cases. Typically the SR triggered by MAC CE (BFR/LBT) is of high priority, e.g. SR for BFR is prioritized over other SRs on PUCCH. Therefore Option 1 seems reasonable to us. |
| OPPO | Option 1 or 2 | We prefer a deterministic UE behaviour. But if it is hard to compromise, we can leave it to UE implementation. |
| ASUSTeK | Option 2 | Since MAC CE is not considered in intra-UE prioritization, it is straightforward to deprioritize SR triggered by MAC CE as well. |

## 2.6 Issue #8: Autonomous Transmission for Cancelled Uplink Grant

In eURLLC WI, pre-emption based on cancellation indicator (CI) was introduced. If a UE has granted resources (PUSCH or SRS) overlapped with cancellation area, such transmissions should be cancelled (stopped or even not started). This cancelled resource could be a CG. The issue here is whether the MAC entity should perform the autonomous transmission by considering the CG as a de-prioritize uplink grant. This situation may be similar with the scenario of autonomous transmission, as described in Figure 2.

Figure 2. Pre-emption by cancellation indicator (R202004964, Ericsson)

Ericsson proposed to follow the same behaviour, i.e. autonomous transmission by de-prioritizing cancelled CG.

- UE autonomously transmits the MAC PDU of the CG, cancelled by Cancellation Indicator (CI), in the next CG resource from the same CG configuration with the same HARQ process ID: Ericsson (R2-2004964, R2-2004965)

Q6) Do companies agree that a CG cancelled by Cancellation Indicator (CI) should be considered as a de-prioritized uplink grant and the MAC entity autonomous transmit the MAC PDU in the subsequent CG?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| LG | Yes | The UE cannot expect whether the CI is received or not. Thus, there is no other ways to resolve this issue than considering it as a de-prioritized grant. For this, the PHY should provide indication to MAC that the MAC PDU is not transmitted by the PHY. |
| Samsung | Yes/No | No strong view. - If we agree, at least an Editor’s Note or a normative text is necessary. - If we do not agree, the current spec does not allow autonomous TX for cancelled CG. |
| ZTE | Yes | In addition to make the CG which is pre-empted as a de-prioritized grant, we also think the PHY layer need indicate to MAC layer about the pre-emption transmission. |
| Lenovo | Yes |  |
| OPPO | Yes/No | We have no strong views. It is an enhancement to inter-UE prioritization. If majority agree with this modification, we are fine to have it. In addition, to assure autonomous transmission for this CG, we also think PHY layer needs to indicate MAC layer the pre-emption information. |
| ASUSTeK | Yes |  |

## 2.7 Issue #9: SR vs PUSCH Related with Random Access

Even in LCH-based prioritization, random access related PUSCH resource, i.e. uplink grant received in RAR or temporary C-RNTI, MSGA transmission is always prioritized. In the current text, if SR overlaps with random access related uplink grant, the MAC entity compares priorities. However, it is not possible (those resources do not have priority) nor consistent with collision between PUSCHs.

- In case that lch-basedPrioritization is configured, and the PUCCH resource of SR transmission overlaps with uplink grant received in RAR, or addressed to temporary C-RNTI, or with MSGA transmission, the SR is not transmitted: Samsung (R2-2005648)

Q7) Do companies agree that SR overlapping with uplink grant received in RAR, or addressed to temporary C-RNTI, or with MSGA transmission cannot be transmitted?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| LG | Yes | We think the proposal is aligned with Rel-15 principle. |
| Samsung | Yes | Agree with LG that it is aligned with Rel-15 principle and Rel-16 Data-Data prioritization. Otherwise, SR can prioritize uplink grant received in RAR. |
| ZTE | Yes |  |
| Lenovo | Yes |  |
| OPPO | Yes | We also prefer to align with Rel-15 principle. |
| ASUSTeK | Yes |  |

## 2.8 Issue #10: Prioritization for Non-Overlapping Scenario

In IIOT WI, intra-UE prioritization is considering only overlapping resources. However, we may need to additionally consider a scenario of prioritization between non-overlapping uplink grants sharing the same HARQ process. For instance, in Figure 3, after the transmission of PDU A, the CG for PDU B may have higher priority. However, the CG cannot be used due to running ConfiguredGrantTimer.

Figure 3. HARQ process collision between two UL grants with different priorities (R2-2005566, ASUSTeK)

- Prioritization with non-overlapping PUSCH duration: ASUSTeK (R2-2005566)

Q8) Do companies agrees to discuss prioritization between non-overlapping CG and DG with the same HARQ process?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| LG | No | If we allow new PDU transmission while the CG timer is running, it will lead to data loss. We think ensuring prioritized transmission does not mean that data loss is allowed. |
| Samsung | No | Agree with LG that it will lead to data loss. Also, NW should allocate DG, by considering potential de-prioritization of the following CG. |
| ZTE | Yes. but in the next release. | This issue was actually existing, but we think this is too late to discuss this issue at the current stage of release, since for solving this issue we need do more work for avoiding the data loss. We suggest to defer this discussion to Rel-17 |
| Lenovo | No | Agree with LG, at least for Rel-16 |
| OPPO | No | We have some sympathy on this issue, but there may be no much time for further discussion. At this stage, we hope the issue can be avoided by the network scheduling. And, it can be discussed in the next release. |
| ASUSTeK | Yes | In RAN2#103bis, an agreement was made that prioritization regarding collision between HARQ processes can be addressed in Rel-16 WI. Since this issue exists and can occur often in IIOT scenarios, we prefer to handle this as soon as possible. |

## 2.9 Issue #11: Capturing Agreement on Resource Selection in Autonomous Transmission

vivo and Samsung (R2-2004739) point out that we did not capture the following agreement:

RAN2#109-e agreement When the CG is de-prioritized, it is up to the UE implementation to determine the processing time restriction determining whether the very next CG resource with same HARQ process can be used, or the/a following one, for an autonomous transmission.

Since the MAC specification does not say anything about that agreement, the current text may mandate the UE to select the immediate next CG for autonomous retransmission. vivo and Samsung proposed to add a NOTE as follows:

NOTE: It is up to the UE implementation to determine the processing time restriction of the uplink grant while determining whether a configured grant configured with autonomousTx can be used for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant.

Q9) Do companies agree to add the following NOTE for the RAN2#109-e agreement?

NOTE: It is up to the UE implementation to determine the processing time restriction of the uplink grant while determining whether a configured grant configured with autonomousTx can be used for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant.

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| LG | No | The processing time should be always considered. Having the NOTE only for this case makes more confusion. Maybe generic NOTE would be better. |
| Samsung | Yes | The implementation of the agreement is missing. |
| ZTE | No | We think if the processing time is not enough UE will always not generate a MAC PDU...I cannot figure out whether this note is necessary since UE have no choice under this scenario. |
| Lenovo | Yes | We agree with Samsung. We also already pointed out the issue in an earlier contribution, that current spec mandates the UE to check whether immediately previous configured uplink grant is deprioritized. However, UE should not check whether the immediate previous configured uplink grant for this HARQ process was deprioritized, but rather whether the previous configured uplink for which UE made a transmission attempt was de-prioritized. We support adding a NOTE in the spec. |
| OPPO | Yes | With this note we can make it more clear. |

## 2.10 Issue #12: Priority of Uplink Grant with No Data

The priority of an uplink grant for which no data is multiplexed or can be multiplexed is lower than the priority of an uplink grant for any logical channel is multiplexed or can be multiplexed. This condition considers only Data-Data prioritization, but does not consider SR-Data prioritization. ZTE (R2-2005124) proposed to correct this to cover SR-Data prioritization.

- TP in R2-2005124, ZTE

The priority of an uplink grant for which no data for logical channels is multiplexed or can be multiplexed in the MAC PDU is lower than either the priority of an uplink grant for which data for any logical channels is multiplexed or can be multiplexed in the MAC PDU or the priority of an SR triggered by one LCH.

Q10) Do companies agrees the correction above?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Samsung | Yes | No technical change but a correction. It looks clearer |
| ZTE | Yes |  |
| Lenovo | Yes |  |
| OPPO | Yes |  |
| ASUSTeK | Yes |  |

# Conclusion

# Annex: Discussions in R2-2005645

## 2.1 Issue #1: Closest N determination

The first issue is how to capture the determination of the closest Nth CG occasions of the type-1 CG, according to the following agreement and Editor’s Note:

Agreement in RAN2#109-e

For Type-1 CG, after receiving the configuration, UE should first identify the lowest N value corresponding to the nearest available CG occasion, then, N is incremented after each CG occasion starting from the N identified in the first step.

Editor’s Note in TS38.321 v16.0.0 and endorsed MAC CR (R2-2004289)

Editor's Note: The step of determining the closest N needs to be added.

In RAN2#109bis-e meeting, there was a discussion but no consensus on agreeable TP. Assuming the simple and clear TP, we can have the following options:

- Option 1: Nokia (R2-2003169)

Upon configuration of a configured grant Type 1 for a Serving Cell by upper layers, the MAC entity shall: 1> store the uplink grant provided by upper layers as a configured uplink grant for the indicated Serving Cell; 1> initialise or re-initialise the configured uplink grant to start in the symbol which is determined according to timeDomainOffset and S (derived from SLIV as specified in TS 38.214 [7]), and which is the closest in time following the reception of the configured grant configuration; 1> consider the configured uplink grant to occur with periodicity.

- Option 2: CATT (R2-2002753)

After an uplink grant is configured for a configured grant Type 1, the MAC entity shall consider sequentially that the Nth uplink grant occurs in the symbol for which: [(SFN × numberOfSlotsPerFrame × numberOfSymbolsPerSlot) + (slot number in the frame × numberOfSymbolsPerSlot) + symbol number in the slot] = (timeReferenceSFN × numberOfSlotsPerFrame × numberOfSymbolsPerSlot + timeDomainOffset × numberOfSymbolsPerSlot + S + N × periodicity) modulo (1024 × numberOfSlotsPerFrame × numberOfSymbolsPerSlot) where N >= 0 and N is the smallest value corresponding to the closest available CG occasion after configured grant Type 1 configuration.

- Option 3: ZTE (R2-2003586)

Upon configuration of a configured grant Type 1 for a Serving Cell by upper layers, the MAC entity shall: 1> store the uplink grant provided by upper layers as a configured uplink grant for the indicated Serving Cell; 1> initialise or re-initialise the configured uplink grant to start in the symbol according to timeDomainOffset, timeReferenceSFN, and S (derived from SLIV as specified in TS 38.214 [7]), and to reoccur with periodicity.

Note that all those options assume the same UE behaviour. During the online and offline discussions in RAN2#109bis-e, some companies thought the determination of the Nth CG occasion can be handled by UE implementation, mainly due to concerns about the UE processing time and “the closest” term being too strict for the UE. On the other hand, it was indicated that leaving the behaviour completely to UE implementation may lead to misalignment between the UE and the network. Eventually, the discussion resulted in the following Chairman notes and decision:

Chair: it seems that it is assumed that start/intializaion is from the moment of configuration, and opportunities are available from there, but detailed timing such as UE processing time is for implementation. The change in the time domain offset seems agreeable, not sufficient support to clarify closest N, at least the way that was proposed here, can discuss more.

Q1) Companies are invited to provide their view on whether and how to solve the issue, e.g. based on one of the TPs above, some variation of them or another proposal.

| Company | Comments |
| --- | --- |
| Fujitsu | We agree that all options seem to assume a same UE behaviour. However, we think that nothing needs to be clarified (UE implementation could solve this issue), but if MAC update is needed, we prefer Option 3 which is the simplest update of MAC. |
| Lenovo | No strong view, but we prefer to leave it to UE implementation. |
| Huawei | UE implementation can solve this issue. If needed, we prefer Option 3. |
| LG | It can be left up to UE implementation. Thus, we prefer Option 3. |
| ZTE | As we suggested, there is no need to define the detail behavior, option 3 is enough, The closest N can be found by UE implementation. |
| vivo | The detailed timing can be left to the UE implementation. We are quite reluctant to use the term “closest”, as this forces the MAC to use such grant even though the grant is unable to be used due to the processing time restriction. This could cause the packet loss at the UE. Option 3 is acceptable to us. |
| CATT | We agree that the “closest” N may not always be achievable considering the processing time, so we prefer leaving it to UE implementation. |
| Sharp | No Strong view. If needed, option 3 is preferred. |
| ITRI | We prefer option 3 to leave it to UE implementation. |
| Intel | We also think that this can be handled by UE implementation. If change to MAC specification is needed, option 3 is preferred. |
| OPPO | It can be left to UE implementation. Considering the different CG periodicity configured and the different UE processing time, it is hard to restrict/specify the first occasion which is used, if the intention is to align the actually used CG resources between the gNB and the UE. In addition, even if N is specified, the associated CG occasion may also not be used due to data unavailability at UE. Thus, Option 3 is preferred. |
| Nokia, NSB | Both Option 1 and the following modified version of Option 2 are acceptable to us: where N >= 0 and N is initialized to the smallest value corresponding to the closest available CG occasion after configured grant Type 1 configuration. Option 3 does not really result in a different behaviour than what is currently specified in the specifications, since the definition of timeDomainOffset (in Section 5.8.2) is already a function of timeReferenceSFN: timeDomainOffset: Offset of a resource with respect to SFN = timeReferenceSFN in time domain; We understand the main concerns is about understanding the word “closest” in a very strict way. It is of course not an intention to violate the UE processing times and obviously the “closest” should consider the processing time. In our opinion this is already expressed by saying “the closest available”, but we could further clarify by saying, e.g. “the closest available and applicable”. Please also note that in the proposal above, it is not said that a UE must use the first available occasion, it is just saying how “N” is initialized. UE may or may not use this occasion for many reasons, e.g. it has not data to send. If that is still unacceptable for some reason, then we could clarify in a note that the UE does not have to start with an “N” equal to 1, but should consider subsequent grants to occur as soon as CG configuration is received. We are strongly against leaving this completely to UE implementation as we cannot afford that some UE implementations, which will implement the specifications literally (i.e. in a correct way actually) will wait with a first transmission until the formula is met for N=1, which may be as long as the duration of a hyper frame in extreme situations. |
| MediaTek | Agree with other companies that this can be left to UE implementation. |
| Samsung | Agree with other companies that we can leave it to UE implementation, but we are ok with clarification of options 1 and 2. Regarding Nokia’s concern on late transmission after hyper frame boundary, we could capture something in the specification or chairman’s note as an agreement. |
| Ericsson | We think most ambiguity of when CG Type 1 is initialized in UE is resolved by including “timeReferenceSFN” as in Option 3. Furthermore, we don’t think that the term “closest” could fix the further uncertainty when UE is ready to transmit on CG after configuration, as UE processing time for RRC configuration is unclear, and HARQ retransmission may happen. gNB needs to be prepared anyway from “best case” moment, i.e. assuming fastest UE processing / no HARQ, to receive on CG resources. It does not pose a problem for gNB if UE does not use those CG resources since didn’t initialize yet, since gNB anyway needs to handle skipped CG transmission from UE due to lack of data. In summary we prefer Option 3. |
| Apple | We agree that the actual details can be left up to UE implementation. No strong view on the options however, if it comes to a majority decision, we would prefer Option 3 due to its simplicity. |
| Sequans | Regarding Nokia’s comment: “a UE will wait with a first transmission until the formula is met for N=1, which may be as long as the duration of a hyper frame in extreme situations”. We had this discussion in Rel-15, it was relevant at that time. However in Rel-16, it seems to us it is less relevant, because we introduced timeReferenceSFN in the MAC formula, with the following definition: “timeReferenceSFN: SFN used for determination of the offset of a resource in time domain. The UE uses the closest SFN with the indicated number preceding the reception of the configured grant configuration” This means MAC formula works e.g. as follows: i.e. most of the time, N=1 occurrence would be “in the past”. The UE would not “wait with a first transmission until the formula is met for N=1”. It seems to us companies agree with the CG occasions occurrence, but prefer to leave it to UE implementation on which exact first CG should be used (first N value). We agree to leave this to implementation, i.e. not mandate to use the “closest”. So we are fine with Option 3 (it helps a bit compared to no change at all). Regarding Nokia’s concern, we are also fine to address it if still not clear enough, e.g. in spec (modified Option 2 with “applicable” seems to work) or in CM note (i.e. confirm the earlier agreement: “For Type-1 CG, after receiving the configuration, UE should first identify the lowest N value corresponding to the nearest available CG occasion, then, N is incremented after each CG occasion starting from the N identified in the first step”) |
| Qualcomm | Option 3 is preferred. For a type-1 CG, the intention is to setup a long-lasting CG occurrence. Even if there is ambiguity in the spec (which we believe is resolved by option 3 anyway), we consider it a corner case to resolve when the long-lasting CG’s first instance occurs. |

< Summary >

- Option 1 or Option 2 (1): Nokia (NSB)

- UE implementation but ok with Option 3 (13): Fujitsu, Huawei, LG, ZTE, vivo, Sharp, ITRI, Intel, OPPO, Ericsson, Apple, Sequans, Qualcomm

- Nothing (fully up to UE) (4): Lenovo, CATT, MediaTek, Samsung

All companies except one company agree to leave up to UE implementation or are fine with minimum change based on TP in T2-2003586 (Option 3)

Proposal 1. For closest N determination, TP in R2-2003586 is adopted.

## 2.2 Issue #2: CG Type 1 continuation after BWP switch

The next issue is how to maintain the CG occasion of type 1 CG after BWP switch. As described in R2-2003586 (ZTE), the source of confusion may be what “(re-)initialization” means, 1) recalculate the CG occasion after BWP activation or 2) keep calculating CG occasion irrespective of BWP switch.

if a BWP is activated and it is not the dormant BWP: … 2> (re-)initialize any suspended configured uplink grants of configured grant Type 1 on the active BWP according to the stored configuration, if any, and to start in the symbol according to rules in clause 5.8.2; … if a BWP is activated and it is dormant BWP for an SCell: … 2> stop all the UL behavior, i.e. stop any UL transmission, suspend any configured uplink grant Type 1 associated with the Scell, clear any configured uplink grant of configured grant Type 2 associated with the Scell; … if a BWP is deactivated: … 2> suspend any configured uplink grant of configured grant Type 1 on the inactive BWP.

There were two interpretations

- Option 1: UE continues to use the occasion of the suspended configured grant type 1 when the related UL BWP is activated

- Option 2: UE recalculates the occasion of the configured grant type 1 based on the timeReferenceSFN, timeDomainOffset, and S and the SFN number when the switch on is occurred.

In RAN2#109bis-e, it remains as an FFS as follows:

FFS if Option 1 or 2

In 38.321 v16.0.0, timeReferernceSFN applies for SFN boundary of the preceding the reception of the CG configuration, not BWP activation. Thus we could say that the current spec assumes Option 1.

In the last meeting, some companies had a concern on UE processing to maintain the suspended CG occasions. If it is a problem at the UE side, we may need to consider Option 2. On the other hand, Option 2 may have a misalignment between UE and NW when UE performs an automatic BWP switch.

Q2) Which option do you prefer and why?

- Option 1: UE continues to use the occasion of the suspended configured grant type 1 when the related UL BWP is activated

- Option 2: UE recalculates the occasion of the configured grant type 1 based on the referenceSFNnumber, timeDomainOffset, and S and the SFN number when the BWP switch takes place.

| Company | Option | Comments |
| --- | --- | --- |
| Fujitsu | Option 1 | Option 1 is the intended behaviour. Option 2 has a drawback of the UE autonomous BWP switching, in which case there may be misalignment between gNB and UE. |
| SONY | Option 1 | This has been our understanding. |
| Lenovo | Option 1 | Agree with Fujitsu |
| Huawei | Option 1 | If, according to Option 2, an UE autonomously switches to another BWP just before a HFN boundary (e.g. with random access which succeeds after several attempts) and the network recognizes that the UE has switched to the new BWP after the HFN boundary, then the UE and the network may have different understanding about the available configured grant type 1 resources. In order to avoid risk of such misalignment, we think Option 1 should be preferred. |
| LG | Option 1 | Option 1 is the correct behavior for CG Type 1. |
| ZTE | Option 1 | In addition to HuaWei’s demonstration, the RACH procedure also can lead to automatic BWP switch, since NW can not deduct the actual BWP switch time point based on the reception of Msg.3 since NW have no idea how many times of the preamble transmission, we still think option 1 is intended behavior. |
| Vivo | Option 1 | The UE autonomous BWP switching may cause the occasion miss-alignment. Not sure whether we need to change anything in the specification, as the specification already states that the occasion calculation is based on the “timeReferenceSFN” at the reception of the RRC message, regardless of the BWP switching. |
| CATT | Option 1 | We agree with Fujitsu on the drawback of option 2. As for option 1, we think a smart UE implementation would not maintain the permanent incrementing of 64 CG type 1 allocations, but would only need to update the stored parameters referenceSFNnumber, timeDomainOffset, and S at each SFN cycle boundary (10240 ms) to account for the potential shift in case the CG period is a non-integer multiple of 10240 ms. So this update only needs to be computed for 64 CG type 1 allocations every 10240 ms, and the associated peak processing can even be distributed sequentially in time by anticipating the calculation in background over a period of time preceding the 10240 ms boundary. Therefore, we don’t view this as a severe complexity issue. |
| Sharp | Option 1 | If we go with option 2, misalignment between gNB and UE may happen. |
| ITRI | Option 1 | Option 1 is the intended behaviour. |
| Intel | Option 1 | Time domain occasions of configured grant should be aligned with traffic patterns. In option 2, there will be misalignment due to the recalculation, which causes additional delay. |
| OPPO | Option 1, but | Considering the definition of timeReferernceSFN, option 1 seems a correct understanding on CG occasion determination. However, we also think there is no need to require UE continuously calculate CG occasion when the BWP is deactivated. How to derive such CG occasion upon BWP reactivation, e.g. using the stored SFN cycle number, or keeping CG occasion calculation when BWP is deactivated, or by other ways, depends on UE implementation. |
| Nokia, NSB | Option 1 | Option 1 allows to keep the alignment between the CG occasions and the traffic periodicity. Option 2 is not desired because it requires reconfiguration of the referenceSFNnumber and timeDomainOffset after BWP activation for periodicities not-integer of 10240 ms. Regarding the concerns on UE processing with Option 1, we don’t think there is need to keep track of each individual “Nth” CG occasion while the BWP is suspended; all that is needed is to re-calculate timeDomainOffset once per SFN cycle as a function of the timeDomainOffset in previous SFN cycle and periodicity. |
| MediaTek |  | While our preference is for option 2, we are willing to compromise and accept option 1 |
| Samsung | Option 1 | We think maintenance of CG occasion is not a big burden to UE. |
| Ericsson | Option 1 | Option 1 is correct behaviour. Option 2 would require further standardization changes to e.g. fix operation for autonomous BWP switch. |
| Apple | Option 1 | It is the most unambiguous. With option 2, there are possibilities of mis-alignment between UE and network. With option 2, different UE implementations might also lead to variations in network implementations. |
| Sequans | Option 1 | Agree with Fujitsu |
| Qualcomm | Option 1 | Agree with the comments from several companies that the UE does not need to necessarily keep calculating each occasion while the CG is suspended, but just needs to act as if it was doing so when the suspension ends. The spec language should be clear on this. |

< Summary >

All companies accept Option 1.

Proposal 2. UE continues to use the occasion of the suspended configured grant type 1 when the related UL BWP is activated.

## 2.3 Issue #3: Already de-prioritized uplink grant after high-priority data arrival

In RAN2#109bis-e, RAN2 confirmed a problem that an already de-prioritized uplink grant may need to be prioritized, after high-priority data arrival, as seen the figure below:

Figure 1. (Potential) Problematic scenario

RAN2 confirms the following problematic scenario happens for the case of two PDUs generation: “An already de-prioritized uplink grant needs to be prioritized after high-priority data arrival. But the current normative text does not allow it”

How to fix in the spec will be discussed in the next meeting.

Companies had different understanding about which options would work or which options would not. Thus, we need to discuss those options with text proposals:

- Option 1: Remove the current condition to perform the prioritization (R2-2002778, vivo): When and how many times UE performs the prioritization is totally up to UE implementation.

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant.

- Option 2: Add a condition (R2-2002942, Samsung): Allow prioritization when the priority of an uplink grant changes.

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant or whose priority has changed higher: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant.

- Option 3: Add a NOTE

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> this uplink grant is a prioritized uplink grant; 3> the other overlapping uplink grant(s), if any, is a de-prioritized uplink grant. NOTE: When to execute the problematic procedure should be up to implementation.

- Option 4: Do nothing but UE/NW implementation should resolve the problem.

Q3) Companies are invited to provide your acceptable option(s).

- Option 1: Remove the current condition to perform the prioritization

- Option 2: Add a condition

  - Option 2-1: Add a condition. Allow prioritization when the priority of an uplink grant  changes higher than the priority of other overlapped uplink resource.

- Option 3: Add a NOTE

- Option 4: Do nothing but UE/NW implementation should do.

| Company | Options | Comments (if any) |
| --- | --- | --- |
| Fujitsu | Option 2 | We should keep the statement highlighted in red i.e. “When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant” because it has specified deterministic UE behaviour for the Case-1 that was discussed in email discussion [RAN2#109-e][036] according to R2-2000797 i.e. L2 (de-prioritized by L1) doesn’t deprioritize L3. The proposed text would be implemented based on the latest version in R2-2004289: Section 5.4.1 When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant or whose priority has changed higher, the MAC entity shall: |
| SONY | Option 1 | We prefer a simple fix where lch-basedPrioritization operates sequentially, that is: each grant or SR has its opprtunity to go through the prioritization procedure once, just before its processing deadline, even if this grant or SR has been already de-prioritized by another earlier grant. Hence, removing “which is not already a de-prioritized uplink grant” is preferred. |
| Lenovo | Option 2 | We think that the Samsung proposal captures the intended behaviour best. |
| Huawei | Option 1 or Option 4 | Option 2 is quite vague since the step for UE to determine whose priority has changed higher is not clearly discussed. We can adopt Option 1 or just rely upon UE/NW implementation to handle this. |
| LG | Option 1 | The problem has to be fixed, and we prefer a simple fix as in Option 1. Option 2 is too vague, and Option 3 and 4 cannot solve the problem. |
| ZTE | Not option 1 | If option 1 is adopted, I am afraid we need to find a new way to implement the following agreement achieved in RAN2#109 meeting: “ An uplink grant is not de-prioritized by other de-prioritized SR or uplink grant. TP in Phase-2 discussion is a baseline.” |
| vivo | Option 1 or Option 2 | The problem of Option 1 is that we need to find another way to capture the agreement to avoid the de-prioritized uplink grant overriding the subsequent SR/PUSCH. Option 2 seems a good way forward. The NOTE of Option 3 is a little bit difficult to understand, as “the problematic procedure” is quite vague. |
| CATT | Option 1 | Option 1 is sufficient because the above issue discussed by Fujitsu is now addressed by the new fix introduced in last meeting: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and (and similar additions for prioritizations of CG and SR). |
| Sharp | Option 1 | Option 1 is the simplest way. |
| ITRI | Option 1 | We prefer a simple fix as in Option 1, and agree with SONY that each grant or SR has its opportunity to go through the prioritization procedure once. |
| Intel | Option 2 | We prefer deterministic UE behaviour. |
| OPPO | Option 2-1 | If option 1 is applied, the prioritization judgement for the already deprioritized grant is done even when no higher priority data arrival. It introduces UE complexity and processing load. Yet, if option 2 is applied, the prioritization judgement is performed only for the case that the priority of the already deprioritized uplink grant changes. Compared to option 1, UE processing load is reduced. However, we also think some enhancement to option 2 should be made, i.e. the condition is changed to something like this: allow prioritization when the priority of an uplink grant changes higher than the priority of other overlapped uplink resource. Considering there might be many cases where the priority of the arrival data is not high enough to trigger the change of the priority comparison relationship among the overlapped uplink resources, Option 2-1 is preferred and valuable. |
| Nokia, NSB | 1 or 2 | We think both Option 1 and Option 2 should be able to “recover” grants that have been de-prioritized due to late data arrival. |
| MediaTek | Option 1 | Agree with CATT |
| Samsung | Option 2 | We agree with Intel and prefer to have a deterministic UE behaviour. Option 1 is also ok to us, but it would be better to give a clearer guidance to UE implementation. |
| Ericsson | Option 1 or option 2 | We understand that by option 1, the agreements that “An uplink grant is not de-prioritized by other de-prioritized SR or uplink grant.“ is captured. the problematic scenario is resolved. Option 2 is also acceptable since it captures exactly the intended behaviour. If it can be confirmed that option 1 has captured the intended behaviours, we prefer option 1 as it is simpler. |
| Apple | Option 1 or Option 2 | We agree with Fujitsu here. |
| Sequans | Option 1 or Option 2 | Both options seem to work, no strong view on which Option to choose as for now. |
| Qualcomm | Option 4, or 1 with changes. | We disagree that the problem under discussion is whether the UE behavior is deterministic or not. The problem was that baseline spec was disallowing (in some companies’ view) the UE to perform more optimized handling of data that arrived between t1 and t2. Option 2 in particular seems quite vague and Option 1 causes extra complexity/operations at the UE. As we stated in the offline email discussion during 109bis-e, the scenario here involves data arriving into the UE buffer within a very narrow window, which is a corner case. So we prefer option 4. But given the majority view, we can live with Option 1 plus a note that says “It is upto the UE whether to perform these steps for a grant that has previously been deprioritized”. |

< Summary >

- Option 1 (13): SONY, Huawei, LG, vivo, CATT, Sharp, ITRI, Nokia, MediaTek, Ericsson, Apple, Sequans, Qualcomm

- Option 2 (11): Fujitsu, Lenovo, ZTE, vivo, Intel, OPPO, Nokia, Samsung, Ericsson, Apple, Sequans,

- Option 3 (1): ZTE

- Option 4 (3): Huawei, ZTE, Qualcomm

Option 1 and Option 2 are almost evenly supported (13 vs 11, 5 companies are ok with either way). Option 3 and Option 4 are not much supported. The rapporteur sees most companies would like to modify the condition of the prioritization by Option 1 or Option 2.

Proposal 3. RAN2 agrees to modify the condition of the prioritization by

- Option 1) removing “which is not already a de-prioritized uplink grant” or

- Option 2) adding “whose priority has changed higher”

## 2.4 Issue #4: De-prioritization by already de-prioritized SR

Another issue raised by vivo during Part 1 discussion is whether already de-prioritized SR could make other overlapping uplink grant de-prioritized. In RAN2#109bis-e meeting, RAN2 agreed to fix a similar problem that a de-prioritize uplink grant could make other uplink grant de-prioritized. The related agreement was

Capture “De-prioritized uplink grant is excluded in prioritization of other grants”. CATT’s TP in the comment is a baseline (adding “which was not already deprioritized”)

The latest endorsed MAC CR (R2-2004289) captures the agreement by restricting comparing uplink grant to that was not already de-prioritized (as seen in the green highlighted text).

1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s).

A potential issue is that it is not clear whether a de-prioritized SR could make other uplink grant de-prioritized. In the current specification, the MAC entity compares the priorities of overlapping uplink grant and “SR transmission”. The question here is whether “SR transmission” here includes a de-prioritized SR. If the answer is yes, we may need to fix the problem.

Q4) Do companies agree the problem?

- Yes, we have to fix it. (Suggestion on TP is encouraged.)

- No, the current text is clear.

| Company | Yes/No | Comments and TP |
| --- | --- | --- |
| Fujitsu | Yes | In fact, RAN2 already agree in RAN2#109-e that “an uplink grant is not de-prioritized by other de-prioritized SR or uplink grant”. The agreement seems not exactly captured in the MAC. The focus of the email discussion [RAN2#109-e][036] was “an uplink grant de-prioritized by an SR is not assigned the de-prioritized status”, but didn’t discuss the necessity of capturing the priority status of the SR. The priority status of the SR needs to be captured. Our suggestion for the MAC improvement is shown below with cyan text based on the latest version in R2-2004289: Section 5.4.1 When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant, the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP where the priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission occasion which was not already de-prioritized where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). Section 5.4.4 2> if the PUCCH resource for the SR transmission occasion does not overlap with a measurement gap: 3> if the PUCCH resource for the SR transmission occasion overlaps with neither a UL-SCH resource nor an SL-SCH resource; or 3> if the MAC entity is configured with lch-basedPrioritization, and the PUCCH resource for the SR transmission occasion overlaps with any UL-SCH resource(s), and the priority of the logical channel that triggered SR is higher than the priority of the uplink grant(s) for any UL-SCH resource(s) where the uplink grant was not already de-prioritized, and the priority of the uplink grant is determined as specified in clause 5.4.1; or 3> if a SL-SCH resource overlaps with the PUCCH resource for the SR transmission occasion for the pending SR triggered as specfied in clause 5.4.5, and the MAC entity is not able to perform this SR transmission simultaneously with the transmission of the SL-SCH resource, and either transmission on the SL-SCH resource is not prioritized as described in clause 5.22.1.3.1 or the priority value of the logical channel that triggered SR is lower than ul-Prioritizationthres, if configured; or 3> if a SL-SCH resource overlaps with the PUCCH resource for the SR transmission occasion for the pending SR triggered as specfied in clause 5.22.1.5, and the MAC entity is not able to perform this SR transmission simultaneously with the transmission of the SL-SCH resource, and the priority of the triggered SR determined as specified in clause 5.22.1.5 is higher than the priority of the MAC PDU determined as specified in clause 5.22.1.3.1 for the SL-SCH resource: 4> consider the SR transmission occasion as a prioritized SR transmission occasion; 4> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s); 3> else: 4> consider the SR transmission occasion as a de-prioritized SR transmission occasion; |
| SONY | Yes | It must be fixed. |
| Lenovo | Yes | Since RAN2 already agreed that an uplink grant is not de-prioritized by other de-prioritized SR or uplink grant, we think that this agreement should be also clearly reflected in the specification. |
| Huawei | Yes | Fujitsu’s proposed TP can be a baseline. Besides, in Section 5.4.1, prioritization determination for a configured uplink grant shall also be updated: 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission occasion which was not already de-prioritized where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). |
| LG | Yes | It must be fixed similar to deprioritized uplink grant. TP can be discussed later. |
| ZTE | Yes | Agree with Fujitsu and huawei |
| vivo | Yes | The issue is illustrated in the above figure. Grant 1 with higher priority de-prioritizes SR. But the SR can further de-prioritizes the Grant2 according to the current specification. As a result, only grant1 can be transmitted. Similar issue also exists in the non-CA scenarios. To us, it is hard to tell whether SR transmission here includes a de-prioritized SR or not. To avoid ambiguity, we prefer to make it clear in the specification that the already de-prioritized SR is excluded from the future SR/data prioritization. Suggested TP: 2> if there is no overlapping PUCCH resource with an SR transmission , which was not already de-prioritized, where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: |
| CATT | Yes | We can use Fujitsu’s TP as a baseline. |
| Sharp | Yes | It should be fix and we think the TP proposed by Fujitsu can be a baseline. |
| ITRI | Yes | Agree with Fujitsu and Huawei |
| Intel | Yes | Agree with the TP from Fujitsu. |
| OPPO | Yes | As we illustrated in Issue #5 in R2-2004130, we think current text does not properly capture the agreement “an uplink grant is not de-prioritized by other de-prioritized SR”. According to section 5.4.1 in MAC running CR, the compared SR in prioritization procedure is described as “SR transmission”. The terminology of “SR transmission” is unclear, thus it is hard for the implementer to know whether “SR transmission” includes the de-prioritized SR or not. To make the spec more readable, we propose the following TP: When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which is not already a de-prioritized uplink grant, the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant and the SR was not already deprioritized: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant and the SR was not already deprioritized: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). |
| Nokia, NSB | Yes | We can follow the similar way as the TP agreed for de-prioritized uplink to resolve this issue: if there is no overlapping PUCCH resource with an SR transmission which was not already deprioritized and where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: |
| MediaTek | Yes | The TP can be similar to deprioritised UL data, i.e. as suggested by Fujitsu |
| Samsung | No strong view | Fujitsu’s TP is ok. But we need to define “de-prioritized SR” which was not defined in the current MAC spec nor running CR. |
| Ericsson | Yes | We understand that the agreement “An uplink grant is not de-prioritized by other de-prioritized SR.” is not captured. There is no clear definition yet in the MAC spec on what is a de-prioritized SR. In order to avoid unexpected errors to other texts, we don’t prefer adding that directly in the procedure text but prefer adding a note in the end of clause 5.4.1, such as The overlapping PUCCH duration with an SR transmission is not considered if its transmission would not be triggered if this uplink grant did not exist |
| Apple | Yes | We agree with the majority opinion above that the issue of “an uplink grant that is not de-prioritized by other de-prioritized SR or uplink grant” should be accurately reflected and captured in the spec. |
| Sequans | Yes | No strong view on the TP yet. |
| Qualcomm | No strong view. |  |

< Summary >

- All companies are ok to fix it, i.e. support or no strong view

- Fujitsu, Huawei, vivo, OPPO, Nokia proposed similar TP for normative text. The high-level principle is 1) to define a de-prioritized SR transmission and 2) exclude the de-prioritized SR in prioritization.

Ericsson proposed to have a NOTE, to avoid unexpected errors to other parts.The rapporteur tends to share Ericsson’s concern that we need to be careful on touching optimally written procedural text. However, many companies are ok with TP proposed by multiple companies and the TP is consistent with the case of de-prioritized uplink grant. The rapporteur would suggest to go with TP by multiple companies and have a careful CR review.

Proposal 4. A de-prioritized SR shall be excluded in prioritization. TP proposed by Fujitsu/Huawei/vivo/OPPO/Nokia can be a baseline.

## 2.5 Issue #5: Autonomous transmission after BWP switching

In RAN2#109bis-e meeting, RAN2 agreed to allow the autonomous transmission if the TBS remains the same, for (re-)activation of type 2 CG or reconfiguration of type 1 or type 2 CG. A potential open issue could be whether to continue the autonomous transmission after BWP switching (R2-2003225, Lenovo). It might be less complex for UE to disallow the autonomous transmission after BWP switching. Potential solutions could be, for instance, priority status (e.g. de-prioritized) of an UL grant is cleared or HARQ buffer is flushed at BWP deactivation.

Since RAN2 has not discuss about BWP switching scenario, the current UE behaviour in the running CR (R2-2004289) is that UE continues the autonomous transmission after BWP switching.

Q5) Do companies agree to disallow autonomous transmission after BWP switching?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Fujitsu | Yes | But no strong view. |
| SONY | Yes |  |
| Lenovo | Yes | We don’t have a strong view. One can argue that there is some benefit if the UE behavior for the case of BWP switching is aligned with the case of type-1 CG reactivation. On the other hand we think from UE implementation perspective it might be less complex for the UE to just disallow autonomous transmissions after BWP switching. |
| Huawei | Yes or No | In the RAN2 #109-e meeting, the following agreements were achieved: => UE autonomous transmission uses the same HARQ process and the same CG configuration. => A HARQ process cannot be shared between different CGs. For two CG type 1 configurations on two BWPs share the same HARQ process of the serving cell, we need to first make clear whether they can be viewed as the same CG type 1 configuration. If they can be regarded as the same CG type 1 configuration, then we think there is no problem to allow autonomous transmission after BWP switching. It is then preferred to not change current text. Otherwise if they shall be regarded as different CG configurations, then autonomous transmission after BWP switching shall be disallowed. |
| LG | No | We don’t see any problem to allow autonomous transmission after BWP switching. The BWP switch is different from the CG Type 2 reactivation case because the confimation MAC CE is not transmitted, and there is no harm to keep the MAC PDU in the HARQ buffer. What is the problem with the current text? |
| ZTE | Yes | In our understanding , different BWPs may have different numerology and different CG configuration across BWP may have the different PUSCH duration, according to the LCH restriction, the data in the HARQ buffer whose LCH maybe no longer suitable for the PUSCH resources of configure grant type 1 after BWP switch. Thus we think the automatic transmission after BWP switch shall not be supported. |
| vivo | Yes, but | We only need to correctly capture the previous RAN2 agreement to restrict the autonomous retransmission only within the same CG configuration, as the CG configurations for different BWPs has to be different according to the current ASN.1 structure. |
| CATT | No | We are not sure of the complexity difference with the normal continuation of data transmission across CGs in different BWPs. |
| Sharp | Yes | CG configuration is per BWP. So, the CGs on different BWP should be considered as different BWPs, allowing autonomous retransmission when BWP switching happens will not alignment with the agreement “UE autonomous transmission uses the same HARQ process and the same CG configuration”. |
| ITRI | Yes or No | If we allow autonomous transmission after BWP switching, the premise is that different CG configurations across BWPs which share the same HARQ process can be viewed as the same CG configuration. |
| Intel | Yes | Our understanding is that autonomous transmission is only for the same CG configuration, and CG configurations from different BWPs cannot be considered as same CG configuration. In our view, current TS 38.321 is clear and there is no need to change specification. |
| OPPO | Yes or No | We share the same view as Huawei. |
| Nokia, NSB | Yes | Continuation is only possible if the same CG configuration has been configured in the new BWP, and we don’t think this is always guaranteed and potentially this could bring unnecessary scheduling restriction for gNB. To make the specification simpler without adding too many conditions, it is more straightforward to disallow continuation of autonomous transmission in this case (which is likely to be corner case anyway). |
| MediaTek | Yes | Agree with Intel that CG configurations on different BWPs cannot be considered as same CG configuration. |
| Samsung | Yes or No | CG is configured per BWP. Thus, CGs configured on different BWPs shall be different CG configurations. So, cross-BWP autonomous transmission cannot occur. The only case that we may consider is autonomous Tx after BWP switching back to the original BWP, i.e. De-prioritization in BWP A ( Switching to BWP B and the HARQ process has not been used at all ( Switching back to BWP A. But we see this is a corner case, so we do not need to consider to disallow the autonomous Tx for this case. |
| Ericsson | Yes | The autonomous transmission after BWP switching should be disallowed because It is not clear how long time the BWP would be re-initialized after it was suspended. Any data stuck in the buffer would most likely be re-transmitted by upper layers. The benefits of continuation are not clear. For configured grant type 2, the grants are cleared during BWP switching and we should align the operations of two types configured grants. |
| Apple | Yes | We agree with Lenovo’s view here. |
| Sequans | Yes | Agree with Intel |
| Qualcomm | Yes |  |

< Summary >

Most companies agree that autonomous Tx cannot be continued after BWP switching. But companies have different understandings on the current behaviour.

- Huawei, OPPO point out that it is not clear whether CGs on different BWPs are viewed as the same CG configuration.

- ZTE, vivo, Sharp, Intel, MediaTek, Samsung, and Sequans see that CG configurations are per BWP. Thus, CGs on different BWPs cannot be the same configuration.

- ITRI has a different view that those are viewed as the same  CG configuration.

- Ericsson mentioned that type 2 CG on deactivated BWP is cleared and prefers to align.

As a start point, we need to discuss whether CG configurations with the same HARQ process on different BWPs are considered as the same CG configuration.

- If the answer is yes, current texts allow autonomousTx after BWP switching.

- If the answer is no, current texts do not allow.

Depending on the correct answer, we can discuss further whether to change the text or current behaviour.

Proposal 5. Discuss whether CG configurations with the same HARQ process on different BWPs are considered as the same CG configuration. After the conclusion, RAN2 will continue to discuss whether to change the current text or behaviour.