3GPP TSG-RAN WG2 Meeting #110 electronic	R2-20xxxxx

Online, June 1 – June 12 2020

Agenda item:	6.7.3

Source:	Samsung

Title:	Report of [AT110e][055][IIOT] MAC: Part 1B

Document for:	Discussion & Decision

# Introduction

This document is for the following offline discussion:

- [AT110-e][055][IIOT] MAC (Samsung)

Scope 1: Treat the email discussion summary in R2-2005645, make agreements as far as possible (difficult discussion can be brought on-line instead, for desicions). Address other relevant issues under 6.7.3.1 not overlapping with the email discussion and/or previous agreements, if any. Address also inter-UE-prioritization below.

Scope 2: Implement meeting agreements in the CR.

Part 1: Agreements (rapporteur to announce deadline)

Part 2: Agreed CRs 38321. Deadline: EOM

This document discusses remaining issues, especially, issues addressed as an outcome of Part 1A discussion, as follows:

< Part 1B Discussion includes >

Discussion 1. Whether to add a NOTE: The UE does not have to start with an “N” equal to 1, but should consider subsequent grants to occur as soon as CG configuration is received and applied.

Discussion 2.

- HARQ process can be shared between CGs on different BWPs?

- If it is shared, do we need to allow autonomous transmission on the switched BWP?

Discussion 3. How to capture Proposal 6, based on TPs (R2-2004558, R2-2004890, etc) and considering together with other issues.

# Confirmation of Part 1A Discussion

During Part 1A discussion [1], companies reached the consensus for the following proposals:

Proposal 1. UE continues to use the occasion of the suspended configured grant type 1 when the related UL BWP is activated. Proposal 2. A de-prioritized SR shall be excluded in prioritization. TP proposed by Fujitsu/Huawei/vivo/OPPO/Nokia can be a baseline. Proposal 3. For closest N determination, TP in R2-2003586 is adopted. Proposal 5. RAN2 confirms “CG configurations with the same HARQ process on different BWPs are different and separate CG configurations.” Proposal 8. A CG cancelled by Cancellation Indicator (CI) is considered as a de-prioritized uplink grant and the MAC entity autonomous transmit the MAC PDU in the subsequent CG Proposal 9. SR overlapping with uplink grant received in RAR, or addressed to temporary C-RNTI, or with MSGA transmission cannot be transmitted. Proposal 10. Prioritization between non-overlapping uplink grants is NOT supported in Rel-16. Proposal 12. TP in R2-2005124 on priority of uplink grant with no data is adopted.

Q1. If you do not accept any of proposals above, please explain the reason. (If you could accept all, you can skip Q1)

| Company | Proposal | Reason why it is not acceptable. |
| --- | --- | --- |
| Nokia | Proposal 3 | timeDomainOffset definition already considers offset with respect to reference SFN. This TP introduces text which is redundant and does not clarify anything in our opinion. |

# Part 1B Discussion

## 3.1 Closest Available N

During the previous discussion, RAN2 agreed not to add any normative text on restriction how to choose closest available Nth CG occasion. However, there is still a proposal to have a NOTE to clarify to avoid misalignment between the UE and the network. The proposed TP could be for example, (text may be improved later):

NOTE: The UE does not have to start with an “N” equal to 1, but should consider subsequent grants to occur as soon as CG configuration is received and applied.

Q2) Do companies agree to add the NOTE above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Lenovo |  | No strong view |
| LG | No | No strong view, but we don’t see a value of the NOTE. |
| Nokia | Yes | We think such clarification is needed, so that text about “Nth occasion” is not interpreted too literally, which would lead to misalignment between the network and the UE on when the CG is applied. Also, it should be noted that UE is never obliged to utilize the UL grant given with CG (e.g. when it does not have data) and such note does not introduce any additional requirement on the UE. |
| Fujitsu | No, but | We think there is limited benefit to have the initial value of “N” less than 1. However, the 2nd text “should consider subsequent grants to occur as soon as CG configuration is received and applied” seems to be an intended NW behaviour. If companies think that it is worth capturing, we can accept. |
| Ericsson |  | The proposal in the NOTE is Ericsson’s understanding on how the feature is supposed to work. No strong view on whether to add this NOTE. If, due to uncertain UE processing time for RRC configuration and HARQ retransmission, the first allocated resource is in the past, then it is straightforward that UE should ignore those resources. This is also one of the reasons why the field timeReferenceSFN has been introduced to clarify where the resource is first allocated. |
| CATT | No | We don’t think the note clarifies much and we are not sure to get the issue of misalignment between the network and the UE since the UE may anyways skip any CG. |
| Samsung | No strong view | Agree with Ericsson. UE behaviour should be the same as NOTE, if resource is not available to UE. |
| Intel | No | The agreed TP in R2-2003586 does not place restriction on UE implementation on choosing the starting value of “N” for the calculation of CG occasion. It is not clear whether the proposed note can provide additional flexibility for UE implementation. |
| ITRI |  | No strong view |
| vivo |  | No strong view |
| MediaTek | No | We do not see additional value by having such a note. |
| ZTE | No |  |
| OPPO |  | No strong view, but we wonder whether it is really needed since we don't see any restriction in MAC to require the UE always starting to use CG with N equal to 1. |
| Sequans | No strong view | We are fine with a NOTE, but would like to propose an alternative wording. There was an agreement that N is non negative. We assume N>=0 would be added along with the formula. Then having a NOTE with “start with an “N” equal to 1” is a bit strange. Alternative proposal: NOTE: Occasions corresponding to lowest N values may occur in the past at the time configuration is received (in which case they are ignored by the UE) |
| DOCOMO | No strong view |  |

## 3.2 Autonomous Transmission after BWP Switching

Since companies confirmed that CG configurations with the same HARQ process on different BWPs are different and separate CG configurations during the previous discussion, the autonomous transmission may be possible only for the case that HARQ process ID is shared between CGs on different BWPs, as in the following figure:

Figure 1. HPI sharing between different CG configurations on different BWPs

However, in RAN2#109e, RAN2 agreed that HARQ process cannot be shared between different CG.

A HARQ process cannot be shared between different CGs.

Discussion for the agreement above is mainly for the same BWP. It may not be crystal clear if the agreement is still valid for BWP switching. The rapporteur would like to check companies view on this. If it can be shared, we may need to discuss if autonomous transmission needs to be supported. Otherwise, autonomous transmission is not allowed at all.

Q3-1) Do companies agree that a HARQ process ID can be shared between different CGs on different BWPs, as in Figure 1?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Lenovo | Yes | Agreement reached in RAN2#109e was for the case of the same BWP, i.e. HARQ operation across different BWPs was not considered at that time. In our understanding the HARQ protocol operation continuous when BWP is switched, this was already clear since Rel-15 for dynamic UL grants. Therefore we think that it’s also possible to continue HARQ operation for CG(s) upon BWP switching given that TBS is same. |
| LG | Yes | Agree with Lenovo. |
| Nokia | Yes | As HARQ entity is per cell rather than per BWP, and only one BWP is active at a time, we think it is possible to share HARQ processes among CGs in different BWPs. |
| Fujitsu | Yes | Agree with Lenovo. |
| Ericsson | Yes | It is indeed not clear whether the agreement applies for the same or different BWPs. One can argue that the agreement “A HARQ process cannot be shared between different CGs” should be more precisely understood as CGs that are active. As there is one active BWP per cell at a time, network can configure overlapping HARQ process ID pools for two CGs in different BWPs. |
| CATT | Yes | It would not make sense otherwise, because the pool of HARQ processes would not be sufficient if distributed across BWPs. |
| Samsung | Yes | The previous agreement is for the same BWP. Since only one BWP can be active, the same HPI can be configured for CGs on different BWPs. |
| Intel | Yes | Our understanding is that HARQ process ID can be shared between CGs on different BWPs, otherwise the available HARQ process IDs would be limited for one BWP. |
| ITRI | Yes | Agree with Lenovo. |
| vivo | Yes |  |
| MediaTek | Yes |  |
| ZTE | Yes |  |
| OPPO | Yes | Agree with Nokia and Ericsson. |
| Sequans | Yes | Agree with Nokia |
| DOCOMO | Yes | Agree with Lenovo. |

Q3-2) Assuming that a HARQ process ID can be shared between different CGs on different BWPs, is the autonomous transmission allowed between CGs sharing the same HARQ process?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Lenovo | Yes/No | We think that it may be possible when TBS is same among the CG(s). However our preference would be to not support autonomous transmission upon BWP witching in order to reduce complexity. |
| LG | Yes | We don’t see any problem to allow autonomous transmission if the TB size matches. |
| Nokia | No | We have agreed that autonomous transmission is only allowed in the same CG configuration, and we have also confirmed that CGs in different BWPs are different CGs. With these agreements that are already made, it is natural we do not allow autonomous transmission cross different CGs and BWPs. |
| Fujitsu | Yes/No | We don’t have strong view. Retransmission for the de-prioritized PDU on the same HARQ process can be supported with present texts. On the contrary, the drawback for not allowing auto-Tx after BWP switching is that the de-prioritized PDU will be flushed and the specification effort is needed. But we are fine if companies don’t accept the autonomous transmission between CGs with the same process. |
| Ericsson | No | The question here is for configured grant type 1. During BWP switching, configured grant type 2 is cleared. To align, it should be dis-allowed. Additionally, the gain is negligible for a low priority data and the data can be retransmitted by a dynamic UL grant from gNB if needed. |
| CATT | Yes | We don't see any problem in supporting this, or any contradiction with earlier agreements, plus it is already supported in the current specification. |
| Samsung | No | We think gain of autonomous transmission is not so big. So we prefer not to allow it. If two CGs share the same HPI, the current text allows autonomous transmission even after BWP switching. Thus, if we prohibit it, the following changes are needed. 3> else if this uplink grant is a configured grant configured with autonomousTxwhich is a prioritized uplink grant; and 3> if the configured grant is configured with autonomousReTx; and 3> if the previous configured uplink grant, in the BWP, for this HARQ process was de-prioritized; and 3> if a MAC PDU had already been obtained for this HARQ process; and 3> if the uplink grant size matches with size of the obtained MAC PDU; and 3> if a transmission of the obtained MAC PDU has not been performed: 4> consider the MAC PDU has been obtained. If we allow autonomous transmission, no change is needed. |
| SONY | No | The transmission parameters may be different for different CGs, so it may not be possible to continue AutoTx. |
| Intel | No | Given that CGs on different BWPs are different CGs, we don’t think there is a need to support autonomous transmission upon BWP switching. |
| ITRI | Yes | Agree with LG and CATT. |
| vivo | No | We think this is an optimization, as we agreed to only allow autonomous retransmission within the same CG configuration. |
| MediaTek | No | This is an optimisation providing marginal gains and is unnecessary at this stage of the discussions. |
| ZTE | No |  |
| OPPO | No | We have made the agreement that the autonomous transmission is only allowed for the same HPI and the same CG configuration. We don’t think we really need to revert our conclusion for this case whose gain may be marginal. In addition, we prefer Samsung’s modification text. |
| Sequans | No | Agree with Nokia |
| DOCOMO | No | With different CG configuration in different BWPs, the gain of autonomous transmission is limited and brings extra different CG parameters checking complexity. |

## 3.3 TP on Second PDU Generation when PHY cannot transmit it.

Regarding the RAN1 agreement that RAN2 should change MAC specification (R2-2006088, R1-2004899),

Agreement RAN2 changes MAC specification to accommodate current PHY behaviour. With this option, MAC will avoid providing second MAC PDU with the same L1 priority to PHY, meaning that PHY would transmit the packet with lower LCH priority data.

RAN2 made the following agreements during the online session in RAN2#110-e:

(When MAC determines to generate a PDU) MAC entity shall not generate a PDU that cannot be transmitted due to collision with transmission (at least due to equal L1 priority).

In this week, RAN1 sent an LS (R2-2006104, R1-2005078) which may be related with the agreement.

Agreement For collision handling between CG and CG with different priorities, If MAC delivers two MAC PDUs, it is up to UE implementation to make sure that the low priority CG PUSCH transmission can be cancelled before the start of the high priority CG PUSCH. Conclusion There is no consensus in RAN1 for the support of the following: high priority DG cancel the transmission of low priority CG in the physical layer high priority CG cancel the transmission of low priority DG in the physical layer No further discussion for Rel.16.

The latest RAN1 agreement mentions that cancellation or pre-emption of ongoing CG is up to UE implementation for different L1 priorities, i.e. later CG has higher L1 priority.

Thus, it would be good to discuss together in TP discussion. Regarding the TP, there are several candidates which are all working. Note that some text has been edited and modified by the rapporteur, to take latest RAN2 agreement into account.

Option 1 (R2-2005647)

When the MAC entity is configured, with lch-basedPrioritization, for each uplink grant which can be transmitted by lower layers the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). NOTE 6: If there is overlapping PUSCH duration of at least two configured uplink grants whose priorities are equal, the prioritized uplink grant is determined by UE implementation.

Option 2 (R2-2004959)

When the MAC entity is configured, with lch-basedPrioritization, the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). NOTE 6: If there is overlapping PUSCH duration of at least two configured uplink grants whose priorities are equal, the prioritized uplink grant is determined by UE implementation. NOTE7: An uplink grant, which cannot be transmitted due to overlapping with another ongoing transmission, is considered as a de-prioritized uplink grant.

Option 3 (R2-2004922, R2-2004599, R2-2004890)

When the MAC entity is configured, with lch-basedPrioritization, the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a delivered MAC PDU which refrains the transmission of the uplink grant in PHY; and 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of a delivered MAC PDU which refrains the transmission of the uplink grant in PHY; and 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). NOTE 6: If there is overlapping PUSCH duration of at least two configured uplink grants whose priorities are equal, the prioritized uplink grant is determined by UE implementation.

Option 4 (R2-2005337)

priority among priorities of the logical channels with data available that are multiplexed or can be multiplexed in the MAC PDU, according to the mapping restrictions as described in clause 5.4.3.1.2. The priority of an uplink grant for which no data for logical channels is multiplexed or can be multiplexed in the MAC PDU is lower than the priority of an uplink grant for which data for any logical channels is multiplexed or can be multiplexed in the MAC PDU. When the MAC entity is configured with lch-basedPrioritization, and there is overlapping PUSCH duration of at least two configured uplink grants whose priorities indicated by phy-PriorityIndex are equal or whose phy-PriorityIndex are not configured, the overlapped MAC PDU(s) is not generated if one MAC PDU has already been generated. When the MAC entity is configured with lch-basedPrioritization, and there is overlapping PUSCH duration of one dynamic grant and at least one configured uplink grant whose priorities indicated by phy-PriorityIndex are equal or whose phy-PriorityIndex are not configured, the MAC PDU associated to dynamic grant is generated. When the MAC entity is configured with lch-basedPrioritization, and there is overlapping PUCCH resource for the SR transmission and any UL-SCH resource(s) whose priorities indicated by phy-PriorityIndex are equal or whose phy-PriorityIndex are not configured, the overlapping SR is not instructed the physical layer to signal. When the MAC entity is configured, with lch-basedPrioritization, the MAC entity shall: 1> if this uplink grant is addressed to CS-RNTI with NDI = 1 or C-RNTI: 2> if there is no overlapping PUSCH duration of a configured uplink grant which was not already de-prioritized, in the same BWP whose priority is higher than the priority of the uplink grant; and …

Q4) Companies are invited provide their preference:

- Option 1

- Option 2

- Option 3

- Option 4

| Company | Preference | Comments (incl. wording suggestion or not acceptable option) |
| --- | --- | --- |
| Lenovo | Option 1 |  |
| LG | Option 1 | We think the option 1 is the most future proof change. |
| Nokia | 3 | While we think Adding a Note is also okay, the wording of Option 2 is a bit too specific as it only considers “on-going transmission”, but in fact it could be a delivered PDU whose PUSCH transmission is not started yet, or other cases agreed in RAN1’s latest agreements. On the other hand, Option 1 is a bit vague. In the context of intra-UE prioritization, the only reason why a MAC PDU cannot be transmitted by PHY is mainly due to another overlapping transmission (e.g. insufficient time to cancel), so we think it should be clarified. Option 4 seems to be too much details. Thus we think Option 3 is a better compromise. |
| Fujitsu |  | Option 1,2 and 4 seem to violate the current LCH-based prioritization in MAC. Option 3 seems feasible, but we think the specific scenario should be clear to address the issue. And we think the issue has to be CG related, i.e. the later PDU is from CG and it is deprioritized by PHY. Other cases, e.g. the PDU from DG is prioritized by MAC but is not transmitted by PHY, may not be resolved by MAC. We suggest a condition to determine if there is any overlapping grant with the same L1 priority which has obtained MAC PDU should be added to the prioritization related to CG. In this way, MAC can do prioritization for CG considering L1 priority besides present LCH-based rule. Corresponding TP is proposed as following: -------------------------------------------------------------------------------------- 1> else if this uplink grant is a configured uplink grant: 2> if there is no overlapping PUSCH duration of another configured uplink grant which was not already de-prioritized, in the same BWP, whose priority is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the same BWP, whose priority is higher than or equal to the priority of the uplink grant; and 2> if there is no overlapping PUCCH resource with an SR transmission where the priority of the logical channel that triggered the SR is higher than the priority of the uplink grant; and 2> if there is no overlapping PUSCH duration of an uplink grant addressed to CS-RNTI with NDI = 1 or C-RNTI which was not already de-prioritized, in the BWP, whose physical priority index is equal to that of the uplink grant and MAC PDU has been obtained; and 2> if there is no overlapping PUSCH duration of another configuration uplink grant which was not already de-prioritized, in the same BWP, whose physical priority index is equal to that of the uplink grant and MAC PDU has been obtained: 3> consider this uplink grant as a prioritized uplink grant; 3> consider the other overlapping uplink grant(s), if any, as a de-prioritized uplink grant(s). |
| Ericsson | Option 1 | If all options are essentially the same, Ericsson prefers the simplest one. |
| CATT | Option 3 | We share the same view as Nokia. The TP would need some polishing though: 2> if there is no overlapping PUSCH duration of a delivered MAC PDU which refrains the transmission by lower layers of the PUSCH associated with this uplink grant; and |
| Samsung | Option 1 | Under the current UE behaviour, there is no actual difference between options. So, we prefer the simplest change. We also agree with LG that it is more future proof. |
| SONY | Option 1 | We are also OK Option 2. |
| Intel | Option 1 | Option 1 is the simplest. |
| ITRI | Option 1 |  |
| vivo | Option 1 |  |
| MediaTek | Option 1 | This is the simplest option, and is best aligned with our agreement |
| ZTE | Option 1 |  |
| OPPO | Option 1 or 4 | If all options can work well, we prefer the simplest one, or the detailed one. |
| Sequans | Option 3 | Agree with CATT |
| DOCOMO | Option3 | Agree with Nokia. Option3 looks more clear. |

## 3.4 Capturing Agreement on Resource Selection in Autonomous Transmission

During the online discussion, we have the following way forward:

A NOTE for RAN2#109-e agreement on next CG selection for autonomous retransmission to be added. Current proposal is not agreeable, possibly a simplified version can be considered, TBD offline (if no agreement in the end we just skip the Note for now).

Since companies’ main concern was too much detail on timeline restriction, the rapporteur would suggest the following simplified note:

NOTE: It is up to the UE implementation to determine whether the very next configured grant configured with autonomousTx can be used for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant.

Q5) Do companies agree to add the following simplified NOTE?

NOTE: It is up to the UE implementation to determine whether the very next configured grant configured with autonomousTx can be used for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant.

| Company | Yes/No | Comments (incl. wording suggestion) |
| --- | --- | --- |
| Lenovo |  | Actually we think that the normative text should be clear. However current normative text mandates the UE to check whether the immediate previous configured uplink grant was de-prioritized, which contradicts the agreed allowed UE behaviour. Therefore we rather prefer to have a small fix the normative/procedural text such as the following: 3> if the previous configured uplink grant for this HARQ process, for which the last transmission attempt of the MAC PDU was made, was de-prioritized; and |
| LG | No | First, we don’t see a value of the NOTE. The UE anyway has to consider the processing time, and if there is not enough processing time, it is obvious that the UE cannot use the very next CG. Thus, our preference is not to capture anything in the specification. However, if something really needs to be clarified, we think NOTE should be used, but the text needs to be updated. e.g. as follows. NOTE: It is up to the UE implementation to determine a next configured grant configured with autonomousTx for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant. |
| Nokia |  | We suggest to change the proposed text a bit: NOTE: It is up to the UE implementation to determine whether the very next select a subsequent configured grant configured with autonomousTx can be used for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant. |
| Fujitsu | Yes/No | MAC spec should be transparent to timeline restriction. We are not sure current NOTE can address this issue. The correction suggested by Lenovo is fine. And the suggestion from Nokia to state “subsequent” instead of “next” looks good since it provides the UE with broad selection of future CG resources. |
| Ericsson | No | Per the LS (R2-2006104, R1-2005078), there is no need for this clarification. Agreement For collision handling between CG and CG with different priorities, If MAC delivers two MAC PDUs, it is up to UE implementation to make sure that the low priority CG PUSCH transmission can be cancelled before the start of the high priority CG PUSCH. Conclusion There is no consensus in RAN1 for the support of the following: high priority DG cancel the transmission of low priority CG in the physical layer high priority CG cancel the transmission of low priority DG in the physical layer No further discussion for Rel.16. Essentially, autonomous transmission can happen only in the CG versus CG case. In this case, UE is well aware of the CG resources in advance and there is no timing issue at all. |
| CATT | Yes | The RAN2 agreement is to capture a note, which we now focus on. We are not sure of Nokia’s variant as it could leave the impression that the UE is allowed, by implementation, to not select any subsequent CG. We have sympathy for LG’s variant with possible further improvement as follows: NOTE: It is up to the UE implementation to determine the closest available next configured grant configured with autonomousTx for the transmission of the MAC PDU of the same HARQ process of the previously de-prioritized configured uplink grant. |
| Samsung | Yes | We are fine to improve the wording. Regarding Ericsson’s view, even in CG-CG collision, CG occasion could be partially overlapping, i.e. not fully overlap. In this case, the timing issue may happen. |
| SONY | Yes | We are not sure Nokia’s wording captures the intention of the note. We prefer CATT’s improved note. |
| Intel | Yes | We’re OK with CATT’s improved text. |
| ITRI |  | Agree with Fujitsu that MAC spec should be transparent to the timeline restriction, and we are fine with the suggestion by Nokia. |
| vivo | Yes but | We think the LG’s text proposal is more proper, as the UE may not be able to use several CG(s) (not just “the very next configured grant”) due to the processing restriction. |
| MediaTek | Yes, but | We prefer Nokia’s wording. |
| ZTE | No | We also think UE anyway has to assess whether the autoretransmission can be performed or not. This note seems no value at all. In addition, There is something so strange, if UE have no time to process the autoretransmission which means UE have no time to generate new MAC PDUs continuously for a series of configured grant as well, I have no idea why NW schedule such stupid CG for UE? |
| OPPO | Yes | We prefer Nokia’s text. |
| Sequans | Yes but | We prefer CATT wording. |
| DOCOMO | Yes | We prefer CATT’s revision. |

# Conclusion

# References

[1] R2-2006046 Report of [AT110e][055][IIOT] MAC: Part 1A, Samsung

# Comments

Based on agreement: Remove the current condition “for each uplink grant which is not already a de-prioritized uplink grant”

Based on agreement: Remove the current condition “for each uplink grant which is not already a de-prioritized uplink grant”

Based on agreement: Remove the current condition “for each uplink grant which is not already a de-prioritized uplink grant”

Based on agreement: Remove the current condition “for each uplink grant which is not already a de-prioritized uplink grant”