3GPP TSG-RAN WG2 Meeting #110	R2-20XXXXX

# Electronic, 1 June – 12 June 2020

Agenda item:	6.0.1

Source:	ZTE Corporation, Sanechips

Title:	Offline-076: [TEI16] R16 corrections to R15 (ZTE)

Document for:	Discussion & Decision

# Introduction

This is a summary of the following offline discussion on uac-AccessCategory1-SelectionAssistanceInfo configuration:

[AT110-e][076][TEI16] R16 corrections to R15 (ZTE)

Scope: Treat R2-2004925 – 4929

Wanted Outcome: determine agreeable parts. For agreeable parts: agreed CRs (don’t need to be merged)

Deadline: EOM

Specially, the rapporteur would like to have two phase discussion:

Phase 1: Down select from the potential solutions Deadline: June 10, 0700 UTC.

Phase 2: For the selected solution, continuation to agree CRs. Deadline: EOM

This document covers the following contributions submitted to RAN2#110-e meeting mainly to address Z118:

R2-2004925	[Z118] Clarification on providing network specific uac-AccessCategory1-SelectionAssistanceInfo	ZTE Corporation, Sanechips, CMCC, Nokia	discussion	Rel-16	NR_newRAT-Core	R2-2002764

R2-2004926	[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 1	ZTE Corporation, Sanechips, Nokia	CR	Rel-16	38.331	16.0.0	1637	-	F	NR_newRAT-Core

R2-2004927	[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 2	ZTE Corporation, Sanechips, Nokia	CR	Rel-16	38.331	16.0.0	1638	-	F	NR_newRAT-Core

R2-2004928	[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 3	ZTE Corporation, Sanechips, Nokia	CR	Rel-16	38.331	16.0.0	1639	-	F	NR_newRAT-Core

R2-2004929	[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 4	ZTE Corporation, Sanechips, Nokia	CR	Rel-16	38.331	16.0.0	1520	2	F	NR_newRAT-Core	R2-2002765

# Discussion: Phase 1

## 2.1 Background and problem statement

In NR R15, the uac-AccessCategory1-SelectionAssistanceInfo can be configured to assist UE to decide whether Access Category 1 applies or not.

As shown below, network can either configure a common UAC-AccessCategory1-SelectionAssistanceInfo applicable to all the PLMNs sharing the same cell via plmnCommon or configure it for each PLMN via individualPLMNList if different PLMNs would like to configure different values.

uac-BarringInfo                     SEQUENCE {

uac-BarringForCommon         		UAC-BarringPerCatList                      	OPTIONAL,   -- Need S

uac-BarringPerPLMN-List      		UAC-BarringPerPLMN-List                    	OPTIONAL,   -- Need S

uac-BarringInfoSetList        		UAC-BarringInfoSetList,

uac-AccessCategory1-SelectionAssistanceInfo CHOICE {

plmnCommon                           	UAC-AccessCategory1-SelectionAssistanceInfo,

individualPLMNList                   SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo

}  																		OPTIONAL    -- Need S

}      																		OPTIONAL,   -- Need R

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

However, among all the PLMNs sharing the same cell, some PLMNs may want to configure access barring for delay tolerant service while others do not.

With the current ASN.1 structure, if one PLMN wants to configure access barring for delay tolerant services, other PLMNs sharing the same cell have to configure a “a”, “b” or “c” either via plmnCommon or individualPLMNList even though they do not want to do so because we did not make each entry in the individualPLMNList OPTIONAL.

As a result, UE configured with delay tolerant service may select access category 1 and perform barring check based on the factor and timer associated with access category 1 upon receiving such configuration although it should have selected another access category and perform access barring check accordingly.

Q1) Base on the understanding of the current uac-AccessCategory1-SelectionAssistanceInfo in SIB1, do companies agree with the following observation?

Observation: Among all the PLMNs sharing the same cell, the current ASN.1 for configuring uac-AccessCategory1-SelectionAssistanceInfo does not allow some PLMNs to configure such assistance information while others not to configure it.

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Nokia, Nokia Shanghai Bell | Yes | We confirm the understanding. The finding is correct: Network has no configuration option to set different values for AccessCategory1-SelectionAssistanceInfo for PLMNs sharing the same cell. Which forces the network to set delay tolerant services for all PLMNs in the same way, even though some of them may wish not to have delay services configured. This isn’t intended design. |
| ZTE | Yes |  |
| MediaTek | Yes |  |
| Samsung | No | We assume there is no problem. The field uac-AccessCategory1-SelectionAssistanceInfo is used to limit the scope to which access category 1 is applied. The field is mandatory if the access category 1 is configured. It’s same as in LTE. In current RRC specification, all access categories including the access category 1 can be configured per PLMN by using uas-BarringPerPLMN-List. If one PLMN doesn't want to configure the access category 1, the configuration corresponding to the access category 1 is not provided via SIB1. If configured, uac-AccessCategory1-SelectionAssistanceInfo shall be also configured. |
| Huawei, HiSilicon | No | We think the scenario described by the proponents is true. However we don’t see extension of the signalling in Rel-16 helps as the legacy UEs are not addressed. It should not be a problem really for NW or UE that all PLMNs need to provide a value in the list. In this case any value can be selected - because if there is no barring parameter provided for a PLMN for access category 1, it is clear that it doesn't apply. So we don’t see much need to change the ASN.1. |

To allow a certain PLMN not to configure the uac-AccessCategory1-SelectionAssistanceInfo field, some potential solutions are listed in chapter 2.2 for companies to down select.

## 2.2 Potential solutions

### Option 1: Introduce UAC-AccessCategory1-SelectionAssistanceInfo-v16xy with value {a, b, c, null}.

If a PLMN does not want to configure access barring for delay tolerant service, the corresponding UAC-AccessCategory1-SelectionAssistanceInfo-v16xy can be set to “null”.

-- ASN1START

-- TAG-SIB1-START

SIB1 ::=        SEQUENCE {

Partly omitted

uac-BarringInfo                     SEQUENCE {

uac-BarringForCommon         		UAC-BarringPerCatList                      	OPTIONAL,   -- Need S

uac-BarringPerPLMN-List      		UAC-BarringPerPLMN-List                    	OPTIONAL,   -- Need S

uac-BarringInfoSetList        		UAC-BarringInfoSetList,

uac-AccessCategory1-SelectionAssistanceInfo CHOICE {

plmnCommon                           	UAC-AccessCategory1-SelectionAssistanceInfo,

individualPLMNList                   SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo

}  																		OPTIONAL    -- Need S

}      																		OPTIONAL,   -- Need R

useFullResumeID                     	ENUMERATED{true}                             	OPTIONAL,   -- Need R

lateNonCriticalExtension          	OCTET STRING (CONTAINING SIB1-v16xy-IEs) 	OPTIONAL,

nonCriticalExtension               SEQUENCE {}                                		OPTIONAL

}

SIB1-v16xy-IEs ::=               SEQUENCE {

uac-BarringInfo-v16xy           SEQUENCE {

individualPLMNList-v16xy 			SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo-v16xy

}  																		OPTIONAL    -- Cond individualPLMNList

nonCriticalExtension             SEQUENCE {}                                          OPTIONAL

}

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

UAC-AccessCategory1-SelectionAssistanceInfo-v16xy ::=    ENUMERATED {a, b, c, null}

-- TAG-SIB1-STOP

-- ASN1STOP

### Option 2: Introduce UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy with value “null”.

If the newly introduced UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy field is present, the UE should ignore the legacy value provided by UAC-AccessCategory1-SelectionAssistanceInfo and consider the access barring for delay tolerant service is not configured.

-- ASN1START

-- TAG-SIB1-START

SIB1 ::=        SEQUENCE {

Partly omitted

uac-BarringInfo                     SEQUENCE {

uac-BarringForCommon         		UAC-BarringPerCatList                      	OPTIONAL,   -- Need S

uac-BarringPerPLMN-List      		UAC-BarringPerPLMN-List                    	OPTIONAL,   -- Need S

uac-BarringInfoSetList        		UAC-BarringInfoSetList,

uac-AccessCategory1-SelectionAssistanceInfo CHOICE {

plmnCommon                           	UAC-AccessCategory1-SelectionAssistanceInfo,

individualPLMNList                   SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo

}  																		OPTIONAL    -- Need S

}      																		OPTIONAL,   -- Need R

useFullResumeID                     		ENUMERATED{true}                             OPTIONAL,   -- Need R

lateNonCriticalExtension          	OCTET STRING (CONTAINING SIB1-v16xy-IEs) 	OPTIONAL,

nonCriticalExtension               SEQUENCE {}                                		OPTIONAL

}

SIB1-v16xy-IEs ::=               SEQUENCE {

uac-BarringInfo-v16xy           		SEQUENCE {

individualPLMNList-v16xy            SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy

}  											OPTIONAL    -- Cond individualPLMNList

nonCriticalExtension             SEQUENCE {}                                          OPTIONAL

}

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy ::=          SEQUENCE {

uac-AccessCategory1-SelectionAssistanceInfoExt-v16xy					ENUMERATED {null}  					OPTIONAL,   -- Need S

}

-- TAG-SIB1-STOP

-- ASN1STOP

### Option 3: Introduce individualPLMNList-v16xy in which a list of network index and the associated UAC-AccessCategory1-SelectionAssistanceInfo are included.

-- ASN1START

-- TAG-SIB1-START

SIB1 ::=        SEQUENCE {

Partly omitted

uac-BarringInfo                     SEQUENCE {

uac-BarringForCommon         		UAC-BarringPerCatList                      	OPTIONAL,   -- Need S

uac-BarringPerPLMN-List      		UAC-BarringPerPLMN-List                    	OPTIONAL,   -- Need S

uac-BarringInfoSetList        		UAC-BarringInfoSetList,

uac-AccessCategory1-SelectionAssistanceInfo CHOICE {

plmnCommon                           	UAC-AccessCategory1-SelectionAssistanceInfo,

individualPLMNList                   SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo

}  																		OPTIONAL    -- Need S

}      																		OPTIONAL,   -- Need R

useFullResumeID                     		ENUMERATED{true}                             OPTIONAL,   -- Need R

lateNonCriticalExtension          	OCTET STRING (CONTAINING SIB1-v16xy-IEs) 	OPTIONAL,

nonCriticalExtension               SEQUENCE {}                                		OPTIONAL

}

SIB1-v16xy-IEs ::=               SEQUENCE {

uac-BarringInfo-v16xy           		SEQUENCE {

individualPLMNList-v16xy            SEQUENCE (SIZE (1..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo-v16xy

}  											OPTIONAL

nonCriticalExtension             SEQUENCE {}                                          OPTIONAL

}

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

UAC-AccessCategory1-SelectionAssistanceInfo-v16xy ::=          SEQUENCE {

plmn-IdentityIndex					INTEGER (1..maxPLMN),

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

}

-- TAG-SIB1-STOP

-- ASN1STOP

### Option 4: Introduce uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap-r16 to indicate whether the value (e.g. a, b or c) configured via plmnCommon or individualPLMN for each PLMN is valid or not.

If this bitmap is present, the UE should ignore the legacy value configured via plmnCommon or individualPLMN with corresponding bit set to 0 (i.e. consider the access barring for delay tolerant service is not configured for the PLMN associated to the bit).

-- ASN1START

-- TAG-SIB1-START

SIB1 ::=        SEQUENCE {

Partly omitted

uac-BarringInfo                     SEQUENCE {

uac-BarringForCommon         		UAC-BarringPerCatList                      	OPTIONAL,   -- Need S

uac-BarringPerPLMN-List      		UAC-BarringPerPLMN-List                    	OPTIONAL,   -- Need S

uac-BarringInfoSetList        		UAC-BarringInfoSetList,

uac-AccessCategory1-SelectionAssistanceInfo CHOICE {

plmnCommon                           	UAC-AccessCategory1-SelectionAssistanceInfo,

individualPLMNList                   SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo

}  																		OPTIONAL    -- Need S

}      																		OPTIONAL,   -- Need R

useFullResumeID                     		ENUMERATED{true}                             OPTIONAL,   -- Need R

lateNonCriticalExtension          	OCTET STRING (CONTAINING SIB1-v16xy-IEs) 	OPTIONAL,

nonCriticalExtension               SEQUENCE {}

}

SIB1-v16xy-IEs ::=               SEQUENCE {

uac-BarringInfo-v16xy           		SEQUENCE {

uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap-r16 		BIT STRING (SIZE (maxPLMN))

}  																			OPTIONAL   -- Need S

nonCriticalExtension             SEQUENCE {}                                          OPTIONAL

}

UAC-AccessCategory1-SelectionAssistanceInfo ::=    ENUMERATED {a, b, c}

-- TAG-SIB1-STOP

-- ASN1STOP

For example, 6 PLMNs share the same cell and three of them would like to configure access barring for delay tolerant service while the others do not.

Expected Setting 1:

| PLMN# | 0 | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| uac-AccessCategory1-SelectionAssistanceInfo | a | / | / | / | a | a |

Possible configuration:

plmnCommon = a

uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap: 100011

Expected Setting 2:

| PLMN# | 0 | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- | --- |
| uac-AccessCategory1-SelectionAssistanceInfo | b | / | / | / | a | c |

Possible configuration:

individualPLMNList = bbbbac

uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap: 100011

Q2) To allow a certain PLMN not to configure the uac-AccessCategory1-SelectionAssistanceInfo field, which option do companies prefer?

- Option 1: Introduce UAC-AccessCategory1-SelectionAssistanceInfo-v16xy with value {a, b, c, null} [1].

- Option 2: Introduce UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy with value “null”[2].

- Option 3: Introduce individualPLMNList-v16xy in which a list of network index and the associated UAC-AccessCategory1-SelectionAssistanceInfo are included [3].

- Option 4: Introduce uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap-r16 to indicate whether the value (e.g. a, b or c) configured via plmnCommon or individualPLMN for each PLMN is valid or not [4].

| Company | Option 1/2/3/4 or any other options | Comments (if any) |
| --- | --- | --- |
| Nokia, Nokia Shanghai Bell | Option 1 or Option 3 | We are open to any solution that resolves the problem with configuration. However Option 1 or Option 3 seems straightforward/clean and allow flexible configuration. |
| ZTE | All | All the options are acceptable to us. |
| MediaTek | See comments | We do not understand why the change should be done in lateNonCriticalExtension. Couldn’t we just add the new define together with other R16 new IEs? We agree with Nokia that option 1 and option 3 are more straightforward. However, we would like to confirm how NW signal the new IE. In my thinking, the NW will not use R15 individualPLMNList and R16 individualPLMNList-v16xy at the same time. The R16 individualPLMNList-v16xy is a replacement of R15 configuration. There is no need to include the field uac-AccessCategory1-SelectionAssistanceInfo if uac-BarringInfo-v16xy is included. Is that correct understanding? R15 field uac-AccessCategory1-SelectionAssistanceInfo CHOICE { plmnCommon UAC-AccessCategory1-SelectionAssistanceInfo, individualPLMNList SEQUENCE (SIZE (2..maxPLMN)) OF UAC-AccessCategory1-SelectionAssistanceInfo } OPTIONAL -- Need S R16 fields uac-BarringInfo-v16xy SEQUENCE { individualPLMNList-v16xy TBD } OPTIONAL, -- Need R |

# Conclusion: Phase 1

Based on the above, RAN2 is request to agree the following proposals:

TBD

# Reference

- R2-2004926_38.331_(REL_16)_CR1637_[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 1

- R2-2004927_38.331_(REL_16)_CR1638_[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 2

- R2-2004928_38.331_(REL_16)_CR1639_[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 3

- R2-2004929_38.331_(REL_16)_CR1520_[Z118] CR on providing network specific uac-AccessCategory1-SelectionAssistanceInfo-Option 4