3GPP TSG-RAN WG2 Meeting#110-e	Draft_R2-2005929

Online, 1st -12th Jun. 2020

Agenda Item:	4.1.1

Source:	Huawei

Title:	Report of [AT110-e][309][NBIOT] R15 Clarification on PHR report for power class 14dBm UE (Huawei)

Document for:	Discussion and Decision

# Introduction

This document is for the following offline discussion on PHR report in NB-IoT:

[AT110-e][309][NBIOT] R15 Clarification on PHR report for power class 14dBm UE (Huawei)

Status: Not Started

Scope: R2-2005026, R2-2005027

Intended outcome: Report in R2-2005929, CRs TBD

Deadline: June 5 1000 UTC

# Discussion

Companies are invited to provide comments on the following CRs:

R2-2005026	Clarification on PHR report for power class 14dBm UE	Huawei, HiSilicon	CR	Rel-15	36.321	15.8.0	1478	-	F	NB_IOTenh2-Core

R2-2005027	Clarification on PHR report for power class 14dBm UE	Huawei, HiSilicon	CR	Rel-16	36.321	16.0.0	1479	-	A	NB_IOTenh2-Core

| Company name | Comments |
| --- | --- |
| Qualcomm | Agree with the intent and general with the proposed change. But because for both cases the sentence ends in “…using the DPR MAC control element “, this can be interpreted as using the same DPR MAC CE used for both the extended and non-extended case. Therefore, we think the in the else case following is better: “- report extended power headroom level using the DPR MAC control element for Extended Power Headroom level reporting.” |

# Summary

TBD

# Conclusion

TBD

# References

R2-2005026, Clarification on PHR report for power class 14dBm UE, Huawei, HiSilicon

R2-2005027, Clarification on PHR report for power class 14dBm UE, Huawei, HiSilicon