3GPP TSG-RAN WG2 Meeting#110-e	Draft_R2-2005929

Online, 1st -12th Jun. 2020

Agenda Item:	4.1.1

Source:	Huawei

Title:	Report of [AT110-e][309][NBIOT] R15 Clarification on PHR report for power class 14dBm UE (Huawei)

Document for:	Discussion and Decision

# Introduction

This document is for the following offline discussion on PHR report in NB-IoT:

[AT110-e][309][NBIOT] R15 Clarification on PHR report for power class 14dBm UE (Huawei)

Status: Not Started

Scope: R2-2005026, R2-2005027

Intended outcome: Report in R2-2005929, CRs TBD

Deadline: June 5 1000 UTC

# Discussion

Companies are invited to provide comments on the following CRs:

R2-2005026	Clarification on PHR report for power class 14dBm UE	Huawei, HiSilicon	CR	Rel-15	36.321	15.8.0	1478	-	F	NB_IOTenh2-Core

R2-2005027	Clarification on PHR report for power class 14dBm UE	Huawei, HiSilicon	CR	Rel-16	36.321	16.0.0	1479	-	A	NB_IOTenh2-Core

| Company name | Comments |
| --- | --- |
| Qualcomm | Agree with the intent and general with the proposed change. But because for both cases the sentence ends in “…using the DPR MAC control element “, this can be interpreted as using the same DPR MAC CE used for both the extended and non-extended case. Therefore, we think the in the else case following is better: “- report extended power headroom level using the DPR MAC control element for Extended Power Headroom level reporting.” |
| Ericsson | We agree with the intention and we are fine with the suggestion above from Qualcomm. The reporting of the extended values depends on the enhanced coverage level, i.e., only when CE level 0 is selected. Please see the tables below from 36.133: Table 9.1.23.4-1A: Power headroom report mapping for UE category NB1 for UE PC6 and supporting enhanced PHR [31] when the enhanced coverage level 0 is selected during random access procedure [17] for UE PC6 Reported value Measured quantity value (dB) POWER_HEADROOM_0 [-54]  PH  [-45] POWER_HEADROOM_1 [-45]  PH  [-41] POWER_HEADROOM_2 [-41]  PH  [-37] POWER_HEADROOM_3 [-37]  PH  [-33] POWER_HEADROOM_4 [-33]  PH  [-29] POWER_HEADROOM_5 [-29]  PH  [-25] POWER_HEADROOM_6 [-25]  PH  [-21] POWER_HEADROOM_7 [-21]  PH  [-17] POWER_HEADROOM_8 [-17]  PH  [-13] POWER_HEADROOM_9 [-13]  PH  [-9] POWER_HEADROOM_10 [-9]  PH  [-5] POWER_HEADROOM_11 [-5]  PH  [-1] POWER_HEADROOM_12 [-1]  PH  [3] POWER_HEADROOM_13 [3]  PH  [7] POWER_HEADROOM_14 [7]  PH  [11] POWER_HEADROOM_15 PH ≥ [11] Table 9.1.23.4-2: Power headroom report mapping for UE category NB1 when the enhanced coverage level other than 0 is selected during random access procedure [17] for UE PC6 Reported value Measured quantity value (dB) POWER_HEADROOM_0 [-54]  PH  [-20] POWER_HEADROOM_1 [-20]  PH  [-10] POWER_HEADROOM_2 [-10]  PH  [0] POWER_HEADROOM_3 PH ≥ [0] |
| ZTE | We also agree with the intention and fine with QC’s suggestion. One typo in both CRs: in section "Other specs affected:", the “Other core specifications” should not be marked “Y”? |

Summary:

3 companies replied and they all agree with the CR with adding “for Extended Power Headroom level reporting” for extended PHR reporting.

1 companies indicates that “Other core specifications” in the coverpage should be “N”

Proposal 1: Update the CRs to add“for Extended Power Headroom level reporting” for extended PHR reporting and change “Other core specifications” to “N”.

# Conclusion

Proposal 1: Update the CRs to add“for Extended Power Headroom level reporting” for extended PHR reporting and change “Other core specifications” to “N”.

# References

R2-2005026, Clarification on PHR report for power class 14dBm UE, Huawei, HiSilicon

R2-2005027, Clarification on PHR report for power class 14dBm UE, Huawei, HiSilicon