3GPP TSG-RAN WG2 #110-e	R2-2005938

Online, June 1st – June 12th, 2020

Agenda item:	7.2.4

Source: 	Sequans Communications (email rapporteur)

Title: 	Report of [AT110-e][315][NBIOT] CSS overlapping case for UE specific DRX (Sequans)

Document for:	Discussion and Decision

# Introduction

During RAN2#110-e, CSS overlapping case for UE specific DRX was discussed based on [3]. The following was agreed:

Try to work offline on an update/variant of B2 to find a way acceptable to all, and if not possible then fallback to C1.

Hence it was agreed to have the following email discussion:

[AT110-e][315][NBIOT] CSS overlapping case for UE specific DRX	(Sequans)

Status:

Scope: Try to work offline on an update/variant of B2 to find a way acceptable to all, and if not possible then fallback to C1.

Intended outcome: Report in R2-2005938

Deadline: Friday 1000 UTC

# Discussion

The discussion input from [3] with current proposal details was copy-pasted in Annex for convenience.

We summarize as follows: we consider an example cell where deep coverage is supported, e.g. paging CSS Rmax=512 (maximum is 2048). With short UE specific DRX cycle T=320ms, there is constant CSS overlap.

Figure 1 - Constant paging CSS overlap

From 36.213, in such case, “the UE is not required to monitor NPDCCH candidates of an NPDCCH search space” (as discussed in [1]), i.e. UE might not monitor paging at all.

C1 prevents this by NW configuration, i.e. above configuration would not be possible. For instance, the NW might deactivate UE specific DRX support in the cell.

B1 adds requirement/guideline for the UE to still monitor CSS candidates if not overlapping (e.g. the red CSS candidate above) so that UEs in good enough coverage would still behave properly. In current B1 wording, it is assumed that this could be handled at RAN2 level (RAN1 specification just says there is no requirement in that case, it does not say the UE shall not monitor those candidates). With B1, above scenario would work for UEs that need up to 256 repetitions.

B2 comes on top of B1, to handle UEs that would need more repetitions than available between POs. Such UE would “switch to next DRX cycle” by skipping POs. E.g. if 512 repetitions are needed, UE would skip every second PO which gives an “effective DRX cycle” of 640ms (note: “skipping PO” without changing DRX cycle T=320ms is mainly to not impact PF/paging carrier calculation which depends on T in 36.304).

Q1: Please detail alternative proposal(s) (including example CM note and/or example specification update)

| Company | Proposal |
| --- | --- |

Q2: Please indicate your views on above proposal(s), if any:

| Company | Proposal(s) / View(s) |
| --- | --- |

# Summary and Conclusion

…

# References

- R2-2004052, “Report of [AT109bis-e][315][NBIOT] UE specific DRX – FFSs”, Huawei

- R1-164404, “On NPDCCH Search Space”, Qualcomm Incorporated

- R2-2006005, “Report of [Post109bis-e][944][NBIOT] CSS overlapping case for UE specific DRX”, Sequans Communication

# Annex – Discussion input from [3]

We consider the use case where the UE would have a UE specific DRX (accepted following NAS negotiation) leading to constant overlapping of paging CSS in one cell, i.e. where “Paging Rmax > number of available subframes for NPDCCH paging repetitions between POs”.

As discussed in [1], CSS/USS overlap (in the general case) is handled in 36.213. Such overlap may occur for various reasons (see e.g. [2] for scenarios), and it is not the goal of the email discussion to discuss the general case. In particular, it is already possible when DL gaps are configured that some paging CSS overlap, and this is handled in the specification. We only focus on the case above, in which there is a constant paging CSS overlap (meaning all paging CSS overlap).

We consider the example UE specific DRX  T = 320ms while paging Rmax=512 subframes.

Figure 1 - Constant paging CSS overlap

Note that paging CSS length is equal to broadcasted paging Rmax, and is independent of the UE coverage state. Typically a UE in good coverage needs only to monitor paging candidates with a few subframes, which is indicated in red in above figure; nevertheless, there is constant paging CSS overlap for such UE.

There are 2 possible issues in this example:

1) A UE in extreme coverage, which would need 512 repetitions, can never accumulate the required number of repetitions hence would be unreachable

2) As discussed in [1], CSS overlap (in the general case) is handled in 36.213. Companies agreed with the following observation: “if CSS overlapping happens, the UE is not required to monitor any of NPDCCH candidates for all CSS.”. In above case, this would mean that the UE is not required to monitor paging at all, whatever its coverage level. Hence, even a UE in good coverage could be unreachable, while still being compliant to specifications.

We see following possible options for clarification.

A) Keep current behavior

A1 No change in specified behavior, i.e. UE is not required to monitor any of NPDCCH candidates for all CSS (consequence: UE may not be reachable at all).

Example CM note:

In case of constant paging CSS overlap due to “Paging Rmax > number of available subframes for NPDCCH paging repetitions between POs", the UE follows procedures specified in 36.213.”

B) Alternatives where scenario “Paging Rmax > number of available subframes for NPDCCH paging repetitions between POs” is possible (main goal of these solutions is to allow short UE specific DRX in cells also supporting deep coverage)

B1 Add requirement/clarification that UE should still monitor (if needed) paging CSS candidates that do not overlap (so that only UEs in extreme coverage may not be reachable)

Example CM note:

In case of paging CSS overlap due to “Paging Rmax > number of available subframes for NPDCCH paging repetitions between POs", the UE is still expected to monitor paging CSS candidates that do not overlap (as needed depending on current CE level).

B2 “PO skipping” whenever the UEs require more repetitions than available (on top of B1, with the intent that all UEs would remain reachable)

Example 36.304 update:

For NB-IoT UEs for which UE specific DRX cycle is applicable, in case the UE requires more repetitions than available during T (overlapping paging CSS), the UE may skip paging occasions and keep PF such that SFN mod Text = 0, where Text is the lowest DRX cycle value for which enough repetitions are available, among possible DRX cycle values. ”

C) Alternative where scenario “Paging Rmax > number of available subframes for NPDCCH paging repetitions between POs” is not possible/should be avoided (those solutions may prevent/limit usage of UE specific DRX in cells supporting deep coverage)

C1 It is up to the NW to avoid the scenario (scenario is prevented by NW configuration)

Example CM note:

“It is up to the network to ensure that there is no constant paging CSS overlap that would lead the UE to become unreachable (e.g. by disabling UE specific DRX in the cell supporting deep coverage)”.

C2 It is up to UE to avoid the scenario (scenario is prevented by UE request of a good “UE specific DRX” value)

Example CM note:

“It is up to the UE to request UE specific DRX value such as there is no constant paging CSS overlap that would lead to a situation where UE becomes unreachable”.

C3 Implicit fallback to default cell specific DRX value or higher DRX value avoiding constant CSS overlap

(as proposed in [1], interested companies might provide details)

# Comments

Should this be required?

[Sequans – OM ]: Yes indeed, thanks

Should this be B1?

[Sequans – OM ]: Yes indeed, thanks