3GPP TSG-RAN WG2#110e			R2-2005832

Electronic meeting, 1st – 12th June 2020

Title:	[Draft] LS on AS RAI and optimization of release

Response to:

Release:	Rel-16

Work Item:	LTE_eMTC5-Core, NB_IOTenh3-Core

Source:	Ericsson (to be RAN2)

To:	SA2

Cc:	-

Contact Person:

#### Name:	Tuomas Tirronen

Tel. Number:	+35892993317

E-mail Address:	tuomas.tirronen@ericsson.com

Attachments:

# 1	Overall description

RAN2 discussed whether UE power consumption can be optimized further when AS RAI is indicated if eNB can release the UE immediately, i.e., without waiting for an acknowledgement from the MME/AMF if the UE indicates AS RAI implying that no further data are expected from the S-GW/UPF.

In RAN2, some companies think the optimization can be beneficial to increase UE power savings in some scenarios, however other companies do not agree.

Some companies have expressed concerns with eNB immediately releasing UE could in some cases lead to state mismatch between UE and CN and in increased power consumption and signalling load.

# 2	Actions

To SA2 and RAN3:

ACTION: RAN2 kindly asks SA2 to take above observations into account.

# 3	Dates of the next TSG-RAN WG2 meetings

TSG-RAN WG2#111			17th - 28th Aug 2020	Online meeting

TSG-RAN WG2#112			2nd – 13th Nov 2020	Online meeting

# Comments

An action from this LS is directly to SA2. If SA2 decides to take any action, then they can inform RAN3 if necessary. See no need for RAN2 to take-up RAN3 time unnecessarily.

The scope of this offline discussion based on the agreement is: "Scope: Draft a LS to SA2 and RAN3 on AS RAI and optimization of release."

The LS would be for information so I think RAN3 can be involved as well already.

We see no need to involve RAN3 as they have nothing to discuss until SA2 decides to do anything. Therefore, we don not see any need to involve RAN3.

This does not reflect the discussion accurately

RAI indicates whether UE expect DL packet in response to UL packet.  It is not predicting the downlink data  availability at UPF

There was no consensus in RAN2 that there can be power savings if eNB releases RRC connection immediately upon reception of RAI. Therefore, we do not support this word. In our view the wording in the previous version accurately reflected the status in RAN2.

In any case, there were no empirical data on power saving hence using ‘observed’ is not right.

not needed . they know that

we have agreed not to ask for anything, just a LS for information

The original wording (before QC change) also doesn't ask anything specific and prefer that. Also, as a specific concern has been raised we can indicate that.

All the pros and cons be captured in the description section and no need for any specific action. Adding the last part implies RAN2 expects a feedback. Even if SA2 decides to do anything, there is no impact on RAN2 specification and no need for SA2 to reply to RAN2.