3GPP TSG-RAN WG2#110e			R2-2005832

Electronic meeting, 1st – 12th June 2020

Title:	[Draft] LS on AS RAI and optimization of release

Response to:

Release:	Rel-16

Work Item:	LTE_eMTC5-Core, NB_IOTenh3-Core

Source:	Ericsson (to be RAN2)

To:	SA2, RAN3

Cc:	-

Contact Person:

#### Name:	Tuomas Tirronen

Tel. Number:	+35892993317

E-mail Address:	tuomas.tirronen@ericsson.com

Attachments:

# 1	Overall description

RAN2 discussed whether UE power consumption can be optimized further when AS RAI is indicated if eNB can release the UE immediately, i.e., without waiting for an acknowledgement from the MME/AMF if the UE indicates AS RAI implying that no further data are expected from the S-GW/UPF.

RAN2 thinks the optimization can be beneficial to increase UE power savings, however some companies doubt power consumption gain, if any, would be significant.

Some companies have expressed concerns with eNB immediately releasing UE could in some cases lead to state mismatch between UE and CN with increased power consumption & signalling load.

# 2	Actions

To SA2:

ACTION: RAN2 kindly asks SA2 to take the above observations into account.

# 3	Dates of the next TSG-RAN WG2 meetings

TSG-RAN WG2#111			17th - 28th Aug 2020	Online meeting

TSG-RAN WG2#112			2nd – 13th Nov 2020	Online meeting

# Comments

An action from this LS is directly to SA2. If SA2 decides to take any action, then they can inform RAN3 if necessary. See no need for RAN2 to take-up RAN3 time unnecessarily.

The scope of this offline discussion based on the agreement is: "Scope: Draft a LS to SA2 and RAN3 on AS RAI and optimization of release."

The LS would be for information so I think RAN3 can be involved as well already.

We see no need to involve RAN3 as they have nothing to discuss until SA2 decides to do anything. Therefore, we don not see any need to involve RAN3.

We are fine to involve RAN3 for this issue. - We agree with ZTE comment during online discussion.

- As far as I know, RAN3 has also discussed this issue.

It is the current agreement so we would need to change that first before removing RAN3. Also we think we can keep RAN3 in.

This does not reflect the discussion accurately

We also think this part can be removed.

RAI indicates whether UE expect DL packet in response to UL packet.  It is not predicting the downlink data  availability at UPF

There was no consensus in RAN2 that there can be power savings if eNB releases RRC connection immediately upon reception of RAI. Therefore, we do not support this word. In our view the wording in the previous version accurately reflected the status in RAN2.

In any case, there were no empirical data on power saving hence using ‘observed’ is not right.

The previous version was not accurate because 1) most companies wanted to send LS and agreed on benefit 2) there would be gain in most cases as delay > 0 3) in some cases the benefit may be small, in some cases larger.

In the latest formulation it is not clear what "other companies" do not agree to – do you think there is no power saving (at all), or do you think the potentially would not be significant enough?

Gains from ‘immediate release’ are speculative as RAN2 has not looked at which dedicated configurations provide gains and which do not, e.g. gains depend on (M/N)PDCCH periodicity, C-DRX configuration, coverage level, CN network latency. None of this has been studied in RAN2. It would have been better for RAN2 to have considered RRC configurations to get empirical values for the gains before asking SA2 to revisit this.

This concern is independent of UE and CN state mismatch.

Power saving is already mentioned above as a concern, no need to include twice.

If we add this content in the LS, we prefer to keep the ACTION part asking the concern on state mismatch between UE and CN.

If signalling load is increased i.e. paging and random access procedure for MT traffic then power consumption is also increased hence the state mis-match increases both.

not needed . they know that

we have agreed not to ask for anything, just a LS for information

The original wording (before QC change) also doesn't ask anything specific and prefer that. Also, as a specific concern has been raised we can indicate that.

We prefer the original text not asking specific action.

All the pros and cons be captured in the description section and no need for any specific action. Adding the last part implies RAN2 expects a feedback. Even if SA2 decides to do anything, there is no impact on RAN2 specification and no need for SA2 to reply to RAN2.