3GPP TSG-RAN WG2 Meeting #110-e					R2-20xxxxx

Electronic, 1 June – 12 June 2020

Agenda Item:		6.12.4	ASN1 review

Source:			Huawei, Ericsson

Title:				Summary on RRC correction

WI code(s):			NR_SON_MDT-Core

Document for:		Discussion and Decision

## 1	Introduction

This paper is to provide a summary on RRC correction.

- [AT110-e][888] RRC correction (Huawei, Ericsson)

Scope: discuss the not treated issues in R2-2006015, R2-2005371 and R2-2004416

Intended outcome: Summary of the offline discussion with e.g.:

§  Set of proposals with full consensus, if any (agreeable over email)

§  Set of proposals to discuss in the follow up conference call

Deadline: Tuesday 2020-06-09 10:00 UTC

Status: will start after the first online session

Basically this paper is based on R2-2006015, and the left issues from R2-2005371 and R2-2004416 are added.

Compaines can provide your comments in relevant tables, and then the email rapporteur will make a conclusion for each proposal.

Section 1 is for discussions of R2-2006015, and section 2 is for discussions of R2-2005371. R2-2004416 has been added in Tdoc list in section 4, and there is a table in section 2.12 for the comments on R2-2004416.

## 2	Issue summary (from R2-2006015)

### 2.1	Guideline

Section 2.1 to 2.12 are discussions based on the RIL papers under the AI 6.12.4.

For ASN1 XLS, compared with v64, v164 has 54 new RILs. There are some RILs with no RIL papers, so section 2.13 are to check them. In XLS, the Status and Cat handling are still following the legacy rules.

### 2.2	CEF report

[1], ZTE, [Z162-Z166]

Proposal 1: Modify “if the UE has connection establishment failure informaton available in VarConnEstFailReport” in 5.3.3.7 and 5.3.13.5 to as ““if the UE has connection establishment failure information or resume failure information available in VarConnEstFailReport”.	// (a)

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Yes |  |
| Nokia, Nokia Shanghai Bell | Yes | The variable is common for both types of failures |

Conclusion: Agreeable.

Proposal 2: UE compares the cell identity to determine the numberOfConnFail before it clears the available information except numberOfConnFail in VarConnEstFailReport. 	// (b)

[QC]: Seems reasonable.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| Huawei, HiSilicon | Yes | At the last RAN2 meeting, RIL (line8, C253) was agreed and is to be implemented in the 38.331 CR. That RIL seems to be the same as this proposal, i.e. move the “clear the content…” after comparing the cell. So we think this propsal is agreeable and has been covered by RIL (line8, C253). |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Yes |  |
| Nokia, Nokia Shanghai Bell |  | Originally the parameter was to record number of failures since last RLF but the latest agreement was to count number of consecutive failed connection establishment or resume attempt in the same cell. |

Conclusion: Agreeable.

Proposal 3: UE shall reset the numberOfConnFail to “0” when this is the first connection failure since UE transits from connected to idle state. 	// (b)

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | No need | Based on the latest online agreements, UE determine the numberOfConnFail irrespective of state transition, therefore P3 and P4 is unnecessary. |
| Huawei, HiSilicon | No |  |
| CATT | No |  |
| Apple | No |  |
| Ericsson | No |  |
| Nokia, Nokia Shanghai Bell | No need | State transition should not impact the value |

Conclusion: Not pursued.

Proposal 4: UE reset numberOfConnFail to “1” when storing resume failure information. And remove the part UE compare the numberOfConnFail from subclause 5.3.13.5. 	// (b)

[QC]: Seems reasonable.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | No need | Please see comments above. |
| Huawei, HiSilicon | No |  |
| CATT | No |  |
| Apple | No |  |
| Ericsson | No | This goes against the agreement. So reject. |
| Nokia, Nokia Shanghai Bell | No need | State transition should not impact the value |

Conclusion: Not pursued.

Proposal 5: Update the field description of to numberOfConnFail to “the latest number of consecutive failed connection establishment or resume attempt in the same cell.’’ 	// (a). Covered by the email 960. Since it has been agreed during online session, no need to re-discuss it.

Proposal 5: It is confirmed in RAN2 that following RA resource related information is included in CEF report and the related description is added in TS 38.331:			// (b)

- absoluteFrequencyPointA (e.g., in FrequencyInfoUL)

b. locationAndBandwidth (e.g., in UL BWP)

c. subcarrierSpacing (e.g., in UL BWP)

d. msg1-FDM (e.g., in RACH-ConfigGeneric)

e. msg1-FrequencyStart (e.g., in RACH-ConfigGeneric)

f. msg1-SubcarrierSpacing  (e.g., in RACH-ConfigCommon)

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Since it is agreed in last meeting that CEF report can also be used for RACH optimization, it is beneficial to include RA resource information. Also the RA resource information has already been included in TS37.320, it is easier to fix in TS 38.331 to align the two specs. |
| Huawei, HiSilicon | Yes | RAN2 made the following agreements: 5. The proposed TP in section 5.1 and 5.2 is to be implemented in the CR, and any update can be discussed during CR discussion (e.g. R2-2005469). One agreement is to group some Ies (as mentioned above) into ra-InformationCommon-r16. If P5 is agreeable, it just needs to put ra-InformationCommon-r16 into CEF report. |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | No | The RA resources used by the UE for initial access is always the same as the UE has to use the initial bandwidth part related RA resources i.e., there is only one set of RA resources. Therefore, the network knows which frequency resources are used by the UE to perform RA procedure. Therefore, we believe the UE need not include the RA related frequency resources again in the CEF report. |
| Nokia, Nokia Shanghai Bell | Yes | RA resource information were agreed to be included |

For P5, 6 Companies support and 1 company does not support, so it is suggested to agree on it.

Conclusion: Agreeable.

[8], Ericsson, [E012]

In the procedural text, set the measResultFailedCell to also include tracking area code. 			// (a). In the last RAN2 meeting, this RIL had been already agreed.

[QC]: Seems okay. But trackingAreaCode is optional so need an optional flag after combining in IE.

[Nokia]: We confirm the need to have OPTIONAL flag

[Huawei]: In [H369], we propose to make TAC as an optional field in the CGI-Info-Logging-r16, and the RIL seems agreeable.

### 2.3	RLF report

[2], ZTE, [Z167][Z169]

Proposal 1: In 5.3.5.8.3, move the RLF report content setting procedure to right before the UE initiate re-establishment procedure. 	// (b)

[QC]: seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | The main intention is to align RLF report setting between NR and LTE. With the change in the proposal, NR RLF won’t store the DAPS HO failure information which is aligned with current LTE specs. Another reasons is that DAPS HO failure has not been discussed in MDT WI, to postpone it to R17 allows more time for companies for analysis the topic thoroughly, and to determine if any specific enhancements is required. |
| Huawei, HiSilicon | Yes | In 6.0.1, we note that there is a paper as below. R2-2005177 [E039] Correction of RLF report upon MCG RLF Ericsson draftCR Rel-16 38.331 16.0.0 F NR_SON_MDT-Core, NR_IAB-Core, NR_unlic-Core Late After double check, we think ZTE’s proposed changes are better than Ericsson’s changes. |
| CATT | Yes | The similar view with ZTE and Huawei, DAPS HO failure should not be discussed in R16 |
| Ericsson | Yes | We are fine with the changes by ZTE but we would like to point out to Huawei’s comments that E039 is not related to DAPS handover. What ZTE is proposing is to not include RLF report when the RLF occurs in DAPS scenario whereas the proposal in E039 is related to handling of MCG failure and how to handle the segments of the RRC messages. |
| Nokia, Nokia Shanghai Bell | yes | We agree the intention was to ensure RLF report alignment between NR and LTE. DAPS HO goes beyond Rel-16 |

Conclusion: Agreeable.

Proposal 2: In 5.3.10.3, in order to allow store RLF information when RLF happens and UE goes to idle, the RLF content setting procedure shall be put in the corresponding section when UE goes to idle with release cause ‘other ’ or ‘RRC connection failure’ as well. 	// (b)

[QC]: seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | The same as commented in above proposal, the intention is to align the condition to store RLF failure in RLF report between NR and LTE. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes | Fine to align with LTE behaviour |
| Ericsson | Main session topic | In the last meeting, this was discussed in the main room and here are the notes. So, we propose that this should be discussed in the main room, otherwise there is a risk of double work. [RIL]: E039 [Delegate]: Ericsson (Tony) [WI]: MDT, TEI [Class]: 2 [Status]: Tdoc2 [TDoc]: None [Proposed Conclusion]: [Description]: Upon detecting radio link failure on the MCG, according to current procedure the UE should discard any segments of the segmented RRC message and store various link failure information in the VarRLF-Report variable. However, this should be done only if before triggering the RRC restablishment procedure. [Proposed Change]: We propose to move the following text just before triggering the RRC reestablishment procedure. A possible implementation is as follow: 5> else: 6> discard any segments of segmented RRC messages received ……(until) 11> set the dlRSRPAboveThreshold to false; 6> initiate the connection re-establishment procedure as specified in 5.3.7. [Comments]: [Samsung] We think that UE should discard the RRC segments for some other re-establishment cases as well. So, it would be better to move this sentence to the clause 5.3.7.2 (initiation of RRC connection re-establishment). Rapp2: Changed Class 1 to Class 2 Rapp2: Main session notes: "ZTE agree with the intention and think there should be an independent section. Ericsson think this can be looks further at off-line. Nokia agrees and think we also need to check how this relaed to cond HO. Vivo agrees. " |
| Nokia, Nokia Shanghai Bell | Yes | Both can lead to the same procedure |

Conclusion: no need to discuss it in MDT session as the same discussion is ongoing in [E039] in main session.

Proposal 3: To create an independent section in 5.3.10.3 for RLF report content setting. 	// (b)

[QC]: seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | With the proposed change, it shows more clearly which behavior UE shall take under different conditions. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes but | We prefer to do this before June RAN plenary, maybe ZTE can give a formal CR to implement this issue ASAP. If the CR rapporteur can do this based on the TP from ZTE, we’re also fine. |
| Ericson |  | Okay but not the most important thing as this is just beautification and needs time to review the contents to make sure that they are correct. ZTE needs to provide a CR for this with the complete section and correct formatting to make the merging easier for the rapporteur. If that is not possible, we propose to not include it now. |
| Nokia, Nokia Shanghai Bell | No strong preference |  |

Some companies support but some companies are concerned about the exra work for it. Since this proposal is more about optimisation of the procedural text and we still have some technical work to do (e.g. open proposals, implementation of new agreements and review), it is proposed to not pursue it.

Conclusion: Not pursued.

[5], Samsung, [S951][S952]

Proposal 1: For the case UE declares radio link failure due to the random access problem indication from MCG MAC: if the random access procedure was initiated for beam failure recovery, rlf-Cause is set to beamFailureRecoveryFailure, otherwise rlf-Cause is set to randomAccessProblem. 	// (a)

[QC]: seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Considering there is not beam failure recovery failure indication in MAC specs, we think above clarification is needed. In addition, the same issue shall be fixed when determining the failureType in SCG failure information. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Yes |  |

Conclusion: Agreeable.

Proposal 2: rlf-cause is set to randomAccessProblem or beamFailureRecoveryFailure if the radio link failure is declared due to the random access problem indication from MCG MAC for 4 step random access procedure. 	// (b)

[QC]: seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | No | RLF report is for error detection, it is preferable that UE can record something in case of RLF resulted by 2stepRA problem. To avoid reopening the discussion on RA information inclusion in such case, one simple solution would be to indicate in the procedure part that UE only include RA information when the RA problem indication is from 4step RA procedure. One more thing we think worth clarification is when 2-step RA completely fallback to 4step RA (due to reach the maximum allow transmission times) whether UE needs to record the 4-step RA information in RA report/RLF report after fallback? |
| Huawei, HiSilicon | Yes | P2 seems reasonable. |
| CATT | Yes | It’s fine to limit the scope to 4 step random access procedure in R16 |
| Apple | Yes |  |
| Ericsson | No | Do not agree with the TP provided. It is better to set rlf-Cause as RandomAccessProblem but do not include any perRAInfoList. Otherwise what to set as rlf-Cause? Anyway in the current spec, the UE does not include ‘perRAInfoList’ related RA parameters if it is for 2 step RA as the entire section, 5.7.10.4 is under the condition that it is applicable only for 4 step RA. |
| Nokia, Nokia Shanghai Bell | Yes | 2-step RA related clarification are set as WI objective for Rel-17 |

There are some supports but 2 companies do not support and show some reasons. So it is proposed to not pursue it.

Conclusion: Not pursued.

[6], Ericsson, [E008]

Proposal 1	Include lbtFailure as an option in rlfCause in RLF report.

Proposal 2	Include lbtFailure as a failureType in SCGFailureInfomationNR in LTE RRC specification.

Proposal 3	RAN2 is kindly requested to agree the TPs in this document.

// (b). Under [961] discussion.

[QC]: QC comment can be found in [961] email discussion.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes, but not further enhancement. | We are fine to add only the cause value in this release. In the following we provide some details on how LBT failure relates to RLF, just for information. According to current specs, when consistent LBT failure is detected, UE will switch to another UL BWP that with RACH resource, initiate RACH procedure and report the failure via MAC CE. If uplink LBT failure is detected on all BWPs with RACH resource within the cell, then UE will declare RLF. |
| Huawei, HiSilicon | Wait for [206] | After online discussion of R2-2004724, RAN2 had the following agreements: FFS: The UE includes lbtFailure as a rlf-Cause. No further LBT failure specific measurements are added to the RLF report in rel-16. Waiting the progress [206] Add the option of scg-lbtFailure as an option for failureType in SCGFailureInformationNR message of TS 36.331. Waiting the progress [206] So suggest to wait for [206] discussions. |
| CATT | Yes, but not further enhancement | Based on the agreement of offline 206, P2 is already implemented in 36.331 and is kept as it was. So it’s also fine to include lbtFailure as a rlf-Cause as well. failureType-v16xy ENUMERATED {scg-lbtFailure, beamFailureRecoveryFailure-r16, spare2, spare1} OPTIONAL Agreements (for LTE and NR) 8 For extension of failure types (which have mandatory R15 field) introduced in R16: - Introduce a value other/ unspecified within the legacy field; Use spares if defined and undefined code point otherwise - Include all new R16 values in an –v16xy extension - When signalling the –v16xy extension, the UE will set the legacy field to other/ unspecified |
| Apple | Yes | Agree with CATT |
| Ericsson | Yes |  |

Based on the comments above, P2 has been agreed in [206]. P1 is agreeable.

Conclusion: Agreeable for P1.

[7], Ericsson, [E009]

Based on the outcome of email discussion Post109bis-e#961 [1], it was agreed to include previousPCellID in the NR RLF report. This contribution provides the text proposal for the same. 	// (a). The proposal is following agreements made in [961]

[QC]: Okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Yes | Already implemented based on the agreements. |

Conclusion: Agreeable and already implemented.

[11], Ericsson, [E200]

Proposal 1	Include T312-expiry as an option in rlfCause in RLF report.	// (b)

[QC]: It is included in the SCGFailureInformation. It should be okay to include in RLFCause.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| Huawei, HiSilicon | No | It is about R16 Mobility enhancements and R16 MDT/SON, so suggest to put it to R17. |
| CATT | Yes | It is already included in the SCGFailureInformation, so we’re fine to do so. |
| Apple | No |  |
| Ericsson | Yes |  |

Some companies support it but 2 companies do not support, so it is proposed to not pursue it.

Conclusion: Not pursued.

[19], Huawei, [H365]

There are only observations in this paper.

[QC]: Okay.

[Huawei]: no need to collect comments for this RIL.

[21], Huawei, [H367]

It is suggested to add the following text regarding UE including failedPCellId-EUTRA in LTE RLF report:  3> set failedPCellId-EUTRA to the PCell in which RLF is detected or the target PCell of the failed handover stored in VarRLF-Report of TS 36.331 [10];		// (a)

[QC]: Okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Already agreed in online session. |
| Huawei, HiSilicon | Yes | We are ok to check if it has been covered by online session. If so, duplicated changes should be avoided. |
| CATT | Yes |  |
| Apple | OK |  |
| Ericsson | Yes | FailedPCell is included in the CR. |

Conclusion: Agreeable and already implemented.

[22], Huawei, [H368]

Proposal: The UE should set the measResult-RLF-Report-EUTRA in rlf-Report for LTE RLF report purpose.	// (a)

[QC]: Okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes |  |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple | OK |  |
| Ericsson | Yes |  |

Conclusion: Agreeable.

### 2.4	RACH report

[3], ZTE, [Z170][Z171][Z173]

Proposal 1: If both CB/CF RA resource with different configuration is used in RA procedure, one common IE is used to indicate the CBRA resource configuration, while another dedicated IE is used to indicate the CFRA resource parameters with different value of that in the common IE. 	// (b)

Proposal 2: contentionDetected flag is no required to be included when the ra-Purpose is set to requestForOtherSI. 	// (b)

[QC] No strong opinion.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | - For P1 The intention is to avoid redundant information included in RA report to further reduce RA report size. Considering in many cases CFRA might reuse the same configuration as CBRA, it is beneficial that UE only include the parameters that is different and being used. For example if UE utilize both CBRA and CFRA resource in one RA procedure, and only the msg1-SCS is different between the two configuration, then UE will set the msg1-SCS/FDM/FrequencyStart in the RAresourceCommon IE , and only include msg1-SCS in RAResourceDedicated. - For P2 ---------------------------------------- From 38.331 ---------------------------------------------- if contention resolution was not successful as specified in TS 38.321 [6] for the transmitted preamble: 10> set the contentionDetected to true; 9> else: 10> set the contentionDetected to false; ---------------------------------------- From 38.331 ---------------------------------------------- As shown above, the contentionDetected is set to true when contention resolution is not successful as specified in 38.321, that is, upon expiry of contention Resolution timer. While for msg1-based SI request, the RA procedure is considered completed upon reception of RAR, there is no contention resolution timer. Therefore the contentionDetected will always set to false in this case, which provides zero information. Based on above comment, we think this flag is no need to include for this event. [ZTE2]: In response to Huawei’s comment, we’d like to make some further clarification. For P1, the intention is not to group the common RA information in one IE, the intention is to correct how to include multiple RA resource information. Currently, UE will always include CBRA resource information in RLF/RA report, which is not correct, since RA can be completed based on CFRA resource solely. Therefore, we provide TP to correct the behavior, and on top of that we suggest enhancements to further decrease the RA report size. As explained in our contribution, UE only need to store two set of RA resource when both resource is used and differently configured,otherwise UE stores only one RA resource (either CB or CF) in the report. Moreover, in order to further decrease the RA report size, when 2 set of RA resource is stored, only the parameters that is differently configured is required to be included. As for P2, we think the original proposal is correct, since for Msg3-based SI request the raPurpose is “accessRelated”, raPurpose is only set to “requestForOtherSI” when it is triggered by Msg1-based SI request . |
| Huawei, HiSilicon | Yes for P2, No for P1 | For P1, RAN2 just made the following agreements early this week, so maybe we do not need more changes. 5. The proposed TP in section 5.1 and 5.2 is to be implemented in the CR, and any update can be discussed during CR discussion (e.g. R2-2005469). For P2, we agree with the intention but we propose the following changes: if raPurpose is equal to ‘requestForOtherSI’ and triggered by msg3, or if raPurpose is not equal to ‘requestForOtherSI’: 9> if contention resolution was not successful as specified in TS 38.321 [6] for the transmitted preamble: 10> set the contentionDetected to true; 9> else: 10> set the contentionDetected to false; |
| CATT | Yes | No strong view |
| Ericsson | Yes | P2 is agreeable. I think changes provided corresponding to P1 includes the following. Possibility to provide only CFRA related RA parameters Creation of ‘common’ list and ‘specific’ list. We are fine with 1) above above but not so much for 2) as there is no technical impact of 2) and we prefer to minimize spec changes at this late stage especially those that involves large changes. |
| Nokia, Nokia Shanghai Bell | Yes for P2 | P1 intention is good, but the reading of the reports is getting more complex |

Based on the comments above, P2 is agreeable. It is suggested to not pursue P1.

Conclusion: Agreeable for P2. Not pursue P1.

[13], Ericsson

Proposal 1	The UE includes beamFailureRecovery in raPurpose in case of beam failure recovery failure in the SpCell.

Proposal 2	The UE includes reconfigurationWithSync in raPurpose when RA is triggered due to reconfiguration with sync.

Proposal 3	The UE includes ulUnSynchronized in raPurpose when RA is triggered by a PDCCH order, irrespective of whether the PDCCH order is for the PTAG or STAG.

Proposal 4	Delete sCellAdditionTAAdjestment from RA-purpose.

Proposal 5	The UE includes either the SpCell or the SCell in which RA occurred when the raPurpose is set to ulUnSynchronized.

Proposal 6	The UE includes schedulingRequestFailure in raPurpose when RA is triggered due to scheduling request failure.

Proposal 7	The UE includes noSRPUCCHResourceAvailable in raPurpose when RA is triggered due to lack of PUCCH SR resources configured at the UE.

Proposal 8	The UE includes requestForOtherSI in raPurpose when RA is triggered to request on demand system information.

Proposal 9	The UE includes reestablishment in raPurpose when RA is triggered to perform reestablishment.

Proposal 10 [new]: RA report doesn’t log the RA information if it is triggered due to consistent LBT failure.

//	put (b) to all above proposals

[QC] Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Agree with most of the part, and | -For P3: We think instead of the initiating mechanism, it is more precise to use the triggering event as a condition to determine the RA purpose since when uplink date arrives while uplink is not synchronized, the RA is triggered by UE itself not PDCCH order. The suggest wording is as follows: The UE includes ulUnSynchronized in raPurpose when RA is triggered by a PDCCH order, irrespective of whether the PDCCH order is for the PTAG or STAG. DL or UL data arrival during RRC_CONNECTED when UL synchronisation status is "non-synchronised" or establishment time alignment for a secondary TAG; - For P8: Since we agreed for Msg3-based SI request we will use accessRelated as raPurpose, we think p8 shall be updated as follows to be more precise: The UE includes requestForOtherSI in raPurpose when RA is triggered to request by Msg1 based on demand system information request. - For P10: As commented in issue 2.3, in current specs UE can also trigger the RA procedure due to consistent LBT failure, since we haven’t discussed this in MDT session, and RA report is just for optimization which is not so critical at this stage, we think it is better to postpone it to R17, and clarify in the specs RA information triggered due to consistent LBT failure won’t store in RA report. |
| Huawei, HiSilicon | Agree with most of parts | We are not ok with P4 and P5, and ok with other proposals. |
| CATT | No for P3 P5 P8 P9 | P3 Prefer the re-wording from ZTE, if we agree the re-wording, P5 is not needed P8 The same understanding with ZTE P9 In the beginning, the reason why Msg3-based SI request is categorised into “accessRelated” is that CBRA resources are used for the RACH procedure which is the same with setup or resume procedure. So from this point, we think reestablishment procedure should also use “accessRelated” as the RACH purpose as CBRA resources are also used for this case. |
| Ericsson | Yes to all | For P3: According to ZTE proposal, it seems that the ulUnSynchronized flag should be used when the timeAlignmentTimer has expired in the PTAG/STAG. That is reasonable to us. However, also the PDCCH order case should be considered, since the network may transmit the PDCCH order when the timeAlignmentTimer is still up and running in the UE side. So we propose to enhance the ZTE wording including the PDCCH order, as follows: The UE includes ulUnSynchronized in raPurpose when RA is triggered in a serving cell by a PDCCH order, irrespective of whether the PDCCH order is for the PTAG or STAG. DL or UL data arrival during RRC_CONNECTED when timeAlignmentTimer is not running in the TAG of the concerned serving cell or by a PDCCH order. For P5: It is important to include SpCell and SCell also, because as per the above discussion, the UE may trigger RA in SpCell/SCell when the PTAG/STAG expires or when the UE receives PDCCH order indicating a certain serving cell For P8: Fine with ZTE/CATT proposal For P9: We believe that having a dedicated flag for reestablishment rather than using “accessRelated” is more informative from network perspective. For P10: No strong view. We are also fine to postpone it to Rel.17 |

The following proposals may need more discusion while others are agreeable:

- P3: Ericsson provided an updated wording based on ZTE’s, and it may be agreeable

The UE includes ulUnSynchronized in raPurpose when RA is triggered in a serving cell by a PDCCH order, irrespective of whether the PDCCH order is for the PTAG or STAG. DL or UL data arrival during RRC_CONNECTED when timeAlignmentTimer is not running in the TAG of the concerned serving cell or by a PDCCH order.

- P4

- P5

- P8: It seems that ZTE’s suggestion is agreeable

The UE includes requestForOtherSI in raPurpose when RA is triggered to request by Msg1 based on demand system information  request.

- P9

- P10 (not pursued)

Conclusion:

- Need discussions in the coming online session: P5, P9

- Agreeable: P1, P2, P3, P4, P6, P7, P8

- Not pursued: P10

[16], Samsung, [S481]

For SSB based RA attempt based on contention free random-access resources contentionDetected-r16 is not included in PerRAInfoList-r16.		// (b). Seems to be related to [961]. It has been agreed in meeting week 1 at RAN2-110-e meeting, so no need to re-discuss it.

[QC]: Under discussion in email discussion 961.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Already agreed in online session. Huawei: agree. |
| Ericson |  | Already implemented. |

[27], ZTE, [Z168][Z172]

Proposal 1: One common IE, e.g. RA-InformationCommon is used to indicate the RA related information, i.e., BWP configuration,RA resoource information and perRA-InfoList.	// (b)

Proposal 2: To create a new subclause 5.7.10.5 for determination of RA information in RA report or RLF report, and put the reference at corresponding section.	// (b)

[QC] No strong opinion.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | -For P1: It has already covered by Samsung’s TP, which is agreed online. But we think the naming can be update from RAresourceInfo to ra-InformationCommon, since there is not only RA resource information is included, but also RA performance related information. - For P2, the intention is to clean up the specs since the determination of common RA information in RA report and RLF report is pretty much the same. |
| Huawei, HiSilicon | Yes | RAN2 had agreed: 5. The proposed TP in section 5.1 and 5.2 is to be implemented in the CR, and any update can be discussed during CR discussion (e.g. R2-2005469). I tend to use R2-2005469 = reference [27] to update the CR. |
| CATT | Yes | No strong view |
| Ericsson |  | This is related to P1 of first question in 2.4. See our response there. |

Three companies support and one company indicates that this is related to P1 of first question in section 2.4 (the conclusion of P1 in section 2.4 is Not pursue P1.). So it is proposed to discuss it in the coming online session.

Conclusion: More discussions.

### 2.5	Sensor measurements

[4], CATT

Proposal1: Add an extra availability indicator for Sensor measurements results in RRCReestablishmentComplete, RRCReconfigurationComplete, RRCResumeComplete, RRCSetupComplete, UEInformationResponse messages to align with Bluetooth/WLAN measurements results. 	// (a). In the summary of email 960, this proposal is agreeable.

Proposal2: RAN2 is kindly asked to agree the corresponding TP. 	// (a)

[QC]: Okay.

[Huawei]: due to the discussion for R2-2005371 in meeting week 1, this is an open issue. So it is proposed to discuss it in section 2.

[ZTE]: No strong view.

[Ericsson]: Agree.

### 2.6	Logged MDT

[9], Ericsson, [E021]

Proposal 1	Modify the procedural text to indicate that the UE shall log anyCellSelectionDetected flag indication and the last serving cell related measurements upon entering any cell selection state only when the UE is configured with periodical logged MDT. 	// (b). At the last RAN2 meeting, this proposal was discussed in MDT and the summary paper can be found inR2-2004003. Generally, 8 companies agreed but 4 companies disagreed. If there is no change on companies’ opinions, it is suggested to not pursue this proposal.

[QC]: Agree.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | No | Agree with Rapporteur’s suggestion, not to pursue this proposal at this stage. Current specs is aligned with LTE’s baseline, and we prefer to keep the specs as it is now. |
| Huawei, HiSilicon | No | We have the same view as made in the last RAN2 meeting. |
| Ericsson |  | We are fine with not changing but we are afraid that also starts a dangerous precedence wherein there is an implementation which is exactly the opposite of an agreement and then it is not allowed to change by quoting that there is no majority support. Please check the past agreement. 2b Remove “last serving cell UE camped on before OOC happens” from the RAN2 minutes, as it is agreed online that it is only the leaving condition. May be our understanding of the above agreement is wrong. In that case, please correct it. |
| Nokia, Nokia Shanghai Bell |  | In our understanding, the proposal (and previous agreements) has good intention, but its formulation leads to misinterpretations. The flag for being in OOC is still needed for regular periodical reporting, as well as for event triggered reporting for event=OOC. The UE should log OOC flag in both cases, but for: Periodical – the UE does logging in periodical manner, and if it is facing OOC it should put the flag once, once the UE is able to select a cell and camp on it, it will continue periodical measurement logging OOC-event based – the UE does not log anything, unless it detects anyCellSelecton state. If it does, it will log the state and will end the logging after leaving condition is met |

Still some companies have concerns, so it is suggested to not pursue it.

Conclusion: Not pursued.

[12], Ericsson, [E235]

Proposal 1	The UE shall include a flag in the logged MDT report to indicate whether the UE is performing RRM measurements based on relaxed RRM measurement policy or normal RRM measurement policy.		// (b)

[QC]: Should be discussed in R-17.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Maybe | It is possible UE won’t record anything if it performs RRM relaxation when durationTimer is running. Considering the durationTimer is not so long, we prefer UE doesn’t perform RRM relexation when T330 is running, at least for signalling based MDT, since it is targeted for specific UE. However, if above is not agreeable, we think a flag might be needed, otherwise the NW might be mislead by the results collected. |
| Huawei, HiSilicon | No | Suggest to put it to R17 as it is related to R16 power saving and R16 MDT and SON. |
| CATT | No | We think it’s too late to discuss this issue in R16 and we need more time to think about the impact on data collection . Now my understanding is that even if RRM relaxation is performed when T330 is running, there is some implicit rule involved in the reported logged MDT data, the TCE node can find the implicit rule and know this data is collected under RRM relaxation. |
| Apple | No | Better discussed in R17 |
| Ericsson | Yes | This is an impact of an agreement taken in another WI which clearly impacts MDT results and their interpretation. Other WIs do not care about MDT and it is our responsibility to care for correct MDT feature. With the current situation, the MDT results will create ambiguities if the cell in which the measurements are collected is broadcasting relaxed RRM measurements related parameters. @CATT: We have tried to explain in the paper that there is no such ‘implicit’ way. If there is such an ‘implicit’ way, we would like to ask CATT to provide more details. |
| Nokia, Nokia Shanghai Bell | No | The flag is not needed, but we agree there may be relaxed RRM configuration, Mayne stage 2 text could cover the proposal. No need to logging behaviour |

Conclusion: Not pursued.

[15], Samsung, [S954]

Proposal 1: The UE does not store logged measurement configurations in the UE Inactive AS Context.	// (b). RAN2 agreed that logged MDT is also applicable in RRC Inactive state, so does this proposal contradict the RAN2 agreement?

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | If the intention is UE that relay on the configuration stored in the VarLogMeasConfig to perform the MDT logging, then the proposal is fine for us. |
| Huawei, HiSilicon | Yes | Share the same view as ZTE. |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Yes | It is the network that stores not the UE. So, this is okay for us, |
| Nokia, Nokia Shanghai Bell | No | The proposal is formulated in a way it precludes the storage in variable.There is no separate handling indeed, but the variable stored in the UE is there also in INactive |

6 companies support and 1 company does not support. It is suggested to agree on it.

Conclusion: Agreeable.

[18], Huawei, [H363]

change "2> when performing the logging:"  into:  "2> when adding a logged measurement entry in VarLogMeasReport, include the fields in accordance with the following:"		// (b)

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Ok to align the wording between NR and LTE. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple | Yes |  |
| Ericsson | Not okay with proposed TP but okay with intentions. | The current procedural text is pasted below. As can be seen, the procedural text mentions ‘perform the logging’ (yellow highlighted) before coming to the actual ‘when performing the logging’ (green highlighted) part of the procedure. So, the current procedural text uses the term ‘perform the logging’ before and therefore it is good to keep the green highlighted text. What we can do, is further add some text further below (with change marks and blue highlighted) instead of what is proposed. 5.5a.3.2 Initiation While T330 is running, the UE shall: 1> perform the logging in accordance with the following: 2> if the reportType is set to periodical in the VarLogMeasConfig: 3> if the UE is camping normally on an NR cell and if the RPLMN is included in plmn-IdentityList stored in VarLogMeasReport and, if the cell is part of the area indicated by areaConfiguration if configured in VarLogMeasConfig: 4> perform the logging at regular time intervals, as defined by the loggingInterval in the LoggedPeriodicalReportConfig; 2> else if the reportType is set to eventTriggered and eventType is set to outOfCoverage: 3> perform the logging at regular time intervals as defined by the loggingInterval in VarLogMeasConfig only when the UE is in any cell selection state; 3> perform the logging immediately upon transitioning from the any cell selection state to the camped normally state; 2> else if the reportType is set to eventType and eventType is set to eventL1: 3> if the UE is camping normally on an NR cell and if the RPLMN is included in plmn-IdentityList stored in VarLogMeasReport and, if the cell is part of the area indicated by areaConfiguration if configured in VarLogMeasConfig; 4> perform the logging at regular time intervals as defined by the loggingInterval in VarLogMeasConfig only when the conditions indicated by the eventL1 are met; 2> when performing the logging: 3> include the fields in VarLogMeasReport as follows: 4> set the relativeTimeStamp to indicate the elapsed time since the moment at which the logged measurement configuration was received; |

Two options on clarifications are provided, so it is proposed RAN2 to decide on one of them.

Option 1:

change "2> when performing the logging:"  into:  "2> when adding a logged measurement entry in VarLogMeasReport, include the fields in accordance with the following:"

Option 2:

Add “3>	include the fields in VarLogMeasReport as follows:” after “2>	when performing the logging:”

Conclusion: Discuss option 1 and option 2.

[24], Huawei, [H371]

Proposal: It is proposed to add UE behaviours regarding the field InterFreqTargetList in the procedural text.	// (b)

[QC] We prefer UE implementation for this.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE |  | No strong view. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes |  |
| Apple |  | Left to UE implementation |
| Ericsson | Yes but the wording needs to be imrpvoded | This is not up to UE implementation as the UE behaviour when InterFreqTargetList is configured needs to be specified. |

Two companies support but there are also some concerns, so it is suggested to not pursue it.

Conclusion: Not pursued.

[25], Samsung, [S959]

Proposal: IE InterFreqTargetList moves out of IE AreaConfiguration.	// (b)

[QC]: Seems Okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Seems reasonable. |
| Huawei, HiSilicon | No | Both AreaConfig and InterFreqTargetList are to limit the area for which UE is requested to perform measurement logging, so it is beneficial to group them in the same IE. |
| CATT | No | The field description is already clear enough. |
| Apple | No strong view |  |
| Ericsson | No | The field description is clear already. |

Conclusion: Not pursued.

### 2.7	UE capabilities

[10], Ericsson, [E028]

TP for 38.331 on UE capabilities.	// (a). email [802] UE capabilities discussion is now covering it. So companies can follow that email if any comment.

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE |  | Treated in email discussion [802.] Huawei: agree. |

### 2.8	Mobility History Information

[14], Samsung, [S953]

Proposal 1: The UE does not include mobilityState in the RRCSetupComplete message if RRCSetup is received in response to an RRCReestablishmentRequest.	// (b)

[QC]: Seems okay.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Since the mobility state is derived based on the number of cell reselection within a period of time, and cell selection is used in re-establishment, the latest mobilitystate might not be available during the re-establishment procedure. If we have to include this, the old mobilitystate before UE entering connected state will be used, which seems not so useful and may provide misleading information. |
| Huawei, HiSilicon | Yes |  |
| CATT | Yes | The mobilityState evaluation is not performed when UE in connected mode, the misalignment between the UE real mobility and the UE old mobility state before UE entering connected state may happen. |
| Apple | Yes |  |
| Ericsson | Yes |  |

Conclusion: Agreeable.

### 2.9	Processing delay requirements

[20], Huawei, [H366]

Proposal: Suggest to add UE information procedure in processing delay requirements and the value could be one of the following options:	// (b)

- (1) 15 ms. This is following LTE definition

- (2) NA

- (3) a specific value different from 15ms

[QC] We prefer same value as LTE. i.e., 15ms.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | 1 | We are fine to follow LTE value . |
| Huawei, HiSilicon | (1) | Ok to follow LTE definition. |
| CATT | 1 | follow LTE definition |
| Apple | 1 |  |
| Ericsson | 3 | 10 ms In LTE all the RRC messages like RRCConnectionReconfiguration, RRCConnectionSEtup use to take 15 ms wherein in NR the corresponding messages take 10ms. Based on this, we believe the UEInformationReqt-Resp also should take 10ms to align with rest of the NR related RRC messages. |
| Nokia, Nokia Shanghai Bell | 1 | Follow LTE definition, as no specific analyses was taken for NR |

Most of companies prefer (1), so it is suggested to go with it.

Conclusion: Option (1) is agreeable.

### 2.10	CGI info

[23], Huawei, [H369][H370]

It is suggested to add Optional for trackingAreaCode-r16 in CGI-Info-Logging-r16.	// (a)

In order to be aligned with the procedural text, in the field description of trackingAreaCode, it is suggested to add the following text:  This field should be included if CGI-Info-Logging-r16 is under RA-Raport-r16 or under ConnEstFailReport-r16.		// (b)

[QC]: Agree.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Yes | Maybe we can relay on the detailed procedure to know when to include the TAC, the field description seems no so necessary. If we decide to add the field description, we think the correct condition is “This field should be included if CGI-Info-Logging-r16 is under RA-Raport-r16 or under ConnEstFailReport-r16 RLF-Report-r16.’ |
| Huawei, HiSilicon | Yes | Agree on the 1st proposal, and we are not strong on the 2nd one. If companies think that procedural text is clear enough on how to include the TAC, we are also ok. |
| CATT | Yes |  |
| Ericsson | Yes | It has been agreed to include TA for RAReport, RLF report and CEF report. So, we do not agree with ZTE’s comments. At the time of including this agreement, ‘CGI-Info-LoggingDetailed-r16’ had TAC as well. 2 Use CGI-Info-LoggingDetailed-r16 instead of CGI-Info-Logging-r16 to encode measResultFailedCell-r16 in ConnEstFailReport-r16. Merge two IEs into one. So, we can add ‘RLF Report’ in the procedural description. |
| Nokia, Nokia Shanghai Bell | Yes |  |

1st proposal is agreeable, and 2nd one is not pursued.

Conclusion: Agreeable for P1. P2 is not pursued.

### 2.11	TP related to SON email 961

[26], ZTE

TP		// (b). Or maybe we can agree to it and review changes in the updated 38.331 CR.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE |  | The TP only captures following 2 agreements: 2 The UE does not include the dlRSRPAboveThreshold-r16 flag for SSB based CFRA if the CFRA is not associated to PDCCH ordered RA and the UE includes the dlRSRPAboveThreshold-r16 flag for SSB based CFRA if the CFRA is associated to PDCCH ordered RA. 3 The UE shall append the new EPLMNs to the PLMN entries in the plmn-IndentityList until the maximum number is reached and after this limit is reached the UE shall stop the recording of the RAReports until the existing contents of VarRAReport is fetched by the network or the 48 hour time window expires. But we are fine to review it when updating 331 CR |
| Huawei, HiSilicon |  | Ok to review it when updating 38.331 CR. |
| CATT |  | Fine to review it when updating 38.331 CR |
| Ericsson |  | Implemented in 38.331 CR. |

Conclusion: further review it when updating 38.331 CR.

### 2.12	CHO + RLF report

[28], CATT, [C210]

Observation 1: For condition handover, the time gap between HO initialization and the point where the UE starts to access the candidate Cell is implementation dependent.

Proposal 1: For LTE or NR RLF report, if the last handover procedure UE performed before declaring HO failure or RLF failure is a condition handover, the starting point of timeConnFailure is the time where UE started to access the first candidate Cell.

Observation 2: UE may try more than one candidate cells during the last handover procedure UE performed before declaring HO failure or RLF failure.

Proposal 2: For LTE or NR RLF report, if the last handover procedure UE performed before declaring HO failure or RLF failure is a condition handover, the ending point of timeConnFailure for condition HO failure is until the last T304 expiry, while for RLF failure case, no change is needed for the ending point of timeConnFailure.

Proposal 3: RAN2 is asked to agree the corresponding TP in section 4.

| Company | Yes/No | Comments |
| --- | --- | --- |
| ZTE | Probably no | We think before discussion above issue , one thing needs to be consider first is whether we shall support recording CHO failure information in RLF report in this release, since the CHO procedure is quite different from R15 HO behavior. Currently, when HO failure happens and UE has been configured with conditional HO configuration, UE can first perform CHO based reestablishment (i.e. without sending RRCReestablishmentRequest ); and if the CHO reestablishment fails UE can go back to normal RRC reestablishment procedure. Since in current specs UE can only set the reestablishment cell id when it transmits RRCReestablishmentRequest message, if the CHO based reestablishment success then UE cannot record the reestablished cell id. If CHO fails and the second reestablishment success, then UE will only record the second reestablishment cell id, and NW cannot know there is a previous CHO reestablishment attempt. We are not sure whether such information is sufficient for CHO cases. Although CATT’s proposals seem reasonable, but based on above comments, CHO is a very different case which has never been discussed in R16 MDT, maybe it is safer to postpone the discussion to R17 so that we can have a thoroughly investigation. |
| Huawei, HiSilicon | No | Suggest to put it to R17 as it is not urgent. |
| CATT |  | If companies think CHO failure will not cause RLF report in the release, we’re fine to discuss it in R17; otherwise, we should discuss it in R16. My understanding is that CHO failure will cause RLF report in R16 as we have agreed LBT failure will cause RLF report in R16 which is also a R16 feature. |
| Apple |  | Better to be discussed in R17 |
| Ericsson |  | Regarding P1, there can be different way to use the existing timeConnFailure in RLF report for CHO case. For example, this is an indication as to how late the actual condition got triggered + time between triggering and declaring failure. The first component is also useful. So, we believe this should not be discarded. So, we believe there is a need for some discussion here. |
| Nokia, Nokia Shanghai Bell | No | Dependencies on CHO were out of scope of Rel-16 |

Conclusion: Not pursued.

### 2.13	New RILs that are not covered by RIL papers

Companies can check the RILs and provide comments in the column Comments.

| ID | Delegate | Description | Proposed Change | Agreeable | Comments |
| --- | --- | --- | --- | --- | --- |
| H360 | Jun Chen (Huawei) | Missing description on SON and MDT. In comparison, TS 36.331 has defined the following: - Support of self-configuration and self-optimisation (not applicable for NB-IoT); - Support of measurement logging and reporting for network performance optimisation, as specified in TS 37.320 [60] (not applicable for NB-IoT); | It is suggested to add similar description as LTE, e.g.: - Support of self-configuration and self-optimisation; - Support of measurement logging and reporting for network performance optimisation, as specified in TS 37.320 [xx]; | (a) | Conclusion: Agreeable. |
| H361 | Jun Chen (Huawei) | For the following description, it is missing "or connection resume failure" in the last part: The UE may discard the connection establishment failure or connection resume failure information , i.e. release the UE variable VarConnEsFailReport, 48 hours after the last connection establishment failure is detected. | Add "or connection resume failure" in the description "48 hours after the last connection establishment failure is detected." | (a) | Conclusion: Agreeable. |
| Z161 | Z(Zhihong) | Missing procedure to release btNameList,wlanNameList and sensorNameList, which is “need M” in OtherConfig | Upon initiation of the procedure, the UE shall: /*Partially omitted*/ 1> stop timer T342, if running; 1> stop timer T345, if running; 1> release idc-AssistanceConfig, if configured; 1> release btNameList, if configured; 1> release wlanNameList, if configured; 1> release sensorNameList, if configured; | (a) | Conclusion: Agreeable. |
| E201 | Ericsson (Pradeepa) | Wrong reference to the section 5.7.10.4 instead of 5.3.10.4 | Existing text: 5> set the rlf-Cause to the trigger for detecting radio link failure in accordance with clause 5.7.10.4; Proposed text: 5> set the rlf-Cause to the trigger for detecting radio link failure in accordance with clause 5.3.10.4; | (a) | Conclusion: Agreeable. |
| H362 | Jun Chen (Huawei) | The 1st, 2nd and 3rd "2>" are for three logging cases, and regarding UE behaviours on "loggingInterval", there are the following text: (1) for periodical MDT, there is " ... by the loggingInterval in the LoggedPeriodicalReportConfig" (2) for event triggered MDT, there is "....by the loggingInterval in VarLogMeasConfig" | Suggest to update the UE behaviours on the loggingInterval for event triggered MDT. For example: 3> perform the logging at regular time intervals as defined by the loggingInterval in VarLogMeasConfig (changed into LoggedEventTriggerConfig) only when the UE is in any cell selection state; 4> perform the logging at regular time intervals as defined by the loggingInterval in VarLogMeasConfig (changed into LoggedEventTriggerConfig) only when the conditions indicated by the eventL1 are met; | (a) | Conclusion: Agreeable. |
| E239 |  |  |  | (b) | Will be handled in main room |
| E206 |  |  |  | (b) | Will be handled in main room |
| H364 | Jun Chen (Huawei) | There are duplicated description on discarding the LTE RLF report (as below). 3> discard the rlf-Report from VarRLF-Report upon successful delivery of the UEInformationResponse message confirmed by lower layers; 3> discard the rlf-Report from VarRLF-Report of TS 36.331 [10] upon successful delivery of the UEInformationResponse message confirmed by lower layers; | Suggest to keep the second "3>" and remove the first one. | (a) | Conclusion: Agreeable. |
| N040 | Nokia (Tero) | Consider grouping the mandatory fields under an IE – these are the fields needed to distinguish the Trace context at network side. | Create IE for these and use it to identify the Trace identity for the UE: NR-Trace-r16 ::= SEQUENCE { traceReference-r16 TraceReference-r16, traceRecordingSessionRef-r16 OCTET STRING (SIZE (2)), tce-Id-r16 OCTET STRING (SIZE (1)), ... } and LoggedMeasurementConfiguration-r16-IEs ::= SEQUENCE { traceIdentity-r16 NR-TraceId-r16 absoluteTimeInfo-r16 AbsoluteTimeInfo-r16, | (b) | Huawei: the changes are just regrouping, and seems no need. [Ericsson] Not needed Conclusion: Not pursued. |
| Z175 | Z(Zhihong) | According to ASN.1 coding guideline, the need code for SetupRelease structure is “need M” | LoggedMeasurementConfiguration message -- ASN1START -- TAG-LOGGEDMEASUREMENTCONFIGURATION-START LoggedMeasurementConfiguration-r16 ::= SEQUENCE { criticalExtensions CHOICE { loggedMeasurementConfiguration-r16 LoggedMeasurementConfiguration-r16-IEs, criticalExtensionsFuture SEQUENCE {} } } LoggedMeasurementConfiguration-r16-IEs ::= SEQUENCE { traceReference-r16 TraceReference-r16, traceRecordingSessionRef-r16 OCTET STRING (SIZE (2)), tce-Id-r16 OCTET STRING (SIZE (1)), absoluteTimeInfo-r16 AbsoluteTimeInfo-r16, areaConfiguration-r16 AreaConfiguration-r16 OPTIONAL, --Need R plmn-IdentityList-r16 PLMN-IdentityList2-r16 OPTIONAL, --Need R bt-NameList-r16 SetupRelease {BT-NameList-r16} OPTIONAL, --Need M R wlan-NameList-r16 SetupRelease {WLAN-NameList-r16} OPTIONAL, --Need M R sensor-NameList-r16 SetupRelease {Sensor-NameList-r16} OPTIONAL, --Need M R | (a) | Conclusion: Agreeable. |
| N002 | Nokia (Tero) | This is a mandatory field but not extendible. If we ever have to extend it, there will need to be discussion on what is filled in for the legacy field. Hence, it would be cleaner to just add ellipsis to the reportType CHOICE definition. | Add ellipsis to the CHOICE. | (a) | Conclusion: Agreeable. |
| I680 | Intel (Sudeep) | Need late and non critical extensions | Add late and noncritical extensions. | (a) | Conclusion: Agreeable. |
| I672 | Intel (Sudeep) | Could be useful to add an extension marker for future. | Add extension marker. Also for LoggedEventTriggerConfig-r16. | (a) | Conclusion: Agreeable. |
| X003 | NEC (Hisashi) | As legacy network may receive the SCGFailureInformation from Rel-16 UE, the legacy failureType shall be set in backward compatible manner, i.e. randomAccessProblem when the new failureTypeExt is set to beamFailureRecoveryFailure. Otherwise, the network cannot identify the failure cause appropriately. This is not only SON/MDT issue, but also NR genral issue. | Change the field description to “The field contains the reason for declaring the SCG failure. When the UE includes failureTypeExt set to beamFailureRecoveryFailure, the UE shall set the failureType to randomAccessProblem. then the network discards the contents of the field failureTyp i.e., Otherwise, the UE can chose any of the option for failureType is failureTypeExt is included.” Then, Remove the corresponding NOTE in 5.7.3.3 and 5.7.3.5. | (a) | Conclusion: Agreeable. |
| I671 | Intel (Sudeep) | Missing Need codes. All of them seem to be one-shot processing in the UE. | Add Need N for all these fields. | (a) | Conclusion: Agreeable. |
| E203 | Ericsson (Pradeepa) | The presence of ‘…’ in the MeasResultServingCell will create a lot of additional overhead. MeasResultServingCell is included in every sample of logged MDT report and thus this extension marker should be removed to reduce the logged MDT report size. | Remove ‘…’ in MeasResultServingCell-r16 in UEInformationResponse message. | (a) | Conclusion: Agreeable. |
| Z152 | Z(QZH) | Current RA report only include one set of RA resource configuration, i.e., msg1-FDM, msg1-SubcarrierSpacing and msg1-FrequencyStart, while during one RA procedure UE might use different RA resource with different value of parameters mentioned above, e.g., when switching between CBRA and CFRA, therefore RA report shall be enhanced to be able to include more than one RA resource configuration. The same problem also appears in RLF report involving RA. Also the ‘msg1-” is updated to “prach-” to cover both 2-step/4stepRA case. For more details please refer to the tdoc provided. Some changes are also needed to the procedure text in sections 5.3.10.3, 5.7.10.4 and 6.4 | Please refer to the contribution R2-2002923. | (b) | It seems that R2-2002923 is not available. |
| E202 | Ericsson (Marco) | The field raPurpose is included as part of the RAReport. But it is not clear as to what value is set by the UE for different RA procedures initiated by the UE | Update the field description as provided in R2-20xxxxx to explicitly capture the UE behaviour related to what value if set by the UE for the field raPurpose when the UE performs an RA procedure. | (b) | ZTE:Covered by above discussion in section 2.4 Huawei: ok to wait for decision for seciton 2.4. Conclusion: Wait for conclusions for section 2.4. |
| Z174 | Z(Zhihong) | The definition of msg1-FrequencyStart and msg1-SubcarrierSpacing in RA-report is the same as the one defined in RACH-ConfigGeneric and RACH- ConfigCommon, no additional information is given, the field description here is unnecessary. | Delete the field description of msg1-FrequencyStart and msg1-SubcarrierSpacing in RA-Report field description. | (a) | Conclusion: Agreeable. |
| C210 | CATT(Jayson) | For condition handover, there may have some gap between HO initialization and the point where the UE starts to access the candidate Cell(UE will check whether the trigger condition is fulfilled or not during the gap), in our view, it doesn’t make sense to consider this gap in timeConnFailure because this gap is not related to HO failure itself, so we prefer to redefine a new starting point for CHO case when recording timeConnFailure. More addition, UE may try several candicate cell before declaring HO failure, so it’s better to clarify the ending point for CHO case when recording timeConnFailure to avoid any confusion. | Redefine a new starting point and ending point for CHO case when recording timeConnFailure. One contribution is requsted from CATT to give more detailed discussion for this class 2 issue. | (b) | This RIL is about CEF and CHO, and maybe it can be put to R17. ZTE: Prefer to postpone to R17. Huawei: agree with ZTE. CATT: See comment in 2.12 Conclusion: Not pursued. |
| I635 | Intel (Sudeep) | This seems to be an uplink IE. Need codes should not be used. | Delete the Need codes for all fields. | (a) | Conclusion: Agreeable. |
| N037 | Nokia (Tero) | These fields are not following ASN.1 guidelines: BOOLEAN + Need R is unnecessary – either we use BOOLEAN + Need M (or even mandatory fields) or ENUMERATED {true} + Need R. | Use mandatory fields with BOOLEAN, i.e. as shown below: Sensor-NameList-r16 ::= SEQUENCE { measUncomBarPre-r16 BOOLEAN, measUeSpeed BOOLEAN, measUeOrientation BOOLEAN } | (a) | ZTE: This has been categorized as Duplicated by RRC rapporteur, and has been implemented in the latest 38.331 CR. Huawei: ok to avoid duplication. |
| B201 | Lenovo (Hyung-Nam) | Need codes for all optional fields are not needed. Furthermore, no Setup/Release funcction is needed for bt-NameList-r16, wlan-NameList-r16, sensor-NameList-r16 in the variable. We can simply refer to BT-NameList-r16, WLAN-NameList-r16, Sensor-NameList-r16. | Remove need codes for all optional fields and remove SetupRelease function call for IE BT-NameList-r16, WLAN-NameList-r16, Sensor-NameList-r16. | (a) | This has been discussed in email 960 (raised from Hakan), and has been implemented in the latest 38.331 CR. Conclusion: Agreeable and has been implemented. |
| S955 | Samsung (Sangbum Kim) | There is no such resultSSB-Indexes IE in ASN.1 so we can remove it. | to include neighbouring cell measurements (excluding the resultsSSB-Indexes IE) that became available [Comments]: | (a) | Conclusion: Agreeable. |
| S956 | Samsung (Sangbum Kim) | Unlike SIB1, the plmn-IdentityList in LoggedMeasurementConfiguration is just one single list and this sentence is already mentioned in SIB1. So we can remove it. | Delete "A PLMN-identity can be included only once, and in only one entry of the PLMN-IdentityInfoList." [Comments]: | (a) | Conclusion: Agreeable. |
| S957 | Samsung (Sangbum Kim) | According to the ASN.1 structure, there is no resultSSB-Indexes IE within the measResultListNR IE in the LogMeasInfo-r16 IE. So the whole sentence can be removed. | Delete "UE does not include the resultsSSB-Indexes IE, if the measResultListNR IE is included in the LogMeasInfo-r16." | (a) | Conclusion: Agreeable. |
| S958 | Samsung (Sangbum Kim) | In order to have delta signalling i.e. avoid that entire list has to be included, need M is more appropriate, which is aligned with LTE. | includeBT-Meas-r16 SetupRelease {BT-NameList-r16} OPTIONAL, -- Need RM includeWLAN-Meas-r16 SetupRelease {WLAN-NameList-r16} OPTIONAL, -- Need RM includeSensor-Meas-r16 SetupRelease {Sensor-NameList-r16} OPTIONAL -- Need RM ]] [Comments]: | (a) | Conclusion: Agreeable. |
| B204 | Lenovo (Hyung-Nam) | Need codes for the optional fields interFreqTargetList-r16, cellist (in InterFreqTargetList-r16) are missing. Since IE AreaConfiguration is optional with Need R, Need R for both fields looks appropriate. | Add Need R for the optional fields interFreqTargetList, cellList. | (a) | Conclusion: Agreeable. |

## 3	Issue summary (from R2-2005371)

Based on RAN2 MDT minutes, the following proposals are listed and companies can provide the comments in the relevant tables.

As below, here are some proposals as there were no consensuses or were not enough time in the relevant discussions, so it is proposed RAN2 to make decisions:

Proposal 3: Regarding how to determine whether a cell is part of the area Indicated by AreaConfiguration, one solution is:

consider only first PLMN-Identity in first PLMN-IdentityInfo of the PLMN-IdentityInfoList, and cellIdentity corresponding to the first PLMN-IdentityInfo.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei, HiSilicon | No | We wonder whether the UE should check all PLMN-Identities in SIB1 in order for the cell, because only the first PLMN-Identity may not be enough. |
| ZTE | Maybe | To check all the PLMN-Identities in SIB1 is a safer choice. But we notice for areaConfiguration in NR, it is a choice among CGI with TAC, TAC alone or TAI, and in NR for different PLMN-Identity, the same geographical area could have different TAC, maybe it would be beneficial to have some restriction so that the understanding of the areaConfiguration is more aligned between NW and UE. |
| Ericsson | No | We also think that all the EPLMN list should be used to check if the configured PLMNInfoList stored in varMeasLogInfo is part of such a EPLMN list or not. |

Conclusion: Not pursued.

Proposal 4: It is proposed to postpone any change to LTE-5GC to later release, and remove 5GC identities in the filed CGI-InfoEUTRALogging.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei, HiSilicon | No | During the online session in meeting week 1 at RAN2-110-e meeting, lots of agreements were made regarding the incoming LSs from RAN3. We think 5GC identities are useful in the field CGI-InfoEUTRALogging for some cases. In addition, we think whether LTE specs should support storing the RLF when UE connected to 5GC is a seperate issue, which can be independent with NR RLF report discussion. |
| CATT | No | The same view with Huawei |
| ZTE | No |  |
| Ericsson | No |  |

Conclusion: Not pursued.

Proposal 5: For location reporting, change the wording “attempt to have…” to “include available…”. Detailed changes are listed in section 2.6.5.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei, HiSilicon | Yes | Seems reasonable. |
| Ericsson | Ok |  |

Conclusion: Agreeable.

3. Option2: Add an extra availability indicator for Sensor measurements results in RRCReestablishmentComplete, RRCReconfigurationComplete, RRCResumeComplete, RRCSetupComplete, UEInformationResponse message to align with Bluetooth/WLAN measurements results.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei, HiSilicon | No strong view | Whether to have available indicator should be discussed case by case. BT/WLAN had discussions on the available indicators in LTE Rel-15, and finally they were agreed. Sensor related indicators are new and it seems not reasonable to follow the same logic as BT/WLAN. On the other hand, if there are no objections of having the indicator, we can be also ok (even if there are some impacts to 38.331 CR). |
| CATT | Yes |  |
| ZTE | No strong view | To add one extra availability bit just to align with WLAN/BT seems lack of motivation. It would be appreciated if proponent companies can give an example on how this availability bit can be useful. |
| Ericsson | Yes |  |

2 companies support and 2 companies do not have strong views, so it is suggested to agree on it.

Conclusion: Agreeable.

4	Upon setup failure or resume failure, UE sets the plmn-Identity to RPLMN if available.

| Company | Yes/No | Comments |
| --- | --- | --- |
| Huawei, HiSilicon | No | This open issue should be related to both S470 and S471. In the summary R2-2005371, S470 and S471 were discussed together as both are related to the above proposal. However, in the latest XLS, S470 has the status PropAgree and it is different from the status of S471, so it needs to be updated later (pending for the conclusion of the above proposal). In general, we disagree with proposal 4, and we think the current text is correct and clear. For LTE definition, RAN2#79 made the following agreements regarding the selection of PLMN for CEF case. Agreements For LTE and UMTS… 1) The UE stores the Selected PLMN (as in 36.331) upon Connection Establishment Failure. Only if that PLMN is the same as the RPLMN in the subsequently established connection, the UE may report establishment failure. 2) Shall capture this in Stage-2, with a NOTE saying that performance is considered to be the same as if the UE would have been able to report to ePLMNs also. In our opinion, during UE mobility procedures, the PLMN may be changed, and thus it is reasonable for the UE to always set the plmn-id from upper layers. In addition, the current text is following LTE definition, and we do not see strong reasons of changing this UE behaviour or having totally different behaviours between LTE and NR on the selection of PLMN. |
| CATT | No | The similar view with Huawei During cell reselection when UE in inactive mode, UE may select a EPLMN cell where the UE current RPLMN is not broadcast in the new cell. And the CEF happen in the new cell, in this case, UE should use the selected EPLMN in the CEF report. |
| ZTE | No | Share the same view as Huawei and CATT, we think current specs captures the correct behavior. |
| Ericsson | No | Same view as CATT. |

Conclusion: Not pursued (for both S470 and S471).

## 4	Conclusion

Based on the discussions in section 2 and 3, here is a summary:

Agreeable proposals: (in XLS, the status will be PropAgree)

[1], ZTE, [Z162-Z166]		Proposal 1: Modify “if the UE has connection establishment failure informaton available in VarConnEstFailReport” in 5.3.3.7 and 5.3.13.5 to as ““if the UE has connection establishment failure information or resume failure information available in VarConnEstFailReport”.

[1], ZTE, [Z162-Z166]		Proposal 2: UE compares the cell identity to determine the numberOfConnFail before it clears the available information except numberOfConnFail in VarConnEstFailReport.

[1], ZTE, [Z162-Z166]		Proposal 5: It is confirmed in RAN2 that following RA resource related information is included in CEF report and the related description is added in TS 38.331:

- absoluteFrequencyPointA (e.g., in FrequencyInfoUL)

b. locationAndBandwidth (e.g., in UL BWP)

c. subcarrierSpacing (e.g., in UL BWP)

d. msg1-FDM (e.g., in RACH-ConfigGeneric)

e. msg1-FrequencyStart (e.g., in RACH-ConfigGeneric)

f. msg1-SubcarrierSpacing  (e.g., in RACH-ConfigCommon)

[2], ZTE, [Z167][Z169]		Proposal 1: In 5.3.5.8.3, move the RLF report content setting procedure to right before the UE initiate re-establishment procedure.

[5], Samsung, [S951][S952]		Proposal 1: For the case UE declares radio link failure due to the random access problem indication from MCG MAC: if the random access procedure was initiated for beam failure recovery, rlf-Cause is set to beamFailureRecoveryFailure, otherwise rlf-Cause is set to randomAccessProblem.

[6], Ericsson, [E008]		Proposal 1	Include lbtFailure as an option in rlfCause in RLF report.

[7], Ericsson, [E009]		Based on the outcome of email discussion Post109bis-e#961 [1], it was agreed to include previousPCellID in the NR RLF report. This contribution provides the text proposal for the same.		(already implemented)

[21], Huawei, [H367]		It is suggested to add the following text regarding UE including failedPCellId-EUTRA in LTE RLF report:  3> set failedPCellId-EUTRA to the PCell in which RLF is detected or the target PCell of the failed handover stored in VarRLF-Report of TS 36.331 [10];		(already implemented)

[22], Huawei, [H368]		Proposal: The UE should set the measResult-RLF-Report-EUTRA in rlf-Report for LTE RLF report purpose.

[3], ZTE, [Z170][Z171][Z173]			Proposal 2: contentionDetected flag is no required to be included when the ra-Purpose is set to requestForOtherSI.

[13], Ericsson:

Proposal 1	The UE includes beamFailureRecovery in raPurpose in case of beam failure recovery failure in the SpCell.

Proposal 2	The UE includes reconfigurationWithSync in raPurpose when RA is triggered due to reconfiguration with sync.

Proposal 3	The UE includes ulUnSynchronized in raPurpose when RA is triggered by a PDCCH order, irrespective of whether the PDCCH order is for the PTAG or STAG.

Proposal 4	Delete sCellAdditionTAAdjestment from RA-purpose.

Proposal 6	The UE includes schedulingRequestFailure in raPurpose when RA is triggered due to scheduling request failure.

Proposal 7	The UE includes noSRPUCCHResourceAvailable in raPurpose when RA is triggered due to lack of PUCCH SR resources configured at the UE.

Proposal 8	The UE includes requestForOtherSI in raPurpose when RA is triggered to request on demand system information.

[15], Samsung, [S954]		Proposal 1: The UE does not store logged measurement configurations in the UE Inactive AS Context.

[14], Samsung, [S953]		Proposal 1: The UE does not include mobilityState in the RRCSetupComplete message if RRCSetup is received in response to an RRCReestablishmentRequest.

[20], Huawei, [H366]		Proposal: Suggest to add UE information procedure in processing delay requirements and the value is 15 ms.

[23], Huawei, [H369][H370]		It is suggested to add Optional for trackingAreaCode-r16 in CGI-Info-Logging-r16.

For RILs mentioned in section 2.13, agree on the conclusions for the RILs.

Proposal 5: For location reporting, change the wording “attempt to have…” to “include available…”. Detailed changes are listed in section 2.6.5 (R2-2005371).

3. Option2: Add an extra availability indicator for Sensor measurements results in RRCReestablishmentComplete, RRCReconfigurationComplete, RRCResumeComplete, RRCSetupComplete, UEInformationResponse message to align with Bluetooth/WLAN measurements results.

Proposals that need further discussions:

[13], Ericsson 		Proposal 5	The UE includes either the SpCell or the SCell in which RA occurred when the raPurpose is set to ulUnSynchronized.

[13], Ericsson 		Proposal 9	The UE includes reestablishment in raPurpose when RA is triggered to perform reestablishment.

[27], ZTE, [Z168][Z172]: (Three companies support and one company indicates that this is related to P1 of first question in section 2.4 (the conclusion of P1 in section 2.4 is Not pursue P1.).)

Proposal 1: One common IE, e.g. RA-InformationCommon is used to indicate the RA related information, i.e., BWP configuration,RA resoource information and perRA-InfoList.

Proposal 2: To create a new subclause 5.7.10.5 for determination of RA information in RA report or RLF report, and put the reference at corresponding section.

[18], Huawei, [H363]: discuss option 1 and option 2, and then select one:

Option 1:

change "2> when performing the logging:"  into:  "2> when adding a logged measurement entry in VarLogMeasReport, include the fields in accordance with the following:"

Option 2:

Add “3>	include the fields in VarLogMeasReport as follows:” after “2>	when performing the logging:”

Propoals that are not pursued: (in XLS, the status will be PropReject)

[1], ZTE, [Z162-Z166]		Proposal 3: UE shall reset the numberOfConnFail to “0” when this is the first connection failure since UE transits from connected to idle state.

[1], ZTE, [Z162-Z166]		Proposal 4: UE reset numberOfConnFail to “1” when storing resume failure information. And remove the part UE compare the numberOfConnFail from subclause 5.3.13.5.

[2], ZTE, [Z167][Z169]		Proposal 3: To create an independent section in 5.3.10.3 for RLF report content setting.

[5], Samsung, [S951][S952]		Proposal 2: rlf-cause is set to randomAccessProblem or beamFailureRecoveryFailure if the radio link failure is declared due to the random access problem indication from MCG MAC for 4 step random access procedure.

[11], Ericsson, [E200]		Proposal 1	Include T312-expiry as an option in rlfCause in RLF report.

[3], ZTE, [Z170][Z171][Z173]			Proposal 1: If both CB/CF RA resource with different configuration is used in RA procedure, one common IE is used to indicate the CBRA resource configuration, while another dedicated IE is used to indicate the CFRA resource parameters with different value of that in the common IE.

[13], Ericsson 		Proposal 10 [new]: RA report doesn’t log the RA information if it is triggered due to consistent LBT failure.

[9], Ericsson, [E021]		Proposal 1	Modify the procedural text to indicate that the UE shall log anyCellSelectionDetected flag indication and the last serving cell related measurements upon entering any cell selection state only when the UE is configured with periodical logged MDT.

[12], Ericsson, [E235]		Proposal 1	The UE shall include a flag in the logged MDT report to indicate whether the UE is performing RRM measurements based on relaxed RRM measurement policy or normal RRM measurement policy.

[24], Huawei, [H371]		Proposal: It is proposed to add UE behaviours regarding the field InterFreqTargetList in the procedural text.

[25], Samsung, [S959]		Proposal: IE InterFreqTargetList moves out of IE AreaConfiguration.

[23], Huawei, [H369][H370]		In order to be aligned with the procedural text, in the field description of trackingAreaCode, it is suggested to add the following text:  This field should be included if CGI-Info-Logging-r16 is under RA-Raport-r16 or under ConnEstFailReport-r16.

[28], CATT, [C210]:

Observation 1: For condition handover, the time gap between HO initialization and the point where the UE starts to access the candidate Cell is implementation dependent.

Proposal 1: For LTE or NR RLF report, if the last handover procedure UE performed before declaring HO failure or RLF failure is a condition handover, the starting point of timeConnFailure is the time where UE started to access the first candidate Cell.

Observation 2: UE may try more than one candidate cells during the last handover procedure UE performed before declaring HO failure or RLF failure.

Proposal 2: For LTE or NR RLF report, if the last handover procedure UE performed before declaring HO failure or RLF failure is a condition handover, the ending point of timeConnFailure for condition HO failure is until the last T304 expiry, while for RLF failure case, no change is needed for the ending point of timeConnFailure.

Proposal 3: RAN2 is asked to agree the corresponding TP in section 4.

Proposal 3: Regarding how to determine whether a cell is part of the area Indicated by AreaConfiguration, one solution is:

consider only first PLMN-Identity in first PLMN-IdentityInfo of the PLMN-IdentityInfoList, and cellIdentity corresponding to the first PLMN-IdentityInfo.

Proposal 4: It is proposed to postpone any change to LTE-5GC to later release, and remove 5GC identities in the filed CGI-InfoEUTRALogging.

4	Upon setup failure or resume failure, UE sets the plmn-Identity to RPLMN if available. (for both S470 and S471)

Others:

[2], ZTE, [Z167][Z169]		Proposal 2: In 5.3.10.3, in order to allow store RLF information when RLF happens and UE goes to idle, the RLF content setting procedure shall be put in the corresponding section when UE goes to idle with release cause ‘other ’ or ‘RRC connection failure’ as well.		(Conclusion: no need to discuss it in MDT session as the same discussion is ongoing in [E039] in main session.)

[6], Ericsson, [E008]		Proposal 2	Include lbtFailure as a failureType in SCGFailureInfomationNR in LTE RRC specification.		(P2 has been agreed in [206])

[26], ZTE		(further review it when updating 38.331 CR)

## 5	Tdocs under AI 6.12.4 ASN1 review

- R2-2004409	[Z162-Z166] Correction to connection establishment failure report	ZTE Corporation, Sanechips	discussion	Rel-16	NR_SON_MDT-Core	Late

- R2-2004410	[Z167][Z169] Correction to RLF report	ZTE Corporation, Sanechips	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004411	[Z170-171][Z173] Correction to RACH report 	ZTE Corporation, Sanechips	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004417	Corrections on Sensor Measurement	CATT	discussion	Rel-16	38.331	NR_SON_MDT-Core

- R2-2004528	Corrections to RA/RLF Report_S951_S952	Samsung Electronics Co., Ltd	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004717	[E008] On adding LBTFailure as SCG Failure cause and RLF cause	Ericsson	discussion

- R2-2004718	[E009] On EUTRA previousPCellID in NR RLF report	Ericsson	discussion

- R2-2004719	[E012] On logging TAC in CEF report	Ericsson	discussion

- R2-2004720	[E021] Any cell selection state related logging for OOC event	Ericsson	discussion

- R2-2004721	[E028] On SON-MDT related UE capabilities addition	Ericsson	discussion

- R2-2004722	[E200] On T312 expiry related RLF cause	Ericsson	discussion

- R2-2004723	[E235] UE power savings impact on MDT	Ericsson, CMCC, Samsung	discussion

- R2-2004733	Clarification to RA-report purposes	Ericsson	discussion

- R2-2004884	[S953] Mobility state reporting in RRC connection re-establishment	Samsung Electronics Co., Ltd	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004886	[S954] Logged MDT configuration in UE Inactive AS Context	Samsung Electronics Co., Ltd	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004902	Text Proposal_for_RIL_S481	Samsung Electronics Co., Ltd	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005371	Summary of [Post109bis-e][960] ASN1 RIL discussion	Huawei	discussion	Rel-16	NR_SON_MDT-Core	Late

- R2-2005372	[H363] Discussion on UE logging of a MDT entry	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005373	[H365] Discussion on conditions for RLF report	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005374	[H366] Discussion on processing delay requirements	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005375	[H367] Discussion on failedPcellId-EUTRA	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005376	[H368] Discussion on measResult-RLF-Report-EUTRA	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005377	[H369][H370] Discussion on corrections of TAC	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005378	[H371] Discussion on applying the field interFreqTargetList	Huawei, HiSilicon	discussion	Rel-16	NR_SON_MDT-Core

- R2-2005416	Correction on MDT Configuration [S959]	Samsung	discussion	NR_SON_MDT-Core

- R2-2005468	TP on cat-a proposal2/3 of SON emailDisc[961]	ZTE Corporation, Sanechips	discussion	Rel-16	NR_SON_MDT-Core	Late

- R2-2005469	[Z168][Z172] Alignment of RA informatiom	ZTE Corporation, Sanechips	discussion	Rel-16	NR_SON_MDT-Core

- R2-2004416	[C210] Discussion on Field Description of timeConnFailure in RLF Report	CATT	discussion	Rel-16	38.331	NR_SON_MDT-Core

## 6	Implement the changes into 38.331 CR

In R2-2006015, the XLS (i.e. MDT RILs_38331 v146 v2) is attached. For the label “1_MDT, NR_SON_MDT-Core”, there are PropAgree RILs and not implemented yet. So the updated CR will capture these new changes by Huawei_110-e_2.

R2-2004724	[Post109bis-e][961][MDTSON] SON open issues (Ericsson)	Ericsson	discussion

// All have been implemented in the 38.331 CR.

Agreements:

1	For SSB based RA attempt based on contention free random-access resources contentionDetected-r16 is not included in PerRAInfoList-r16.

2	The UE does not include the dlRSRPAboveThreshold-r16 flag for SSB based CFRA if the CFRA is not associated to PDCCH ordered RA and the UE includes the dlRSRPAboveThreshold-r16 flag for SSB based CFRA if the CFRA is associated to PDCCH ordered RA.

3	The UE shall append the new EPLMNs to the PLMN entries in the plmn-IndentityList until the maximum number is reached and after this limit is reached the UE shall stop the recording of the RAReports until the existing contents of VarRAReport is fetched by the network or the 48 hour time window expires.

4	Add the possibility to include EUTRA CGI as the previousPCellID in NR RLF report

5	Change the field description of failedPCell-EUTRA to indicate that this field is used to encode the PCell in which RLF is detected or the source PCell of the failed handover.

6	Agree the following TP related to MHI.

1>	Upon change of cell, consisting of PCell in RRC_CONNECTED or serving cell in RRC_IDLE or RRC_INACTIVE (for NR cell) or in RRC_IDLE (for E-UTRA cell), to another NR or E-UTRA cell, or when entering out of service.

We should refer to ‘any cell Selection’ or ‘camp on any cell’ in NR and or ‘any cell Selection in LTE’ or ‘camp on any cell’ instead “out of service“

Agreements

1	Add the possibility to include EUTRA CGI as the failedPCellID in NR RLF report.

2	Include reconnectedCellID in NR RLF report and add the possibility to include EUTRA CGI or NR CGI and the associated TAC as part of the reconnectedCellID.

3	Include timeUntilReconnection in NR RLF report which signifies the time interval between HOF/RLF and successful RRC re-connection.

4	Add the possibility to include NR CGI as the previousPCellID in LTE RLF report.

5	Add the possibility to include NR CGI as the failedPCellID in LTE RLF report.

6	Add the possibility to include EUTRA CGI (reconnectedEUTRA-CellId) or NR CGI (reconnectedNR-CellId) and the associated TAC of the cell in which the UE successfully performs reconnection after declaring RLF or HOF.

7	Include timeUntilReconnection in LTE RLF report which signifies the time interval between HOF/RLF and successful RRC re-connection.

R2-2006006	Summary of AI 6.12.2 - Essential input from RAN3	Ericsson	discussion

Agreements:

1	The management-based MDT configuration should not overwrite signaling based MDT configuration in all the single connection scenarios and EN-DC scenario. UE based soltuion is not supported in R16.

R2-2005371	Summary of [Post109bis-e][960] ASN1 RIL discussion	Huawei	discussion	Rel-16	NR_SON_MDT-Core	Late

=>	Agree on the status change of RILs (i.e. Category, Status) in conclusion parts in section 2 in R2-2005371

Agreements:

1	Introduce new IE ueMeasurementsAvailable-r16 to contain flags.		// implemented

2	For numberOfConnFail , This field is used to indicate the latest number of consecutive failed RRCSetup or RRCResume procedures in the same cell independent of RRC state transition.	// implemented

4.	Add the nonCriticalExtension and laterNonCriticalExtension fields to the LoggedMeasurementConfiguration message.	// implemented

5. 	The proposed TP in section 5.1 and 5.2 is to be implemented in the CR, and any update can be discussed during CR discussion (e.g. R2-2005469).	// implemented

6.	 For the reference of TS 36.133, it is suggested to keep the current 36.133 (no extra change).	// no extra changes.

# Comments

Covered in online session.

Huawei: agreed.

We noticed NR-U has added a new RA trigger: consistent LBT failure in 38.300.  Since this haven’t been discussed in R16 MDT, we suggest to postpone it to R17 and add description in 38.331 to exclude include RA information when it is triggered by consistent LBT failure. According to above comments we suggest to add one more proposal for further discussed: RA report doesn’t log the RA information if it is triggered due to consistent LBT failure.

Huawei_Jun: ok to add it as a new proposal.

ZTE_Zhihong: This is not new RILs. It was treated in last meeting and the status shall be ProReject.

Huawei_Jun: Sorry. I wrongly put it to new RILs. Ok to remove it from here and from in the XLS.