3GPP TSG RAN WG2 Meeting #110-e		R2-2005947

1 – 12 June 2020

Title:	(draft) LS on system support for WUS

Response to:	R2-2004317/S2-2003217 Reply LS on assistance indication for WUS

Release:	Release 15

Work Item:	NB_IOTenh3-Core, LTE_eMTC5-Core

Source:	Qualcomm (to be RAN2)

To:	SA2, RAN3

Cc:

Contact person:	Mungal Dhanda

mdhanda (at) qti (dot) qualcomm (dot) com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

# 1	Overall description

RAN2 has discussed changes to its specification to implement system support for WUS as advised in the SA2 LS in R2-2004317/S2-2003217. RAN2 has already notified SA2/RAN3 of the issue resulting from handover/reestablishment in R2-2005939.

RAN2 has identified another potential issue with the solution described in R2-2004317/S2-2003217 if it is possible for the eNB to release the RRC connection with RRCConnectionRelease without establishing/releasing the S1 connection (e.g. in case of CN overload or MME reset). The UE would be unreachable while it remains camped on this cell or till the UE establishes/resumes RRC connection (i.e. MO data, MO signalling). RAN2 assumes the same issue could also happen in 5GC.

Due to this and the earlier issue identified in R2-2005939, RAN2 has postponed the CRs.

# 2	Actions

To 3GPP SA2, RAN3

ACTION: RAN2 respectfully asks SA2 and RAN3 to take the above scenario into account, if it is considered possible, in the final solution.

# 3	Dates of next TSG RAN WG2 meetings

TSG RAN WG2 Meeting #111e	17 – 28 August 2020

TSG RAN WG2 Meeting #112e	2 – 13 November 2020