## Slide 1: Multiple reference configuration for inter-CU LTM
KDDI, LG Electronics, Nokia, ZTE, Rakuten, KT, CMCC, ETRI, ITL, ITRI
Fujitsu, SK telecom, Uplus
3GPP TSG-RAN WG2 Meeting #127bis
Hefei, China, Oct 14th – 18th, 2024
Agenda: 8.6.2
R2-2409031

## Slide 2: Drawbacks of single reference configuration
For inter-CU LTM, single reference configuration requires interaction with all involved CUs to generate or update the reference configuration, which incurs a huge Xn signaling.
  If each CU has its own reference configuration, the required Xn signaling is limited toward the concerned CU.
When a reference configuration is updated, all candidate cell configurations should be reconfigured, which incurs a huge RRC signaling.
  If each CU has its own reference configuration, the required RRC signaling is limited to the candidate cell configuration belonging to the concerned CU.
Considering that a neighbouring gNB could contain DUs and cells with completely different configurations, using a single reference configuration implies the following below, which defeats the original intention of introducing the concept of reference configuration.
  the delta configuration for candidate cell configuration is almost a full configuration; and/or
  the reference configuration is efficient only for a subset of candidate cells belonging to a specific CU, and for other candidate cells, complete configuration is required.
To make reference configuration feature useful (or at least to avoid making the feature obsolete) for inter-CU LTM, it is essential to support multiple reference configuration.

## Slide 3: Support of multiple reference configurations
Multiple reference configuration (reference configuration per CU) for inter-CU LTM is aligned with the Rel-18 reference configuration principle for intra-CU LTM.
  In Rel-18 LTM is limited to intra-CU cell switch, where reference configuration is applied to configured candidate cells of the same CU. That is, reference configuration is implicitly per CU already.
Specification impact to support multiple reference configuration is small.
  It only requires extending one reference configuration to multiple configurations.
  Each reference configuration needs to be configured with a list of associated candidate cells, i.e., reference configuration per CU.
It is up to network implementation how many reference configurations it configures, from zero to multiple.
  UE capability of support for multiple reference configuration should be introduced.
    FFS whether multiple bits indicating the number of supported reference configuration should be considered or whether a single bit with a fixed number of supported reference configuration capability is sufficient.

## Slide 4: Proposal:
Proposal1: To support multiple reference configuration
  Each reference configuration is associated with a list of candidate cells (reference configuration per CU)
  UE capability signaling for multiple reference configuration is introduced. FFS the details.
Proposal2: To send LS to RAN3 to inform the support of multiple reference configuration