## Slide 1: Way forward on the uplink grant used for UEIBR
OPPO, Huawei, Ofinno, Samsung, ZTE, Qualcomm, LG, Nokia, ASUSTek
3GPP TSG-RAN2 Meeting #129bis R2-2503036
Wuhan, China, Apr 7-11, 2025

## Slide 2: Background
Observation 1: RAN1 agreed that Type-1 CG PUSCH in Mode-B for carrying the UE initiated beam report does not carry UL-SCH (i.e. MAC PDU). Whether the PUSCH for Mode-A can carry UL-SCH has not been discussed yet.
Observation 2: In TS 38.321, if UCI multiplexing is required for PUSCH or aperiodic CSI is triggered, the MAC needs to generate MAC PDU for both CG and DG, as requested by RAN1. The MAC specification needs to be clarified to align with the RAN1 agreement.

## Slide 3: Way forward
Proposal: Confirm the following RAN2 understandings:
  The CG type-1 PUSCH carrying the beam report of Mode-B does not carry MAC PDU (i.e. UL-SCH).
  The DG PUSCH carrying the beam report of Mode-A carries MAC PDU (i.e. UL-SCH) as legacy.