## Slide 1: FFS issues on (re)selection Huawei, HiSilicon
Offline-419

## Slide 2: FFSs for Relay Reselection Procedure
L2 multi-hop U2N Remote UE in idle/inactive triggers relay reselection upon PC5-RRC signaling from the first relay UE indicating (FFS on the detailed PC5-RRC signaling design):
  cell reselection, handover, Uu RLF, or Uu RRC connection establishment/resume failure between the last relay UE and network.
  release of RRC connection between an intermediate relay UE and the network.
  PC5 RLF or PC5-S connection release between the multi-hop U2N Relay UE(s).
  FFS: link quality degradation of the upstream links resulting in a notification.
  FFS if any of these conditions can occur without notifying the remote UE (e.g., allowing recovery by the intermediate relay UE).
  FFS on the signalling contents of the PC5-RRC indication from the first relay UE.
  FFS applicability to L3.
The intermediate relay UE can adopt the same AS triggering condition of relay (re)selection of the R17 remote UE. FFS upper layer conditions and whether the spec impact will be modelled as a separate relay UE behaviour or through functioning as a remote UE.
Upon intermediate relay UE performing relay (re)selection, it can notify its child node. If the cause of (re)selection already causes a notification, there is no double-trigger of the notification.
  FFS if (re)selection as such is captured as a cause of notification (intention to maintain no double-trigger)
  FFS if the notification is required in all cases
  FFS the content in the notification
  FFS the child node behaviour after receiving this notification
  FFS other condition/timing that the intermediate relay UE notifies its child node

## Slide 3: FFS: link quality degradation of the upstream links resulting in a notification.
R2-2502609 proposes to reuse the R17 mechanism where if the upstream PC5 links in the multi-hop chain degrade
  either the intermediate or the first relay UE will trigger relay reselection or cell selection when they are in IDLE/INACTIVE state or a path switch when they are in RRC_CONNECTED state.
  Upon relay (re)selection or cell selection or path switch, the upstream relay UE in the multi-hop chain will send a notification message to the child relay UE, which will then forward it to the remote UE.
Proposal 3: Link quality degradation of the upstream links will lead to path switching (for the CONNECTED state) or relay (re)selection or cell selection (for the IDLE/INACTIVE state), rather than triggering an immediate notification. The relay UE will send a notification once path switching or relay (re)selection or cell selection occurs. FFS if path switching happens in the same cell
Company Views
Link quality degradation Notification Needed: ZTE, IDC
Link quality degradation Notification not needed: NEC, QC, E//, OPPO, APPLE, VIVO, LG, Samsung, Kyocera, HW

## Slide 4: FFS if any of these conditions can occur without notifying the remote UE (e.g., allowing recovery by the intermediate relay UE).
R2-2502609 proposes to extend the single hop R17 notification mechanism to multihop.
  It is beneficial for the remote UE to be informed by the serving Intermediate Relay UE/First Relay UE when it receives a notification message indicating cell reselection, handover, Uu RLF, or Uu RRC connection establishment/resume failure of the U2N Last Relay UE. This allows the remote UE to take corrective action eg perform reselection.
  Similarly it is also beneficial for the intermediate and first relay UE to either forward or send the notification message to the child UE downstream so that remote is informed of the PC5- RLFs
Proposal 4: The notification message received from the U2N Last Relay UE indicating a failure on the Uu interface should be forwarded downstream by the Intermediate/First Relay UE to the Remote UE. To achieve this, we can reuse the PC5 RRC Notification message as a baseline.
?Proposal 6. If there are multiple relay UEs in the multi-hop chain, there is a possibility of encountering a multi-hop failure on the PC5 links. In this case, it would be beneficial for the child relay UE to forward or send the notification message downstream until the Notification Message is delivered to the Remote UE. FFS if it is needed for PC5 failures in the upstream links
FFS to check if some mechanism for forwarding exists in SA2 specs.
Company Views
Notification Needed: Samsung (only for Uu), E//(only for Uu), OPPO (all cases), ZTE (all cases), LG (all cases)
Notification not needed in certain cases: QC, Kyocera

## Slide 5: FFS if any of these conditions can occur without notifying the remote UE (e.g., allowing recovery by the intermediate relay UE).
R2-2502609 proposes to not to have group mobility mechanism for R19.
  Considering that group handover/mobility is not supported since R17, it is simpler to adhere to the legacy mechanism where the multi-hop U2N Remote UE triggers relay reselection when cell reselection, handover, Uu RLF, or Uu RRC connection establishment/resume failure is indicated by the multi-hop U2N Relay UE(s)
?Proposal 5: Failure Scenarios in which the remote UE is not notified and recovery is handled by the intermediate relay UE not considered to be supported in R19.
Company Views
Remote UE always notified: OPPO, HW, ZTE
Cases Remote UE is not notified: Samsung, IDC, LG, QC

## Slide 6: FFS on the signalling contents of the PC5-RRC indication from the first relay UE.
For the content in the PC5-RRC indication when an intermediate relay UE forward the notification message received from the parent relay UE, there can be two options as proposed in R2-2502609.
  Option 1: Intermediate relay UE forward the PC5-RRC indication from the parent relay UE without the content update.
  Option 2: The intermediate relay UE updates the content in the notification message based on the reaction of the intermediate relay UE when it receives the notification message from parent.
If the intermediate relay UE forward the notification message form the parent relay UE without the content update, there will be some ambiguity since some failure cause are specific to the last relay UE will not happen at the intermediate relay UE.
?Proposal 7. Upon receiving the notification message form the parent relay UE, the intermediate relay UE/first relay UE may update the indication in the notification message to the remote UE to indicate the action it has taken.
Company Views
Option 1:
Option 2:Samsung, E///, Oppo, Kocera , IDC, LG

## Slide 7: FFS applicability to L3
R2-2502609 proposes that the RAN 2 part of the scope is limited to the L2 Mulit hop Relay design RAN 2 will not look into L3 aspects. .
Proposal 8: RAN2 will focus solely on the L2 Multi-hop Relay design. Therefore, we do not need to discuss the applicability of L3 Multi-hop relays.
company Views
Most of the companies agree with P8

## Slide 8: Proposal from 419 Offline
Link quality degradation
Proposal 1: Notification for Link quality degradation is not supported. Link quality degradation of the upstream links will eventually lead to path switching (for the CONNECTED state) or relay (re)selection or cell selection (for the IDLE/INACTIVE state). The relay UE will send a notification once path switching or relay (re)selection or cell selection occurs. FFS on sending the notification if the path switching happens in the same cell.
Notification from the upstream Relay UE
Proposal 2: The notification message received from the U2N Last Relay UE indicating a failure on the Uu interface should be forwarded downstream by the Intermediate/First Relay UE to the Remote UE. To achieve this, we can reuse the PC5 RRC Notification message as a baseline.
Proposal 3. RAN 2 to further discuss and agree if the Notification Message is forwarded/ sent down stream, all the way to the Remote UE, in case PC5 Link failures on the multi hop chain are encountered. FFS to check if some higher layer mechanism for forwarding already exists in SA2 specs
Group Mobility Support
Proposal 4: RAN 2 to discuss if group mobility/handling is to be supported in R19 where recovery is handled by the intermediate relay UE without remote UE being notified of any failures.
Content in the Notification Message
Proposal 5. Upon receiving the notification message form the parent relay UE, the intermediate relay UE/first relay UE may update the indication in the notification message to the remote UE to indicate the action it has taken. FFS if we need any new cause value

## Slide 9: Proposal from 419 Offline
Applicability to L3
Proposal 6: RAN2 will focus solely on the L2 Multi-hop Relay design. Therefore, we do not need to discuss the applicability of L3 Multi-hop relays.