## Slide 1: Way forward on UL delay measurement
CMCC, Qualcomm Incorporated, Huawei, Alcatel-Lucent, Samsung, ZTE, Intel, CATT, ITRI, Nokia Networks, China Telecom
3GPP TSG-RAN WG2 Meeting #91
Beijing, China, 24 - 28 Aug 2015
Agenda Item: 7.8
Document for: Discussion and decision
R2-153191

## Slide 2: Target of feMDT on UL Delay measurement
To derive cause of UL delay through MDT mechanism

## Slide 3: The causes of UL delay
Scheduling => queueing delay
Coverage => transmission/HARQ delay
Interference => transmission/HARQ delay

## Slide 4: How to achieve the target
UL coverage and interference issues can be detected through M2 and M3 of existing MDT
  M2: Power Headroom measurement by UE.
  M3: Received Interference Power measurement by eNB.

## Slide 5: How to achieve the target
The only gap to achieve the target is to detect scheduling issue
To bridge the gap, we propose to focus on solutions, which can reflect the queueing delay and detect the scheduling problem

## Slide 6: How to achieve the target
Proposal 1: UL packet delay metric should focus on reflecting the queueing delay.

## Slide 7: How to achieve the target
In addition, taking complexity to UE and eNB into account, we propose the following principles:
  UL packet delay measurement should be performed per QCI per UE
  UL packet delay measurement should reflect the packet delay observed at UE’s PDCP layer only
    E.g. recording the time duration between the point in time that a PDCP SDU arrives at PDCP upper SAP and the point of time that the first part of this PDCP SDU enters MAC
  How and when UE reports will be addressed in WI phase

## Slide 8: How to achieve the target
Proposal 2: UL packet delay measurement should be performed per QCI per UE and should reflect the packet delay observed at UE’s PDCP layer only
  Detailed realisation will be addressed in WI phase

## Slide 9: Conclusion
Proposal 1: UL packet delay metric should focus on reflecting the queueing delay
Proposal 2: UL packet delay measurement should be performed per QCI per UE and should reflect the packet delay observed at UE’s PDCP layer only