## Slide 1: Way forward on RAN2 aspects of multiple PRB operations
NTT DOCOMO, INC., Ericsson, Vodafone, Qualcomm, ZTE, Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Intel
R2-161888
TSG-RAN WG2 meeting #93
15-19 February 2016, St. Julian’s, Malta

## Slide 2: Prerequisite – RAN1 agreements –
The UE in RRC_IDLE camps on the NB-IoT carrier on which the UE has received NB-PSS/SSS, NB-PBCH and SIB transmissions.
The UE in RRC_CONNECTED can be configured, via UE-specific RRC signaling, to a PRB, for all unicast transmissions (not intended to excluding SC-PTM, if supported), different than the NB-IoT carrier on which the UE has received NB-PSS/SSS, NB-PBCH and SIB transmissions.
  If the different PRB is not configured for the UE, all transmissions occur on the NB-IoT carrier on which the UE has received NB-PSS/SSS, NB-PBCH and SIB transmissions.
The UE is not expected to receive NB-PBCH, and NB-PSS/SSS and any transmissions other than unicast transmissions in the configured PRB.
PRACH is supported on anchor PRB.
  Logical consequence from the RAN 1 agreements.
■ Additional RAN1 agreements not described in the RAN1 LS (R2-161053).

## Slide 3: Proposals (1/3) - Configurations of non-anchor PRB -
For C-plane solution, a non-anchor PRB can be configured when an RRC connection is established (i.e., Msg.4).
For U-plane solution, a non-anchor PRB can be configured when an RRC connection is (re)established, resumed or reconfigured.
Configurations of a non-anchor PRB is included within the IE radioResourceConfigDedicated.
After the successful completion of RRC connection (re)establishment, resume or reconfiguration, if configured, the UE can start to receive NB-PDCCH/NB-PDSCH and/or transmit NB-PUSCH on a non-anchor PRB.
A UE that has been assigned a non-anchor PRB, remains on that PRB throughout RRC_CONNECTED or until transmission of NB-RACH is needed in RRC_CONNECTED (see bullet 3 on next slide) or until re-assigned to another PRB.

## Slide 4: Proposals (2/3) - Random Access/RRC connection (re)establishment procedure -
The RA procedure is performed on an anchor PRB.
The RRC connection (re)establishment/resume procedure is initiated on an anchor PRB.
  After the HARQ acknowledgement for Msg.4, UE start monitoring an non-anchor PRB and Msg.5 is delivered on an non-anchor PRB.
If the UE needs to perform a RA procedure while on the non-anchor carrier (e.g. due to SR or PDCCH order) it goes back to the anchor carrier and stays there throughout RRC_CONNECTED or until re-assigned to another PRB.
  We may consider the mechanism to go back to the non-anchor PRB after the RA procedure.

## Slide 5: Proposals (3/3) - Upon leaving RRC_CONNECTED -
A UE that operates on a non-anchor PRB selects an NB-IoT carrier (via cell selection) upon leaving RRC_CONNECTED.
  FFS whether the eNB may redirect a UE to another NB-IoT carrier during RRC Connection Setup and/or RRC Connection Release.
A UE in RRC_IDLE receives paging on an anchor PRB.