## Slide 1: Way Forward on providing internal WT MAC address to UE
Broadcom, Brocade, CableLabs
R4-170xxxx

## Slide 2: Background and concerns
In order for a LWA UE to send UL traffic over WLAN access, the MAC address of the WT shall be known by the UE;
Both in RAN based authentication as well as in Core Network based authentication, the internal WT MAC address (i.e. the MAC address of the WT interface facing the WLAN access) may be made available to the UE using WLAN specific methods; however, it is acknowledged that there are cases where this is not possible;
There are concerns associated with a procedure that communicates the WT MAC address outside the realm of the Wi-Fi infrastructure (namely to the eNB in order for it to provide it to the UE).

## Slide 3: Proposal:
The WT internal MAC address shall be provided to the UE using WLAN based procedures when available. When such procedures are not available, the WT internal MAC address shall be provided to the UE through eNB signaling.
The following text proposal is suggested to be captured in TS 36.300:
“The WT shall provide the WT MAC address to the LWA UE at the end of the authentication stage using WLAN specific transport when available. If no such transport is available, the WT shall provide the WT MAC address to the LWA UE through the eNB, using the Xw interface.”