3GPP TSG-RAN WG3 #115-e																	      R3-221557

21th Feb – 3rd Mar 2022

Online

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 38.410 | CR | 0030 | rev | 11 | Current version: | 16.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | MBS BL CR for TS 38.410 |
| --- | --- |
| Source to WG: | ZTE |
| Source to TSG: | R3 |
| Work item code: | NR_MBS-Core |  | Date: | 2022-03-17 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) … Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | As per RP-193248, NR MBS is supported in release 17. |
| Summary of change: | NR MBS is introduced. Editorial change Capture agreed TP：R3-207054, R3-214381 Capture agreed TP R3-216046 based on R3-214660 Capture agreed TP R3-221169 based on R3-220070 |
| Consequences if not approved: | NR MBS cannot be supported in Rel 17. |
| Clauses affected: | 3.2, 4.4, 5, 6, 7.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: | Rev-1: R3-206526 rev in R3-207051 with editorial changes. Rev-2: R3-207250 = baseline R3-207051 + integrated agreed TP from RAN3#110: R3-207054 Rev-3: R3-207250 rev in R3-210016 for resubmit. Rev-4: R3-211478 for resubmit. Rev-5: R3-213144 for resubmit Rev-6: TP R3-214381 is agreed and merged Rev-7: R3-214660 Rev-8: R3-216268 Rev-9: R3-220070 |

--------------------------------Start of the First Change-----------------------------

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 38.411: "NG-RAN; NG layer 1".

[3]	3GPP TS 38.412: "NG-RAN; NG signalling transport".

[4]	3GPP TS 38.413: "NG-RAN; NG Application Protocol (NGAP) ".

[5]	3GPP TS 38.414: "NG-RAN; NG data transport".

[6]	3GPP TS 23.502: "Procedures for the 5G system".

[7]	3GPP TS 38.300: "NR; Overall Description; Stage 2".

[8]	3GPP TS 23.501: "System Architecture for the 5G system".

[9]	3GPP TS 38.415: "PDU Session User Plane Protocol".

[10]	3GPP TS 38.455: "NR Positioning Protocol A (NRPPa)".

[11]	3GPP TS 36.300: "E-UTRAN); Overall description; Stage 2".

[xx]	3GPP TS 23.247: “Architectural enhancements for 5G multicast-broadcast services; Stage 2”

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in TR 21.905 [1] and the following apply. 
A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

gNB: as defined in TS 38.300 [7].

NB-IoT: as defined in TS36.300 [11].

ng-eNB: as defined in TS 38.300 [7].

NG-RAN node: as defined in TS 38.300 [7].

UPF: as defined in TS 23.501 [8].

## 3.2	Abbreviations

For the purposes of the present document, the terms and definitions given in TR 21.905 [1] and the following apply. 
A term defined in the present document takes precedence over the definition of the same term, if any, in TR 21.905 [1].

5GC	5G Core Network

AMF	Access and Mobility Management Function

CIoT	Cellular IoT

MBS	Multicast/Broadcast Service

NB-IoT	Narrow Band Internet of Things

NG-U	NG User plane interface

PTP	Point to Point

PTM	Point to Multipoint

RIM	Remote Interference Management

SMF	Session Management Function

UP	User Plane

UPF	User Plane Function

# 4	General aspects

//skip unchanged part

## 4.4	NG interface capabilities

The NG interface supports:

-	procedures to establish, maintain and release NG-RAN part of PDU sessions

-	procedures to perform intra-RAT handover and inter-RAT handover;

-	the separation of each UE on the protocol level for user specific signalling management;

-	the transfer of NAS signalling messages between UE and AMF;

-	mechanisms for resource reservation for packet data streams.

-	procedures to establish, maintain and release NG-RAN part of MBS sessions

# 5	Functions of the NG interface

//skip unchanged part

## 5.xx	NR MBS Session Management function

The MBS Session Management function is responsible for establishing, modifying and releasing the involved NR MBS sessions NG-RAN resources for user data transport once an MBS context is available in the NG-RAN node.

NGAP supports transparent relaying of MBS Session related information by the AMF as described in TS 23.247 [xx].

## 5.yy	Multicast Group Paging Function

The Multicast group paging function supports the sending of multicast group paging requests to the NG-RAN nodes in order to group-page UEs that have joined the Multicast MBS Session

# 6	Signalling procedures of the NG interface

//skip unchanged part

## 6.xx	NR MBS Session Management Procedures

The following list of MBS Session management procedures are used to establish, release, or modify NG-RAN resources for a NR MBS session:

-	Broadcast Session Resource Setup;

-	Broadcast Session Modification;

-	Broadcast Session Resource Release;

-	Multicast Session Activation;

-	Multicast Session Deactivation;

-	Distribution Setup;

-	Distribution Release;

## 6.yy	Multicast Group Paging Procedures

The following Multicast Group Paging procedure is used to send multicast group paging requests to the NG-RAN nodes:

-	Multicast Group Paging.

# 7	NG interface protocol structure

## 7.2	NG User Plane

The NG user plane (NG-U) interface is defined between a NG-RAN node and a UPF. The NG-U interface provides non guaranteed delivery of PDU Session /MBS session user plane PDUs between the NG-RAN node and the UPF.

The protocol stack for NG-U is shown in Figure 7.2-1.

Figure 7.2-1: NG-U protocol structure for PDU Session

--------------------------------End of the Changes-----------------------------

# Comments

Need to be updated to RAN meeting info